## Slide 1: The simplest CMOS two-stage op-amp
First stage: p-input differential amplifier with mirror load
Second stage: n-input common source class-A stage
Bias currents of the op-amp
The output of the first stage is "referred to gnd"
The input of the second stage is "referred to gnd"
CC, RC: frequency compensation network

## Slide 2: Use of a single M8 device to bias multiple op-amp
M8 can be shared among different amplifiers and is not part of the op-amp architecture
For this reason, we do not consider M8 in the amplifier topology
Vbias

## Slide 3: Degrees Of Freedom (DOFs)
Possible DOFs:
W, L of all devices (14 DOFs)
I0, I1
CC, RC
Not all DOFs are independent.
It is necessary to choose a set of independent DOFs
First estimate: Total number of DOFS: 18
But ...

## Slide 4: Constraints
Constraints are relationships among DOFs
Two types of constraints:
Equality constraints:
For example:
Inequality constraints:
For example:

## Slide 5: Constraints
Every equality constraint reduces the dimension of the DOF space. Equality constraints represent exact conditions that has to be fulfilled in order to guarantee correct operation of the circuit. Some equality constraints derive from simple considerations, such as symmetry: M1=M2, M3=M4. With a few exceptions, equality constraints are specific of the topology and does not depend on the specifications
Inequality constraints are derived from the circuit specifications. They do not reduce the dimension of the DOF space but select regions of the DOF space where the specs are met.

## Slide 6: The sizing process: role of multiple inequality constraints
Combining the various inequality constraints, we find a domain (the intersection of all regions) where all points satisfy all constraints. All points in the domain are valid solutions.
If such region does not exist (null intersection), the sizing problem is: "unfeasible".
A very simple case with only two independent DOFs and two inequality constraints

## Slide 7: The sizing process: automatic algorithms
Computer programs that perform automatic sizing, are not compatible with an infinite number of feasible solutions. To find a single solution, an optimization condition is often added.
If the design is performed manually, any point (set of DOFs values) in the intersection domain is a good solution. Also in this case, optimization or arbitrary techniques can be used to operate the choice

## Slide 8: Sizing of a new topology: steps
Find equality constraints to reduce the number of independent DOFs. These constraints will be of two types: (a) Strictly necessary constraints (if not respected the circuit does not work properly) (b) Arbitrary constraints: they are added to further reduce the DOF set and simplify the design. These constraints should be motivated.
Choose a set of DOFs that have the following properties: (a) the remaining dependent DOFs can be easily derived from this set; (b) the specifications (inequality constraints) can be written easily and in a simple form as a function of the selected DOFs
Write the specifications in terms of the selected DOFs and try to find general design rules.

## Slide 9: Equality constraints for the simple 2-stage op-amp
Symmetry (necessary to obtain low offset and low CMRR
M1=M2 (W1=W2, L1=L2) ------ 2
N. of equality
constraints
M3=M4 (W3=W4, L3=L4) ------ 2
Current ratios
-------------- 1
Initial DOF number: 18 , Resulting DOFs after reduction: 18-5=13

## Slide 10: Necessary constraint: null systematic offset
It is not possible to exactly predict Vout, but it will be far from Vdd / 2 if ISC is consistently different from zero

## Slide 11: Necessary constraint: null systematic offset
Since only a common mode voltage is applied to the input:

## Slide 12: More constraints
Good matching M5-M3: L5=L3
Null (small) systematic offset
Good matching M6-M7: L6=L7
Symmetric output swing
(same margins to Vdd and gnd)
Arbitrary constraints
Let's now consider the output characteristic

## Slide 13: Residual number of DOFs
13 - 4 = 9
Of these residual DOFs we can separate two ones (CC and RC) that do not affect the dc performances and the operating point. We will come back to them later. Then we will focus on 7 DOFs (bias current I0 and device size) that affect the operating point and we will call them "static" DOFs).
We could select 7 DOFs within the original set of 16 DOFs ( RC and CC are not included), and then try to derive the remaining ones using the equations that tie them (equality constraints).
It is more useful to choose a set of DOFs that may not necessarily include the original 18, in a way that the other ones can be easily derived.

## Slide 14: Selection of the 7 DOFs
Rationale: the most important MOSFETs of the circuits are M1 (=M2) and M5, since these are the devices that are at the heart of the two stages, where they perform the V-to-I conversion.
We include all possible DOFs of M1 and M5 into the selected set
6 DOFs
To complete the set, let us include also L6 into the DOFs
Final set of static DOFs:

## Slide 15: Derivation of all the op-amp parameters from the 7 DOFs
M2 is dentical to M1, then M1 DOFs specify also M2 parameters
M3=M4:
All conditions will refer to the operating point (Vid=0)

## Slide 16: Derivation of all the op-amp parameters from the 7 DOFs
M6:
M7:

## Slide 17: Small-signal equivalent circuit
All these values are functions of the DOFs
(+)
(-)
Note: the equivalent circuit can be used to represent the behavior of most two-stage topologies, not just the simple amplifier of the figure.

## Slide 18: dc gain

## Slide 19: dc gain as a function of the DOFs

## Slide 20: Frequency response of a two-stage op-amp
This circuit does not include all components that affect the frequency response:

## Slide 21: Frequency response
These capacitances determine the load presented by the amplifier to the signal source. We will suppose that vi1 and vi2 are produced by ideal voltage sources, thus no loading effect will be considered
(-)
(+)
Tail pole
Mirror pole
The tail pole and mirror pole (and a zero created by
The short circuit output current of the first stage also depends on frequency
M1
M2
M3
M4
M7
Vi1
Vi2
V1
H
K
I0
Ctail
Cmirror
First stage
their combination) affect Ym(s). Frequencies are of the order of

## Slide 22: Frequency response, simplified small-signal circuit
If the compensation group CC-RC is not present:
We still have Cgd5 parasitic capacitance, which is not sufficient to produce the compensation effect

## Slide 23: Uncompensated frequency response
Cgd5-Miller
Without compensation, we have two poles at frequencies fp1, fp2, which are of the same order of magnitude and none of them is dominant.
The result is a very small or even negative (= instability) phase margin.
fp1
fp2

## Slide 24: Miller compensation Pole splitting
It is convenient to divide the bridge impedance RC-CC into two impedances by means of the Miller theorem
To do this, we need to calculate the Miller factor K=vout/v1. We force voltage v1 and use the Norton equivalent model of the output port.
iout-sc

## Slide 25: Miller factor
iout-sc
Z(s)
Miller factor:

## Slide 26: Transformation of the bridge impedance ZC by the Miller Theorem
Z
The low frequency limit of the K factor:

## Slide 27: Miller transformations: shifting the input pole to very low frequencies
First effect of Miller compensation: a very large capacitor Gm2R2CC is brought back to the input mesh, shifting the input pole back to low frequencies:
This sets the dominant pole:
Using

## Slide 28: Second effect of Pole Splitting: shifting the output pole to high frequencies
Gm1vid
R1
C1
vi1
vi2
Gm2v1
R2
C2
h
o
vid
v1
RC
CC
vout
At frequencies such that:
and still:
Current source Gm2v1 is controlled by the voltage across it:
We cannot use the Miller theorem again, because the resulting pole would fall at frequencies where K is very different from K(0).
The equivalent circuit reduces to:
C2M
NO

## Slide 29: Second effect of Miller Compensation: shifting the output pole to high frequencies
Then, it is equivalent to a resistance:
This resistance "sees" a capacitance:
This sets a pole at:
Note: Rv is actually the op-amp output resistance at medium and high frequencies. It is of the order of 1/Gm2 and is much smaller than the value in dc (order of rd).

## Slide 30
Second effect of Miller Compensation: shifting the output pole to high frequencies
Series of C1 and C2

## Slide 31: Miller Factor and overall transfer function
Miller factor:
Factorizing A:

## Slide 32: The zero introduced by RC-CC
If RC=0
(no RC)
There is a zero in K(s):
This zero occurs also in the overall transfer-function of the amplifier (A). It cannot be cancelled by an equal zero, since an unstable pole (>0) would be required

## Slide 33: Effects of the zero in the transfer function
With this choice for RC, we can eliminate the zero and cancel its bad effect on the phase delay.
Other possible choices are possible:
for Rc>1/Gm2 it is possible to change the positive zero into a negative one and use it to compensate fp2.
Degradation of the phase margin
Thanks to RC:

## Slide 34: Summary of pole splitting
Capacitor CC introduces a feedback across the second stage that:
Puts an equivalent large capacitor (CCGm2R2>>C1) across the output resistance of the first stage (R1) shifting the first pole back to very low frequencies
Reduces the output resistance (RV) at medium/high frequencies from R2 to a value close to 1/Gm2. This shifts the output pole to much higher frequencies.
Resistor RC is significant only at high frequencies and "shapes" the zero, either cancelling it or turning it into a negative zero

## Slide 35: Pole splitting, graphical view
Before compensation
After compensation

## Slide 36: Summary of singularities
This third pole (s3= -w3), can be guessed considering that at very high frequencies the whole network reduces to the three capacitors and resistor RC.