## Slide 1: Amplifier Norton schematization with output referred noise source
ion-sc
vi1
vi2
vin
Ym(s)vin
vo
zout
It is possible to model any amplifier
(whole amplifier or single amplifier stage) with a Norton equivalent circuit of the output port
Input referred noise voltage
and take into account noise with an additional current source ion-sc
General input-output law of a voltage amplifier with noise/offset:

## Slide 2: General method to calculate the input referred noise / offset
Generic amplifier with M internal noise current sources
Step 1. Noise sources off, input signal on, determine Ym
Step. 2 Signal off, determine ion-sc with the superposition theorem

## Slide 3: Application of the method to the two-stage op-amp
h
Gm1vid
R1
C1
i1n-sc
vid
It is convenient to calculate the equivalent output noise currents of the two stages individually, and then study the whole amplifier using the following equivalent circuit.
o
vout
Gm2v1
R2
C2
v1
i2n-sc
RC
CC
First stage
Second stage
First stage
Second stage

## Slide 4: Output noise short circuit current of the first stage
In order to calculate the output noise short-circuit current, we need to calculate the current gains AIk, from each one of the MOSFET noise sources to the output short circuit current.
Input stage with noise current sources of all devices

## Slide 5: Effect of in3, in4
in4 is directly connected to the output port, then it flows directly into the output short circuit:
in3 is directly connected to the input of the current mirror. It sees a low resistance towards the mirror and high resistance towards M1 (2rd1). Then it flows almost completely into the mirror and reaches the output port after an inversion (caused by the mirror).

## Slide 6: Effect of in7
In the case of perfect symmetry and zero input differential voltage (Vid=0), which is the case that we are analyzing:
If a relatively large input differential voltage is present, a can be significantly different from 0.5 and the effect of in7 is no more negligible.
In the following part of this analysis, we will consider a=0.5

## Slide 7: Effect of in1, in2
Since in1 and in2 are floating, we can split them into two sources with a terminal at gnd.
in1-a: same effect as in3: AI1-a  -1
in1-b: same effect as in7: AI1-b  0
Repeating the procedure for in2

## Slide 8: Putting all contribution together for the first stage:

## Slide 9: Equivalent output noise current of the second stage
Equivalent small signal circuit with current sources
No input signal because we are calculating the effect of noise

## Slide 10: Putting the two stages together
Step 1. Calculate the Ym of the op-amp
AIh is the transfer function (current gain) from a current source connected between node h and gnd to the output short circuit current

## Slide 11: Calculation of AIh
admittance YC

## Slide 12: Calculation of AIh
AIh drops below 1 (0 dB)
around the unity-gain
frequency of the op-amp:
dc value:
qualitative frequency
dependence

## Slide 13: Let us come back to the noise
Circuit for calculation of the total output noise current

## Slide 14: In the simple 2-stage op-amp
A more interesting formula can be obtained substituting the equivalent gate noise voltage

## Slide 15: Input noise density of the op-amp
For this amplifier ID3=ID1, then:

## Slide 16: Thermal noise
using:

## Slide 17: Flicker noise
using:
with:

## Slide 18: General considerations about the op-amp noise:
Let us recall the thermal noise and use: gm1=ID1/VTE1)
For both the thermal and flicker noise, it is convenient to set F<<1 (VTE1<<VTE3)
The larger ID1, the lower the input thermal noise voltage density
A small VTE1 helps obtaining small thermal noise densities with lower current
A small flicker noise density can be obtained using large M1 and M3 areas
Thermal
Flicker

## Slide 19: Input offset voltage of the op-amp
Op-amp with the equivalent current sources that takes into account parameter variations
Let us just replace the noise current sources with the equivalent current sources of parameter variations
Note that M1,M2 and M3,M4 form pairs of matched devices.
Then, we can group their parameter variation sources into single contributions that contain only matching errors

## Slide 20: Input offset voltage of the op-amp
in strong inversion

## Slide 21: Input offset voltage of the op-amp
F
Contribution of the input pair devices
Contribution of the mirror devices
in strong inversion:

## Slide 22: Input offset voltage of the op-amp: standard deviation

## Slide 23: Design for input offset voltage
Total gate area of the input pair and mirror:

## Slide 24: Offset voltage: area optimization procedure
Example: if a=1, we are assigning the same area to the input pair and to the mirror
Optimization problem: find the value of a that allows obtaining the required svio with the minimum area occupation.
We need to find the minimum of this function of a

## Slide 25: Offset voltage: area optimization procedure
only these two terms depend on a. then
we have to find the minimum of:
a
f(a)
(a>0)

## Slide 26: Current consumption of the op-amp
In this section, we will consider the main factors that affect the current consumption of the operational amplifier.
We have already found an expression that ties the current consumption with the GBW specification
Here, we will review that expression, introducing also the role of the "F" parameter that comes from the noise and offset analysis
After that, we will find an expression of the current consumption that highlights the relationship with the thermal noise specification

## Slide 27: GBW and supply current (from the GBW and jm design procedure)
Since VGS5=VGS3
define:
Fraction due to
the second stage
Fraction due to
the first stage

## Slide 28: Current consumption of the op-amp - role of the thermal noise spec
If the "dominant" specification is the thermal noise PSD (SVn-th), we can use a different expression
Let us start again from the general formula:
We need to highlight the role of gm1
... and consider the expression of the input thermal noise voltage PSD:

## Slide 29: Current consumption of the op-amp
Fraction due to
the first stage
Fraction due to
the second stage
Note:
low thermal noise (Svn-th) means high current consumption
Note: F and 1/F appear: an optimum F value can be calculated

## Slide 30: Examples
Case 1:
Case 2: as above, but the GBW specification is replaced by noise specs:

## Slide 31: Consistent and contrasting specifications
As we have seen in previous example, the GBW specification and thermal noise density specification are consistent, since for both the following rule holds: the stricter the specification, the higher the required supply-current.
If the design include both specifications, then one of them is likely to be dominant. In the previous example, the noise specification dominates: the minimum supply current required to meet the required noise specification is much larger the current required for the given GBW-CL combination. Then, if we design the amplifier for the noise density, we certainly meet the GBW requirement.
Other specification pairs are likely to be contrasting: thermal noise and speed are in contrast with the supply current specification. The same can be said about flicker noise and area.

## Slide 32: Action of various specifications:
GBW
Svn-th
gm1, gm5
CL, jm
gm1, gm5
Flicker Noise
Offset
W1L1, W3L3
W1L1, W3L3
F
VTE1
A0
VTE1, VTE3, L1, L3, L5, L6,
W1/L1, W5/L5
W1/L1, W5/L5
gm3
W3/L3
W1,L1,W3,L3, W5,L5
AREA
Power Consumption
VTE5
VTE1

## Slide 33: Commercial products: high speed - low thermal noise CMOS op-amp
low power?

## Slide 34: Commercial product: low power op-amp