## Slide 1: Introducing myself
Michele Dei: michele.dei@unipi.it
Teaching during this year: ~20 hours
Topics: Comparators, ADCs, DACs, Integrated Filters
New here! My hope is to maintain the high standards of this teaching

## Slide 2: Comparators
Ideal Input/Output response
Symbol (differential input kind)
Detect the sign of a differential analog signal. Sometimes S/E input case: Vi2 is derived from an internal voltage reference
Codify the outcome in digital domain

## Slide 3: Applications
Building block in:
Mixed-signal front-ends: sensors AFEs; signal-processing (ADCs, DACs)
Signal-and-function generation
Digital communication (symbol recognition in a noisy channel)
Artificial neural networks (perceptron: linear binary classification)

## Slide 4: Continuous-time vs dynamic comparator
Continuous-time (CT) comparator:
Used in level-crossing event-driven circuits
Static power consumption
Can be designed in order to embed hystheresis
Output always valid
Dynamic comparator (or latched comparator):
Used in clock-synchronous circuits (as the comparator needs a driving clock signal)
No static power consumption (in basic single-stage configuration)
No hysteresis
Sometimes: output valid only during half clock period
Vi1
Vi2
Vout
Vi1
Vi2
Vout
Vout
Vi1
Vi2
clk
With hystheresis
Without hystheresis

## Slide 5: CT Comparators: amplifier-based implementations
A high-gain amplifier can be used as a comparator:
Op-amp topologies can be used in open loop or even positive feedback:
Speed is prime: no frequency compensation (no stability issues)
Accuracy loss: a region exists where the logical level is undefined
In several applications this may lead to unwanted stable or metastable states (→)
“0” or “1”?

## Slide 6: CT Comparators: amplifier-based implementations
Glitches for slow varying input common issue to all CT comparators without hysteresis
If level crossing is used as trigger in a complex system with feed back: time uncertainty and/or stability issues
If the comparator is interfaced with a synchronous digital FSM: Thold, Tsetup violation (need for synchronizer circuit otherwise data are loss)
Transient behaviour:
(RTI noise on Vi1 port)

## Slide 7
Thanks to the hysteresis, the comparator produces a valid output level across the whole input range. Use of positive feedback: “vertical” edges.
The hysteresis introduces an uncertainty band that reduces the accuracy but helps rejecting noise when the input differential voltage is close to zero.
Possible regenerative comparator: Op-amp-based Schmitt trigger.
Drawbacks
Over-sized solution for integrated cells
Low impedance on the non-inverting input
Regenerative comparators: hysteresis

## Slide 8
Programmable hysteresis from 0 to 160 mV (ΔVH) depending on current on pin HYS
No built-in hysteresis. Datasheet suggests Schmitt trigger configuration
HYS input
The digital output has its own VDD
Off-the-shelf devices

## Slide 9
Four-transistor hysteresis cell
Inputs: I1, I2
Outputs: V1, V2
Formed by:
Cross-coupled MOSFETs M2-M3
Load MOSFETS M1, M4
Constraint:
I1 + I2 = I0 = constant
Analysis: I2 in [0, I0]
Notable points:
I2 = 0; I1 = I0
I2 = I1 = I0/2
I2 = I0; I1 = 0
Compact comparator cell for Systems on a Chip
b2,3 = bC
b1,4 = bL

## Slide 10
Let us start from: I2=0 (I1=I0)
since:
Considering M4 and M2:
Then it is M1 that carries all current I1:
(M3 is on)
Analysis of the four-transistor cell: starting point

## Slide 11
Analysis of the four-transistor cell: starting point
V1, V2
Design condition: we size bL in such a way that:
The reason will be clear later

## Slide 12
Analysis of the four-transistor cell: increasing I2
V1, V2
As I2 increases, I1 decreases by the
same amount, then V1 decreases:
V2 increases:
as a consequence of I2 increase while VGS3=V1 decrease
Until V2 < Vt: M2, M4 are off

## Slide 13
Analysis of the four-transistor cell: V2 reaches Vt
V1, V2
For V2 = Vt, M2 and M4 are still off.
Then (M1 and M3 have the same VGS):
Hypothesis: If M3 is now in saturation:
βL
βC

## Slide 14
Analysis of the four-transistor cell: M3 saturation hypothesis
V1, V2
Let us check whether M3 is now in saturation
(was in triode region at the beginning)
For the design condition mentioned earlier
OK

## Slide 15
Analysis of the four-transistor cell: V2 reaches Vt
V1, V2

## Slide 16
Analysis of the four-transistor cell: starting from the opposite end point
V1, V2
Repeating the same procedure but starting from the rightmost point (I1 = 0, I2 = I0), we obtain a symmetrical behavior (around I0/2) with V1 and V2 interchanged.
Now V1 reaches Vt for I1/I2 = rH.

## Slide 17
Analysis of the four-transistor cell: combining the two behaviours
In this region, there are two possible stable states, depending on which extreme we started from:
This means that there is hysteresis
Now, we investigate what happens when the lower voltage hits the Vt line

## Slide 18
M2 and M4 turn on (while M1 and M3 are still on)
Let us focus on M2
1. As M2 turns on, it start stealing current from M1
3. VGS3 =V1, then ID3 reduces, increasing the current that flows into M4
2. V1 decreases:
4. V2 increases:
5. VGS2 =V2, then ID2 increases further
Positive feedback loop
Analysis of the four-transistor cell: phenomena that happen when V2 overcome Vt

## Slide 19
Each half circuit is equivalent to an amplifier
Small signal equivalent circuit
Due to the presence of the rd's, the magnitude of A is slightly less than
Positive feedback loop: small-signal analysis

## Slide 20
A1
A2
Positive feedback
When V2 overcomes Vt, all MOSFETs are on:
Positive feedback loop: small-signal analysis

## Slide 21
Therefore, a stable condition cannot exist if all MOSFETs are on.
(DC instability)
V1 and V2 cannot be greater than Vt at same time in a stable condition
Then, when M1 is on, M4 is off and vice versa
Important condition
Positive feedback loop: regeneration

## Slide 22
In this case, the positive feedback is unable to cause an abrupt transition:
Hysteresis is not present
Positive feedback loop: non-regenerative case (no hysteresis)
This configuration is never used
(should be regarded as a design error)

## Slide 23
Proceeding from the left, when V2 overcomes the Vt line, the positive feedback makes the voltage evolve autonomously
The new stable solution is the one we already found proceeding back from the right: the regeneration stops when loop gain is no longer > 1
Positive feedback loop: the “click”

## Slide 24
Only one stable solution exists in these regions
Unstable solutions in this region (all devices are on)
+ 2 possible stable solutions (either M1, M3 off or M2, M4 off)
Positive feedback loop: stable characteristics and unstable solution
I2 > I1:
V2 up, V1 down
V2
V1
Suppose forced initial condition:
½ probability to evolve to one of the two stable solutions
Most probable evolution?

## Slide 25
We start with a p-version of the hysteresis cell
Currents I1 and I2 are derived from the input voltage Vid=Vi2-Vi1 by means of a differential pair
Only one at a time between V1 and V2 is greater than the p-mos threshold voltage.
If V1> |Vtp|, V2<|Vtp| MA, MB and Mo2 are on, while Mo1 is off:
If V2> |Vtp|, V1<|Vtp|, only Mo1 is on:
A simple comparator based on the 4-transistor hysteresis cell

## Slide 26
Using a linear approximation of the differential pair:
A simple comparator: upper threshold (VH)

## Slide 27
In quiescent conditions:
Dividing the upper equation by the lower one:
A simple comparator: upper threshold (VH)

## Slide 28
A simple comparator: complete characteristics

## Slide 29
Make VTE1 as small as possible
Make rH just slightly larger than 1
However, other requirements impose to make rH significantly larger than 1, because:
The calculated |bA|=(rH)2 is overestimated, since we have neglected the rd's
Process error can make rH < 1 if the margin to 1 is too small
The transition is faster with larger |bA|
A typical robust choice:
DVH as small as 50 mV
To obtain a small hysteresis
A simple comparator: minimum achievable hysteresis

## Slide 30
The simplest solution is using a pre-amplifier:
In discrete time systems the amplifier offset can be canceled with CDS
gain G:
The hysteresis is divided by the preamplifier gain (G)
A simple comparator: low hysteresis using a preamplifier

## Slide 31
This comparator is designed
to have a large hysteresis
When Vout=0, the capacitor is charged by IP
When Vout=1, the capacitor is discharged by IN
VR+VH
VR+VL
VC
A simple VCO for low-frequency applications
First step: place the comparator in a feedback loop with a current-controlled charging-discharging mechanism

## Slide 32: A simple low-frequency VCO: oscillator frequency
rise time =
fall time =
period =

## Slide 33: A simple low-frequency VCO: Implementation with "current starved" inverter
IP
IN
If IP = IN = Itune:
The frequency is proportional to the tuning current (CCO)
Using a linear voltage to current converter it is possible to make Itune to be proportional to a voltage, transforming the CCO into a VCO

## Slide 34: A simple voltage-to-current converter
OTA
The OTA, and M1 form a two-stage op-amp with output on node H, stabilized by CC (Miller compensation). The op-amp is closed as a buffer:
This circuit can be used also to produce constant currents from a single reference voltage

## Slide 35: Speed and metastability issues
Small signal equivalent circuit of half cell: + inertial component (C)
RV: negative signed for regenerative
positive feedback
Metastability: the comparator does not provide a clear logical output level in a given amount of time

## Slide 36: Speed and metastability issues
Approximations around the “click” points:
Not rigorous but useful for understanding purposes: the circuit is non-linear anyway. Accurate results only through electrical simulations

## Slide 37: Speed and metastability issues
Under this approximation, the circuit is completely symmetric:
We can study only half circuit, for simplicity

## Slide 38: Speed and metastability issues
Transient response characterized by growing
exponential response: eat
Hence, the higher βA, the faster is the response (as mentioned previously).
Designing low-hysteresis comparator by pushing βA close to 1 is a BAD IDEA: not only process sensitivity may lead to lack of hysteresis, but also the comparator would result very slow:
The pre-amp solution with is always used in such cases

## Slide 39: Syllabus
Design of integrated comparators
Done (today’s class):
Ideal behaviour
Applications
Taxonomy
The 4T-hysteretic cell for SoC
Simple comparator based on the 4T-hysteretic cell
Low-frequency relaxation oscillator based on simple VCO
Notes on speed and metastability (optional material)
To do (next class):
Dynamic comparator example: the StrongARM case
Other comparator structures from literature (optional material)