## Slide 1: DAS: Data Acquisition Systems
A DAS is required to allow an electronic system to get information on the external environment
The development of extremely miniaturized DASs capable of detecting a large number of different and inhomogeneous quantities is currently urged by emerging fields, such as robotics, security and health care.
This is giving a significant contribution to the request for analog and mixed signal integrated SoCs
The design of a DAS involve architectures and specifications that recur in many other branches of analog and mixed signal microelectronic circuits.

## Slide 2: The electronic system and the enviroment

## Slide 3: Main blocks of an Electronic System
DAS (full acquisition operations)

## Slide 4: Elements of a DAS: a two-channel case

## Slide 5: Signal classification on the basis of quantization
Magnitude
Time

## Slide 6: DAS estimation errors
Identity (ideal DAS)
Actual value of the
Input quantity
(as measured by the
Reference instrument)
Output stream of
estimated values
Total error
(input referred)
In d.c
Is the input offset

## Slide 7: Sensitivity factors
0 1 2 3 4
j
i

## Slide 8: Block diagram of the DAS with error sources and a few sensitivities

## Slide 9: Input referred contribution corresponding to an error source
Input referred (RTI)
contribution of exi

## Slide 10: Effect of non-linear response on the RTI error
smaller k
larger RTI error
larger k
smaller RTI error
Even a simply addittive error may give an RTI error that depends on the value of the input quantity

## Slide 11: Error on dependent quantities

## Slide 12: Error on Angular Quantities
X
Y
V
q

## Slide 13: Error on angular quantities

## Slide 14: Type of errors
Quasi static: offset, gain, non-linearity These errors are nearly constant when the input quantity is constant (their variation is much slower than the system time-constant)
Dynamic errors These errors are caused by the system finite speed of response and are absent when the input quantity is constant
Noise The error caused by noise is always present, time varying and random. Only the statistical properties of noise are known. The mean value of noise is zero.

## Slide 15: Quasi-static errors: offset
Output offset
Input offset

## Slide 16: Quasi static errors: Gain error
The gain error can be easily defined for linear systems. If the system is non-linear, we can refer to a linear approximation.
For a linear system, nominally:
In a real system:
If kX-real is unknown, we must use the nominal gain (kX-nom) to
Estimate Xm from Vxi-real
-Xe-gain

## Slide 17: Quasi static errors: Gain error
The result of the gain error (xe-gain) is proportional to the input quantity (it is not an addittive error)
To estimate the result of the gain error we must take into account the relative gain error Dk/k
Design approaches to reduce the gain error:
Make transfer functions as much as possible dependent on ratios of omogeneous quantities. These ratios are minimally sensitive to process errors and temperature.
The number of non-dimentionless quantities that should appear in the transfer function should be as small as possible and these quantities should be related to precision components or adjustable components.

## Slide 18: Ratiometric systems
In a ratiometric system, the sensitivity is proportional to the supply voltage Vdd.
VX
kX
In this way the need of a precise and stable VREF for the ADC is removed

## Slide 19: Non-linearity errors
Generally the maximum non linearity error in the whole range of the input quantity X is indicated in the secifications
If the non-linear curve is well reproducible, the non-linearity error can be compensated for by means of a non-linear estimator.
For random non-linearities, individual multi-point trimming is necessary.

## Slide 20: Dynamic errors
Settling time tset:
Time required to have the
output voltage stay close
to the final value within
a given relative error
Typical error specs:
1 % (low accuracy)
0.01 % (high accuracy)

## Slide 21: Linear time and slew-rate time
Linear-time only
(all stages behave linearly)
Slew-rate only
(most of the transition time at least one stage is saturated)

## Slide 22: Noise
Interval | Total interval width (xnp-p) | Probability | 1 - probability
±s | 2 s | 0.683 (68.3 %) | 0.317
±2s | 4 s | 0.954 (95.4 %) | 0.046
±3s | 6 s | 0.997 (99.7 %) | 0.003
±4s | 8 s | 0.999936 (99.9936 %) | 6.410-5
Xn-pp
If we sample the output
Signal Xm, then the standard
Deviation of the samples is:
Cf= crest factor

## Slide 23: Noise and resolution
X
Transition X  X+DX
Samples in this range are compatible
with both the X and X+DX input.
Therefore, it is not guaranteed that
a difference DX can be recognized
The minimum difference that
can be detected (resolution)
Involve noise bands in contact
but with null intersection.

## Slide 24: Detection limit
The detection limit xdl is the minimum value of the input quantitity that can be distinquished from a zero input.
For X=0
max(|xio|)+
xn-pp
2
max(|xio|)
-max(|xio|)
max(|xio|)+
xn-pp
2
-[
]
0
xdl
vio can be
anywhere in
This band
Total uncertainty
band

## Slide 25: The Dynamic Range (DR)
Xmax
Xmin
Xmax-Xmin=XFS
Signal range
Full scale (excursion)
dx can be:
The resolution (most frequent case)
The detection limit
The maximum total error (combination of offset + noise + non-linearity)

## Slide 26: DR and maximum number of significant levels
Xmax
Xmin
XFS
Let us consider that dX is the
System resolution
dx
Fist level that the system can distinguish from Xmin
Number of distinguishable levels = DR
The presence of noise cause a sort of quantization of the analog signal, at least in terms of usable levels

## Slide 27: Dynamic range of a cascade of blocks (series connection)

## Slide 28: DR in series-connected blocks