## Slide 1: Low frequency disturbances: offset and flicker noise
The offset strongly affects the accuracy of most sensor interfaces and their detection limit
When the quantity estimation require integration operations, such as dead reckoning (position from acceleration or speed), the offset result in a drift of the final quantity.
The flicker noise, with its power accumulation at low frequency, make the problem worse, reducing resolution.

## Slide 2: State of art of amplifier offset
The best amplifiers use BJTs and resistor trimming, to achieve offsets as low as 15 mV with 0.1 mV/°C drift (typical) and low frequency noise < 0.5 mV pp in the 0.1-10 Hz frequency band.
It is obtained with very large area and a non-CMOS technology, resulting non suitable for modern SoCs.
Trimming of the individual amplifiers is required
In many examples of sensor interfacing, offsets as low as 1 mV are required.
This option is often not convenient:

## Slide 3: Dynamic techniques for the offset and noise flicker reduction
Auto-zero (AZ)
Correlated Double Sampling (CDS)
Chopper modulation (CHS = Chopper stabilization)
Three main techniques
We are interested in understanding the principle of operation, the residual noise spectrum and possible limitations of the various techniques.
The three techniques are not limited to pure electronic circuits, but can in general be applied to other physical systems and, in particular, in a DAS, may involve also the sensor.

## Slide 4: Premise
In all cases, in order to simplify the formalism, we will refer to the case of a voltage amplifier:
where vn includes both the input referred noise and offset voltage.
If we remove the signal from the amplifier input, the output becomes:
Voltage - input
Current - input
Nulling the input
signal in:

## Slide 5: Auto – Zero (AZ)
Two phases: AZ and NO (Normal operation)
Principle:
In the AZ phase the signal is removed and the effect of vn (noise/offset) is stored in a memory (typically an analog memory, i.e. a capacitor)
In the NO phase, the signal is connected and the vn value stored in previous phase is subtracted.
Example, for an amplifier with voltage input

## Slide 6: Signals and noise during the AZ cycle
clock
ts
AZ
NO

## Slide 7: Auto-Zero: phases and signal diagrams
NO
AZ

## Slide 8: Auto-Zero simplified noise model
We consider that the duration of the AZ phase is negligible (ideally zero), then the amplifier is in NO phase during the whole period.
T
2T
3T
nT
(n+1)T
vn(t)
for each clock cycle, tS coincides with the beginning of the cycle
tS instants form a discrete set
(a sequence nT)
AZ
AZ
AZ
AZ
AZ

## Slide 9: Calculation of the spectrum of the residual noise vn-eff
We consider a single realization of the noise random process
Vn(f)
Fourier Transform
fS
2fS
-2fS
-fS
0
+
-

## Slide 10: Calculation of the spectrum of the residual noise vn-eff
H0(f)
H1(f)
Zero-order replica extracted from the sum

## Slide 11: Calculation of the spectrum of the residual noise vn-eff
Now, remember that this transformation is applied to the rendom process vn(t) with spectral density Svn(f):

## Slide 12: Calculation of the spectrum of the residual noise vn-eff
|H0(f)|2
The 0-th replica is weighted by H0(f):
The offset is cancelled
The flicker noise is strongly reduced
For f>>fck (fS)the spectrum is nearly unchanged
fS
-fS

## Slide 13: Contribution of replicas other than 0-th one
For f<fck (fS), several contribution equal to SVBB are added together. For f<<fck the sinc leaves the sum unchanged
The offset delta functions and the flicker regions of each replica fall over one of the zeros (at fck) of the sinc and are deleted or strongly reduced
for f>>fck: large attenuation

## Slide 14: In Summary:
Contribution of replicas different from 0-th
for f<<fck
Region f<<fck
Approximate effective noise PSD

## Slide 15: Example: LTC 1051, a commercial auto-zero operational amplifier

## Slide 16: Correlated Double Sampling (CDS)
CDS is a sampled data approach. Both the signal and the noise are discrete-time signals.
It involves two clock phases: phase 1 and phase 2
phase 1
phase 2
(n-1)T
(n+1)T
nT
nT-td
at nT the signal is sampled
(together with noise/offset )
at nT-tD the signal is removed
and the noise/offset is sampled
clock cycle

## Slide 17: Correlated Double Sampling
The output voltage at instant NT of the system that adopts the
CDS technique is the difference between the two samples:
We have the subtraction of two samples (hence "Double Sampling").
If the sample are similar ("Correlated") they cancel each other effectively
Differently from the autozero, also the signal is sampled.
Then, all limitation coming from the Shannon theorem applies

## Slide 18: CDS: effective noise
Generally, tD = , thus:
The operation applied to the noise involve sampled data and should be analyzed using the typical approaches of this domain, such as the Z-transform.
Problem: not all samples are sampled at instants that are multiple of T

## Slide 19: CDS: effective noise
It is then preferred to use a mixed continuous-time / discrete-time approach, that does not represent the actual operations but that gives the same final result.
Equivalent model of the operations applied to the original noise by the CDS approach.
CT
DT
Sampling at intervals nT
we obtain the CDS effective
noise
nT
nT

## Slide 20
CDS: effective noise
H(f)
We are interested in the transfer function from the input of the model to the input of the sampler. In the frequency domain:

## Slide 21
CDS: effective noise
Noise spectral density:
4
fck
2fck

## Slide 22
CDS: effective noise
=
X

## Slide 23: Effect of sampler
fck
2fck
+
=1

## Slide 24: CDS: Residual noise in the DT frequency domain
2kfck
(2k+1)fck
Every two replicas (an odd and an even replica) we have a contribution equal to 4SBB.
even
odd
DT domain
odd + even replica
Total number of replica pairs:
Total PSD in
the DT domain:

## Slide 25: Chopper modulation: a premise.
f0
signal modulation
signal demodulation
SBB
sinusoidal modulation

## Slide 26: Problems of the sinusoidal modulation
Sinusoidal modulation requires a real analog multiplier (i.e a Gilbert Cell), that is marked by a very large equivalent input offset and noise.
Generation of sinusoidal waveform with precise magnitude is not simple using only on-chip components

## Slide 27: Chopper modulation: based on a square waveform
Dimensionless square waveform
with unity magnitude and strictly
50 % duty-cycle
Modulator and demodulator can be implemented by switch matrices: virtually free from 1/f noise and offset

## Slide 28: A simplified analysis in the time domain
Hypotheses:
The amplifier has infinite bandwidth and zero delay
The input signal (VS) is constant
Zero noise and offset

## Slide 29: Simplified time-domain analysis: how the offset is processed
The effect of the offset is
Vdm
OFFSET RIPPLE: frequency = fck
fH
The offset ripple is completely deleted if:
LPF: fH<fck
<m(t)>=0 (requires duty-cycle=50%)

## Slide 30: Chopper modulation: analysis in the frequency domain
The simplified analysis in the time domain is useful to gain an intuitive understanding of the CHS principle of operation but can give quantitative prediction for non-constant signal and noise components
In order to model the effect on non-constant signal and noise components it is necessary to perform the analysis in the frequency domain.
Fourier series of the m(t) waveform

## Slide 31: Effect of modulation on the signal
VS(f)
LPF

## Slide 32: Effect of modulation on the signal
Power of the modulating waveform m(t)
Power =
Application of chopper modulation in the case of INFINITE bandwidth and null delay does not alter the function and gain of the original amplifier

## Slide 33: Effect of CHS on the noise spectrum
LPF

## Slide 34: Effective noise PSD referred to the input
Application of chopper modulation in the case of INFINITE bandwidth result in cancellation of the flicker noise and in a residual noise in the signal bandwidth just equal to the broadband noise PSD of the original amplifier
No Noise foldover occurs!

## Slide 35: Effect of finite amplifier bandwidth

## Slide 36: Effect of finite amplifier bandwidth
Summation is now limited to a finite number of terms
Let us consider only positive vaules of index k
B

## Slide 37: Minimum amplifier bandwidth
Minimum amplifier bandwidth to amplify at least one signal replica
Case N=1
amplifier frequency response

## Slide 38: Effect of phase delays
simple delay
typical amplifier
phase response
Replicas that undergo a phase shift are attenuated when they are brought back to baseband.
For q=90° total cancellation of the contribution
For q=180° the sign of the contribution is reversed

## Slide 39: Time domain analysis with finite aplifier bandwidth

## Slide 40: Effect of the amplifier finite bandwidth on the output noise PSD
LPF
Maximum order of replica that still gives a contribution in the baseband:

## Slide 41: Finite bandwidth: effective input referred noise density
Amplifier effective gain:
Output noise PSD
N | 1 | 3 | 5 | 15
 | 0.8106 | 0.9006 | 0.9331 | 0.9747
1/ | 1.234 | 1.110 | 1.072 | 1.026
N | 1 | 3 | 5 | 15
 | 0.8106 | 0.9006 | 0.9331 | 0.9747
 | 1.234 | 1.110 | 1.072 | 1.026

## Slide 42: AZ, CDS and CHS compared
Residual noise at low frequencies
AZ:
CDS:
CHS:
The CHS technique gives the lower residual noise in the signal bandwidth, for the same broadband SBB of the original amplifier
The AZ and CDS techniques suffer from noise foldover, which is represented by the ratio B/fck. The minimum value of this ratio is not the same for the two techniques

## Slide 43: B/fck ratio requirements for AZ
In the AZ phase the amplifier passes from full output signal to a small value (-Avn). At the end of the AZ phase, the residual error should be small, otherwise part of the output signal is sampled together with the noise/offset

## Slide 44: B/fck ratio requirements for CDS
In the CDS the amplifier must settle to the final value in a period equal to half the clock cycle (T/2).
In practice, the requirement for small residual error (high accuracy) and the occurrence of the slew rate phenomenon impose larger value for B/fck. Generally:

## Slide 45: AZ, CDS and CHS compared
Method | Signal bandwidth (BS) | Residual baseband noise (f<fck/2) | fck constraints | Particular characteristics
AZ | BS=B |  | fck<<B | Maintains the original time continuous frequency response of the amplifier.
CDS | BS< fck/2 |  | fck<B/3 | Fully sampled data system.
CHS | BS<fck | SBB | fck+BS<B BS<fCK | Requires fully-differential architecture and the presence of an effective low pass filter.

## Slide 46: The ping-pong approach to reduce the B/fck ratio in AZ systems

## Slide 47: Simple example of circuital implementations
AZ Amplifier

## Slide 48: Simple example of circuital implementations
CDS Amplifier
f2-S
Vout
f2-S

## Slide 49: Simple example of circuital implementations
Chopper Amplifier
A differential input and differential output facilitate the implementation of the modulator and demodulator, respectively (fully-differential amplifier)
The amplifier gain cannot be arbitrarily high, otherwise the amplified offset could saturate the amplifier. Typical values of A are < 1000