## Slide 1: Single-Ended operational amplifiers
Voltage amplifiers
Very large DC gain
Stability over a wide range of negative feedback conditions.
High input impedance on both inputs
Differential input
Typical requirements

## Slide 2: Typical op-amp-based negative feedback loop
This is a design specification

## Slide 3: Requirement on the output impedance
Zout should be low enough to guarantee that A is large enough to maintain the relative error below the maximum value allowed in all the expected load conditions

## Slide 4: Example ADA4628 (Analog Devices)
Passing from RL=10kW to RL=2 kW the amplifier looses around 8 dB
A1
A2
RL1
RL2

## Slide 5: Output stages - specifications
Source
Sink

## Slide 6: Examples
OPA 377 (Analog Devices)
Linear Tech.

## Slide 7
Single supply case
In a single supply voltage circuit, the load cannot be connected to gnd (or Vdd) if we want a to impose both positive and negative voltages across it.
To achieve this result, the load should be applied across the amplifier output port and a proper constant voltage, typically equal to Vdd/2.
This voltage must be generated by a proper cell, starting from Vdd.

## Slide 8: Oputput stage classes
By subtracting two unipolar
currents, we obtain a bi-directional output current
constant Idev2

## Slide 9: Low power efficiency of class A output stages
The maximum symmetrical current coincides with Idev 2, which is a constant bias current.
Therefore, the maximum (symmetrical) output current is smaller than the quiescent current absorption.

## Slide 10: Class – A source followers
The large margin to to Vdd makes it not suitable for rail-to-rail output stages (practically mandatory in modern, low voltrage applications)
The n-MOS source follower can be used as a negative voltage-shifter
Because the circuit that produces Vin (driver) uses the same Vdd

## Slide 11
Margin to Vss
(too large for typical supply voltages used in modern CMOS processes)
The p-MOS source follower can be used as a positive voltage shifter.

## Slide 12: Class-A source followers: output current limits
The positive output current (IOP) is limited only by the MOSFET size
The negative output current (ION) is limited by I0, which is the quiescent supply current
n source follower
p source follower
opposite condition: it is the positive current to be limited by I0,

## Slide 13: Class AB – push pull source follower
Practically useless for the low supply voltages used in modern analog circuits, which require rail-to-rail output voltage swings
Imposes large margins to both the positive and negative rail

## Slide 14: Common source output stages: class-A case
Margins to the rails are now only a VDSAT, which is much smaller than a VGS.
The common source output stage has a practically rail-to-rail output swing

## Slide 15: Other info on the class-A common source
The input voltage is invariant to the supply voltages when it is referred to Vss: the preceding stage should provide an output with the same property
VGSn
-VGSp
I0
I0
p-version:
(the input signal is invariant when referred to Vdd)
n-version
class-A
class-A

## Slide 16: Small signal properties of the class-A common source stage

## Slide 17: Class-AB common source: principle of operation
Mn turns off
Mp turns off
push
pull
operating
point
class-AB control
(driver)

## Slide 18: Class-AB common-source output stages: maximum output currents
Different topologies are available for the class-AB driver. They differ for the maximum VGS that can be delivered to Mp and Mn and for the minimum supply voltage
Driver
bp , bn

## Slide 19: Class-AB common-source output stages: quiescent current
The driver must be able to set the quiescent current with a good accuracy, since IQ sets the operating point power consumption and the small signal performances of the stage
Quiescent condition:

## Slide 20: Class-AB common-source output stages: small signal behavior
vgn and vgp must have the same sign to produce in-phase effects on vout
Frequent case:

## Slide 21: Class-AB common-source output stages: equivalent voltage source
Vdd
Vss
Vout
Vgp
Mn
Mp
Vgn
VB
At least for small signals, this is equivalent to have a voltage source (battery) across the two gates.

## Slide 22: Class-AB common source: voltage shifter case
Voltage Shifter (positive)
Alternatively, we can connect Vin to VGp and use a negative voltage shifter to produce VGn.
Advantage: Simplicity
Drawback: low efficiency in terms of maximum VGS.

## Slide 23: Frequency response requirements: closed loop gain (bA)
180°
90°
fp
f2
fm
0°
|bA|
|b(0)A(0)|
bA
f0bA
f3
f4
The phase margin (fm) is the main stability indicator
The closed loop configuration is stable for fm>0
However, fm must be significantly greater than 0 to guarantee:
Stability even against all possible PVT variations
A step response with reduced ringing and overshoot
Typically, we require: fm>70°

## Slide 24: Amplifier gain and loop gain: role of the b factor
In this case, f0bA represents the -3dB upper band limit of the closed loop transfer function.
f0 is the unity gain frequency of the amplifier, equal to GBW (Gain-BandWidth for a dominant pole response
resistor-only or capacitor-only feedback networks

## Slide 25
Amplifier gain and loop gain: role of the b factor
f0b A
2
f0b A
1
b1
b2
fm
Worst case for stability:
maximum |b|: b= -1
b= -1
f0bA gets lower: smaller bandwidth for the closed loop transfer function.
fm increases: greater stability
Smallest phase margin
Unity gain configuration

## Slide 26: Example of non-unity-gain stable op-amp
Stability for gains for non-inverting amplifiers config.
The advantage is a large GBW

## Slide 27: Single non-dominant pole case
s | 0.5 | 1 | 2 | 3 | 5
fm | 26.6° | 45° | 63.4° | 71.6° | 78.7°
s is an important design parameter
design for
unity-gain stable
op-amps
frequent choice

## Slide 28: Design specifications for the amplifier response speed
Gain-BandWidth product (GBW)
For a single pole frequency response:
In a closed loop configuration, the upper
band limit is given by:
For the non-inverting amplifier:
The same relationships are approximately valid for dominant-pole
frequency responses
Slew rate (sR): this is the maximum slope that can be obtained from the output voltage. The slew rate affects the behavior for large and fast input transients
1.
2.
3.

## Slide 29: A possible set of specification for design of a CMOS op-amp
dc gain A0
Speed: Gain-Band-Width product (GBW) and Slew rate (sR)
Closed loop stability: e.g. phase margin in unity gain configuration and with a maximum capacitive load (CL)
Input referred voltage noise: Thermal : SvT, Flicker: kF=fSvF(f)
Offset (Input offset voltage: Vio)
Static power consumption (Isupply, minimum Vdd)
Maximum output current IOP-max, ION-max
Ranges: Input common mode range (CMR), output swing.
CMRR, PSRR
Area

## Slide 30: Design of an anolog cell: phases
Specifications
Choice of the topology
Device sizing
Number of stages, use of cascodes, amplifier class ...
We have to set the values of the Degrees of Freedom (DOFs): W, L, Ibias, VGS-Vt ...

## Slide 31: Operational amplifiers: number of stages
In the op-amp design terminology, the number of stages refer only to gain stages.
A gain stage is formed by a V-to-I converter and a network I-to-I that brings the output current(s) of the V-to-I converter to the output port.
V-to-I : two inputs n=2
two outputs m=2
I-to-I
single output:
k=1
Example

## Slide 32: Single stage op-amps
With very large Rout values, gains up to 100 dB can be obtained (cascode and regulated cascode architectures)
In the case of resistive loads, the gain falls down to
In the case of no resistive load (only capacitive load, as in switched-cap. circuits:
Includes the load brought by the feedback network

## Slide 33: Single stage op-amps with resistive load
In single gain stages, Gm coincides with the transconductance (gm) of a single device or is a linear combination of device transconductances
Can be as low as several tens of kW
In most practical cases, loading a single stage op-amp with an even moderate resistive loads means reducing the gain to very small values, not suitable for op-amp closed loop applications.

## Slide 34: Two-stage op-amps
(40 dB - 100 dB)
The resistive loads affects only the gain of the second stage.
Even in the case that the gain of the second stage falls down to a few units, the total dc gain remains as large as to be suitable for most closed-loop configurations.
The second stage is the output stage and must be designed to provide the required current and voltage ranges to the load.

## Slide 35: Considerations on the op-amp number of stages
Single stage op-amps: they can be designed to provide enough gain for a large variety of applications only in the case that the load and the feedback networks are capacitive (switched capacitor circuits). Their advantage is their simple frequency compensation and their power efficiency. Their stability increases with large capacitive loads.
Two-stage amplifiers: they are the most popular options for general purpose op-amps since they are suitable for both capacitive and resistive loads and can be designed to provide very large dc gains. Their stability decreases with large capacitive loads.
Three-stage amplifiers: this option is necessary when two stage amplifiers cannot provide enough gain. This is the case, for example of very low supply voltages that prevent the use of cascodes. The gain of two-stage amplifiers can be too low also in the case of very fast op-amps, where the gain of each single stage is limited by the necessity to use short-length MOSFETs. Three stage amplifiers requires complicated frequency compensation strategies, such as the nested-Miller compensation combined with feed-forward paths (multi-path architectures)