## Slide 1: Fully differential and unipolar (single-ended) circuits
Each signal is carried by a single wire. Signals (v1, v2, ...) are voltages differences between the wires and a common node (usually gnd).
Each signal is carried by a wire pair. Signals (v1, v2 ...) are the voltage difference between the wires that form the pairs..

## Slide 2: Fully differential systems: motivations
Lower sensitivity to interference
Wider output range
Better linearity
Advantages of fully differential circuit with respect to unipolar circuits
Drawbacks
Greater complexity (e.g. the feedback networks are formed by twice the components as in the unipolar case).
Require stabilization of common mode voltages.

## Slide 3: Interference coupling mechanisms
Ground currents (non-uniform gnd)
Vdd variations
Capacitive coupling
Substrate noise
Ground currents: ideal case
All interconnections have null series impedance. Gnd and Vdd can be considered as single nodes.

## Slide 4: Ground currents: real case
Physical interconnections have non-zero resistance and non-zero inductance
iG
Gnd and Vdd conductors carry considerable currents since they distribute power to all blocks.
vG
Current iG flowing in the ground conductor creates a difference vG between the two local grounds in the vicinity of blocks A and B.

## Slide 5: Critical cases
Isup-C
Isup-C
If block C is a digital circuit synchronized by a fast clock, its supply current Isup-C, contains spectral components up to very high frequencies.
The resulting interference on the analog circuits can be difficult to reject since high frequency components can fold-back to low frequencies through sampling (ADCs, SC circuits) or non-linearities.

## Slide 6: Origin of the ZG impedance.
Integrated circuits
Interconnect lines (tens of Ohm if gnd routing is not performed properly)
Vias (typically 0.1 Ohm / via)
Inductance is generally negligible up to a few GHz
Printed Circuit Boards (PCBs)
Interconnect resistances are in the mW range
Inductances can be significant
Board-to-Board interconnections (connecting wires)
Inductance is generally dominant
Contact resistance in connectors can be important

## Slide 7: Immunity of differential architectures to non-uniform gnd potential
The wires that carry the signals do not experience significant voltage drops, since the currents that pass through them is generally negligible.
Block B Diff. input
Differential components (signals)
Common mode components

## Slide 8: Vdd variations
Isup
Vdd
The cause of Vdd variation is the same that produces the gnd non-uniformity.
The effect on the signal is smaller, since Vdd is not commonly used as a reference for block-to-block signal transmission.
Coupling to the signal is mainly due to low PSSR. Single ended blocks have a PSSR that decreases steeply at high frequencies.
Note that the Vdd variation can be caused by the supply current of block B itself. Since the supply current generally depends on the input signal, this effect may result in an unstable feedback loop.

## Slide 9: Just a look to datasheets
Impulsive and high frequency currents (zero mean) are provided by the capacitor and do not run through the interconnections
100 nF
This practice can be also applied inside integrated circuits, but the small values of on-chip capacitors make it effective only for very high frequency components and comes at the expense of large area occupation.

## Slide 10: Optimal ground and Vdd distribution in mixed signal ICs.
Sensitive cells, such as analog blocks and noisy circuits, such as digital sub-units should be provided of separate gnd and Vdd power buses. The AGnd (analog gnd) and DGnd (digital gnd) will be connected in a single point, as close as possible to the gnd pad. Even better, they may have separate pads and the connection is made on the PCB.

## Slide 11: PSSR and CMRR characteristics of fully differential blocks
Symmetry axis
Symmetrical stimuli
Gnd potential variations
Vdd variations
Common mode signals
Global process errors
All types of symmetrical stimuli cannot produce any effect on the differential output voltage if the circuit is perfectly symmetric.
A reduced amount of leakage from symmetrical stimuli and differential quantities can be due to the unavoidable asymmetries caused by (1) process errors and (2) presence of large differential components due to large input signals.

## Slide 12: Interference capacitive coupling
It is possible to exploit the symmetry of a fully-differential block to get same interference signals on the two wires that form the input and output ports. To obtain this a symmetrical layout and environment is essential.
(e.g. a clock line)

## Slide 13: The substrate noise
progagation and
attenuation
body effect
Highly doped substrate
Lightly doped
epi-layer

## Slide 14: Approaches to reduce substrate noise
If the sensitive circuits (e.g. analog circuits) and the interference source (i.e. digital circuits) are sufficiently far apart, then substrate noise can be considered uniform over the area of the sensitive circuit.
In fully-differential architectures, it acts as a common mode interference and is rejected
Separate as much as possible the digital and analog circuit
Use guard rings of substrate taps to reduce propagation

## Slide 15: Other advantages of fully-differential circuits: double output range
Each single output (Von, Vop) has a range
The differentia output (Vop-Vop) has a range

## Slide 16: Other advantages of fully-differential circuits: increased linearity
Vod has the odd symmetry, then its Taylor polynomial calculated from the origin has no even terms
Greater linearity, lower harmonic distortion
(no even harmonics)
The single outputs (Von,Vop), in principle, have no symmetries, then all terms are generally present in the Taylor polynomial

## Slide 17: Fully differential circuits: the need for a stabilized output common mode voltage
Vic Vid
Voc Vod
VoC is too high: reduced range
An extreme case: no linear range
Ideal in-out relationship

## Slide 18: Input output characteristics in a fully-differential circuit: the correct feasible case
Ideal: zero input offset voltage (not possible, due to process errors)
Possible: there is an offset voltage, but the linearity range is still maximum
In the majority of fully-differential cells, the output common mode voltage should be stabilized and fixed to a convenient value.

## Slide 19: The fully-differential operational amplifier: definitions
The inverting output is placed on the same side of the non-inverting input to simplify drawing of closed loop configurations
This symbol means that the amplifier includes a common mode stabilization circuit

## Slide 20
The fully-differential operational amplifier: properties
Filtered version of the input noise voltage
Imperfect virtual short circuit
Contribution of noise to the input differential voltage in closed loop

## Slide 21: The "unity gain configuration"
It is common practice to indicate this configuration by "unity-gain".
This is improper because there is no available port to insert a signal.
However, this configuration is particularly useful in switched-capacitor circuits.

## Slide 22: Fully differential amplifier with resistive feedback
Analogous S/E configuration: inverting amplifier.
The fully-diff. version needs twice the passive components
In fully-differential architecture, speaking of inverting and non-inverting topologies is meaningless, since a sign change can be obtained by simply swapping the wires

## Slide 23: Fully differential amplifier with resistive feedback
b1
1-b1

## Slide 24: Fully differential amplifier with resistive feedback
Nominally b1=b2, but unavoidable
process errors (local errors) make
them different
It is convenient to split the two coefficients as a mean value and a difference:

## Slide 25: Fully differential amplifier with resistive feedback
+
-
Differential mode analysis

## Slide 26: Fully differential amplifier with resistive feedback
Add
Acd
relative
matching error

## Slide 27: Fully differential amplifier with resistive feedback
Nominal case:

## Slide 28: Fully differential amplifier with resistive feedback
We do not know the input common mode voltage
Generally, determination of the common mode voltage does not require high accuracy. We can use the nominal case.
We have to check that for all possible values of vSC, the input common mode voltage does not exceed the amplifier input CM range

## Slide 29: 3-op-amp fully-differential instrumentation amplifier
This circuit alone cannot be used as an instrumentation amplifier
since it has too low an input resistance
Nominal case
Rin-d=2R1
We could use input buffers built with single-ended operational amplifiers.
But there is a more versatile option ...

## Slide 30
3-op-amp fully-differential instrumentation amplifier
First stage: is identical
to the first stage of the single-ended in-amp
Second stage: reject the input common mode voltage and produces a stabilized output common mode voltage.
Often its gain is set to 1

## Slide 31: Versatility limits of the fully-differential operational amplifier
These are topologies that present a high input resistance. They cannot be implemented in the fully differential domain using a FD op-amp.
For example, the fully-differential unity-gain configuration, differently from its S/E counterpart cannot work as a buffer. There is not an input port available for the signal.

## Slide 32: Versatility limits of the fully-differential operational amplifier
Single ended op-amp (electrical symbol)
Fully-differential op-amp (electrical symbol)
Functional representation
Functional representation: in fully differential architectures every wire pair is a single signal

## Slide 33: The DDA: Difference Differential Amplifier
In a closed loop configuration, if the circuit is stable and the amplifier is in its linearity range (A>>1)
This is the equivalent of the virtual short circuit in DDAs. Note that, individually ViA and ViB can be large

## Slide 34: DDA-based instrumentation amplifier