## Slide 1: Mixed Signal Design Flow
System on a chip with distribution of analog and digital units
Digital control
unit
Analog units
Traditional mixed circuit system
(e.g. interface for a MEMS sensor)
Both are examples of Mixed Signal integrated circuits

## Slide 2: Possible design flows
Analog centric (or analog on top): the analog and digital units are designed with their proper tools and integration is performed using the analog tool.
Digital centric (or digital on top): the analog and digital units are designed with their proper tools and integration is performed using the (highly automated) digital tool.

## Slide 3: Analog Design Flow and examples of CAD tools
Schematic design
Electrical simulation
Layout design
Verification:
DRC
LVS
PEX
Virtuoso schematic editor
Analog Design Environment (ADE)
Spectre electrical simulator
Virtuoso layout editor
Assura
Calibre
CADENCE
Mentor
Graphics
PEX: Parasitic extraction (for post-layout simulations)

## Slide 4: A few screenshots from the Cadence environment
Library Manager:
Collects all libraries, cells and views

## Slide 5: The schematic editor

## Slide 6: ADE (Analog Design Environment)

## Slide 7: Layout: Automatic generation of components
It is possible to generate the instances of all cells or selected cells into the layout view
Moving the individual instances into the final position and connecting the cells together is generally performed manually, although automatic tools exist

## Slide 8: Layout Design: Manual Place and Route
The connection between components (instances) of the schematic view and their corresponding instances in the layout is maintained. Connection to be made in the layout are suggested dynamically.
Violations (DRC and, partly, LVS) are shown immediately during creation of the layout.
Final DRC and LVS performed on the whole circuit are still strictly necessary

## Slide 9: Digital Design Flow and CADENCE tools
High level description
(HDL - RTL)
Logic Simulation
Gate-Level Synthesis
Automatic Place and Route
CADENCE “Genus”
CADENCE “Innovus”
CADENCE “Xcelium”
Text Editor (e.g. "Gedit")

## Slide 10: High level description
The HDL description (e.g. in vhdl or verilog languages) must be done adhering to the RTL (Register Transfer Level) format, in order to enable the synthesis with all kind of digital standard cells. The RTL is ideal for the description of finite state machines.
Additionally, portions of code can be generated using specialized tools. For example, using dedicated MATLAB toolbox, it is possible to design digital filters and translate them into vhdl code.

## Slide 11: Gate Level Sinthesis
The RTL description is translated into a digital network formed by the elementary standard cells of the process.
The standerd cells are characterized with their timing parameters (delays) that the synthesiser use to produce a network free of set-up and hold violations.

## Slide 12: Automatic layout generation (Automatic Place and Route, P&R)
Standard cells:
Velirog description
Layout (LEF or GDS)
Gate level netlist:
Verilog description
Delay file
Automatic P&R tool
Automation script file
Layout (GDS)
Post P&R netlist (verilog)
In the P&R operation, the tool change the original network adding components that allow respecting the timing requirements (e.g. clock buffers)
The LEF format is more versatile than GDS, since it allows easy partial description (e.g. creation of layout abstract views, where only the information for the P&R are included

## Slide 13: P&R: a few important steps (can be automated)
At the beginning of the process, it is necessary to decide the area where the network must be placed by choosing the aspect ratio and the "density". Then the "channels" that host the standard cells are defined, with their power rails

## Slide 14: Result of P&R
Empty spaces between cells are covered by "filler" elements in the final layout. Fillers includes n-wells and other layers that improve continuity between cells

## Slide 15: Mixed Signal Design Flow: Analog Centric Approach
Analog Schematic design
Mixed Signal system level design
("pen-and-paper, SIMULINK-SIMSCAPE, VHDL-AMS, Verilog-A ...)
High level description
(HDL - RTL)
Logic Simulation
Gate-Level Synthesis
Analog cells
Digital cells
Mixed Signal Schematic design
Electrical simulation
Mixed Signal simulation
digital netlists
Automatic Place and Route
Analog Layout
(mainly manual)
Layout of the Mixed Signal Circuit
(mainly manual)
Verification
Digital layout

## Slide 16: Creation of the Mixed Signal schematic view
The Mixed Signal schematic is a conventional analog layout where a digital block is instantiated.
After a digital cell described with vhdl is imported into an analog library, three views are created:
entity counter is
.....
architecture fsm of counter is
.....
cell: counter
VHDL description
view: entity
view: symbol
view: fsm

## Slide 17: View symbol
The view "symbol" is created automatically starting from the "entity" part of the vhdl description, where the input and output pin are declared.
It is the symbol view that has to be used to create an instance of the digital cell inside an analog schematic view, forming the mixed signal schematic.

## Slide 18: Example of mixed signal schematic view
Analog cell
Digital cell

## Slide 19: Objects that are necessary for the Mixed Signal simulation
Mixed Signal Schematic
Views:
schematic
adexl
config
The view used by the ADE simulation environment
A view that has to be explicitly created and includes, for each instance, indication on which view has to be used in the simulation
ADE
Connect Rules
The connect rules associate electrical quantities to the logical values. They represent the interface between the digital (logical) and electrical world

## Slide 20: The config view
Instances of
cells
View to be used in the simulation

## Slide 21: Example of connect rules
High logic level: 1.8 V
Low logic level: 0 V

## Slide 22: Importing the digital cells after synthesis and P&R
Layout: gds file generated by the P&R
Symbol
Netlist gate-level
(imported as a schematic view)
Views of the imported cell , as they appear in the library manager

## Slide 23: Creation of the final layout of the mixed signal integrated circuit
Analog cell
Digital cell
Layout view
Schematic view
In the analog centric flow, the analog and digital cells are automatically instantiated into the layout following the schematic view. Generally, P&R is performed manually

## Slide 24: Example: the SENSIPLUS versatile sensor interface
Process: CMOS 0.18 mm
1.5 mm
Analog pads
Digital pads with I/O buffers
Digital finite state machine