## Slide 1: Comparators
ideal response
Symbol

## Slide 2: Comparators: amplifier-based implementations
An amplifier with very high gain can be used as a comparator. Op-amp topologies can be used with no need of frequency compensation
a region exists
where the logical
level is undefined
since the comparator is used in open loop configuration or positive feedback.
In several application this may lead to unwanted stable or metastable states.
For slow-varying signals, threshold crossing may be too noisy
Note:

## Slide 3: Regenerative comparators: hysteresis
Thanks to the hysteresis, the comparator produces a valid output level across the whole input range
The hysteresis introduces an uncertainty band that reduces the accuracy but helps rejecting noise when the input voltage is close to zero.
Op-amp based Smith trigger.
Oversized solution for integrated cells
Low impedance on the non-inverting input
Drawbacks
Possible regenerative comparator

## Slide 4: Commercial products
Programmable hysteresis from 0 to 160 mV DVh depnding on current on pin HYS
No built-in hysteresis. The
datasheet suggests Schmitt trigger configuration
HYS input
The digital output has its own Vdd

## Slide 5: Compact comparator cell for Systems on a Chip
Four-transistor hysteresis cell
Cross-coupled MOSFETs
Load MOSFET
b=bC
b=bL
Load MOSFET
b=bL
Currents I1 and I2 varies with the input signal in such a way that:

## Slide 6: Analysis of the four-transistor hysteresis cell: starting point
Let us start from: I2=0 (I1=I0)
since:
Considering M4:
Then it is M1 that carries all current I1:
(M3 is on)

## Slide 7: Analysis of the 4-transistor cell
Design condition:
we size bL in such a way that:
The reason will be clear later

## Slide 8: Increasing I2
As I2 increases, I1 decreases of the same amount, then V1 decreases:
V2 increases:

## Slide 9: Increasing I2
As I2 progressively increases, V2 decreases. Until V2 remains below the threshold voltage Vt, M2 and M4 are off

## Slide 10: V2 reaches the threshold
Let us check whether M3 is now in saturation (was in triode region at the beginning)
For the design condition mentioned earlier
For V2=Vt, M2 and M4 are still off. Then:
Since M3 is in saturation:
M3 is in saturation

## Slide 11: V2 reaches the threshold
Case of interest:
for
For bC>bL, V2 reaches the threshold when I2 has overcome the middle of the allowed range [0, I0]

## Slide 12: Starting from the other extreme
Repeating the same procedure but starting from the rightmost point (I1=0, I2=I0) we obtain a symmetrical behavior with V1 and V2 swapped.

## Slide 13: Putting the two behaviors together:
In this region, there are two possible states, depending on which extreme we started from
This means that there is hysteresis
Now we have to investigate what happens when the lower voltage hits the Vt line

## Slide 14: Phenomena that happen when V2 overcome Vt
M2 and M4 turn on (while M1 and M3 are still on)
Let us focus on M2
1. As M2 turns on, it start stealing current from M1
3. VGS3 =V1, then ID3 reduces, increasing the current that flows into M4
2. V1 decreases:
4. V2 increases:
5. VGS2 =V2, then ID2 increases further
Positive feedback loop

## Slide 15: Positive feedback loop: small signal analysis
Each half circuit is equivalent to an amplifier
Small signal equivalent circuit
Due to the presence of the rd's, the magnitude of A is slightly less than

## Slide 16: Positive feedback loop: dc instability
A1
A2
Positive feedback
When V2 overcomes Vt, all MOSFETs are on:

## Slide 17: The effect of positive feedback
Therefore, a stable condition cannot exist if all MOSFETs are on.
(dc instability)
V1 and V2 cannot be greater than Vt at same time in a stable condition
Then, when M1 is on, M4 is off and vice versa
Important condition

## Slide 18: The "click"
Proceeding from the left, when V2 overcomes the Vt line, the positive feedback makes the voltage evolve autonomously.
The new stable solution is the one we already found proceeding back from the right
M1,M3: on M2,M4 off
M2,M4: on M1,M3 off

## Slide 19: The two stable characteristics
Only one solution exists
(stable)
Three solutions exist:
2 stable
1 unstable (all devices are on)

## Slide 20: Non regenerative case (no hysteresis)
In this case, the positive feedback is unable to cause a real abrupt transition
A hysteresis is not present

## Slide 21: A simple comparator based on the 4-transistor hysteresis cell
We start with a p-version of the hysteresis cell
Currents I1 and I2 are derived from the input voltage vid=vi2-vi1 by means of a differential pair
Only one at a time between V1 and V2 is greater than the p-mos threshold voltage.
If V1> |Vtp|, V2<|Vtp| MA, MB and Mo2 are on, while Mo1 is off:
If V2> |Vtp|, V1<|Vtp|, only Mo1 is on:

## Slide 22: Calculation of the comparator upper thresholds
Using a linear approximation of the differential pair:

## Slide 23: Calculation of the comparator upper thresholds
In quiescent conditions:
Dividing the upper equation by the lower one

## Slide 24: Complete characteristics of the comparator

## Slide 25: Minimum achievable hysteresis
Make VTE1 as small as possible
Make rH just slightly larger than 1
However, other requirements impose to make rH significantly larger than 1, because:
The calculated |bA|=(rH)2 is overestimated, since we have neglected the rd's
Process error can make rH <1 if the margin to 1 is too small
The transition is faster with larger |bA|
A typical robust choice:
DVH as small as 50 mV
To obtain a small hysteresis

## Slide 26: How to obtain a comparator with very low hysteresis
The simplest solution is using a pre-amplifier:
In discrete time systems the amplifier offset can be cancelled with CDS
gain G:
The hysteresis is divided by the preamplifier gain (G)

## Slide 27: A simple low-frequency VCO based on comparator hysteresis
This comparator is designed to have a large hysteresis
When Vout=0, the capacitor is charged by IP
When Vout=1, the capacitor is discharged by IN
VR+VH
VR+VL
VC

## Slide 28: Calculation of the oscillator frequency
rise time =
fall time =
period =

## Slide 29: Implementation with "current starved" inverter
IP
IN
If IP = IN = Itune:
The frequency is proportional to the tuning current (CCO)
Using a linear voltage to current converter it is possible to make Itune to be proportional to a voltage, transforming the CCO into a VCO

## Slide 30: A simple voltage-to-current converter
OTA
The OTA, and M1 form a two-stage op-amp with output on node H, stabilized by CC (Miller compensation). The op-amp is closed as a buffer:
This circuit can be used also to produce constant currents from a single reference voltage