## Slide 1: ADC linearized model
Linearized model
vn includes all causes that make vin-dig different from Vin
The error due to quantization can be represented by a component of vn: the quantization noise:

## Slide 2: Signal to Noise Ratio and resolution
Input range of the ADC
Considering only quantization noise:

## Slide 3: Effective Number Of Bits (ENOB)
Distortion and SFDR (spurious free dynamic range)
PD=total power of the harmonics
Quantization and electrical noise
Also indicated with SNDR

## Slide 4: Quantization noise in the frequency domain
Vin is a dc signal
Since the ADC samples the input data, the output frequency domain is
[-fs/2,+fs/2]
The vnq spectrum
is a Dirac delta
Vin is fast-varying signal
of magnitude >> LSB
Two extreme cases
uniform distribution

## Slide 5: The uniform power spectral density (PSD) model for the quantization noise
This model is very useful and simple but should be applied with much care.
In real cases, the quantization noise depends on the input signal, and so does its spectrum.
The uniform spectral density model is acceptable when the input signal has magnitude and/or frequency such that the output levels are changed in a fast and almost random way.
This happens when the average time spent by the signal on a single level is short (of the order of the sampling time).

## Slide 6: Uniform quantization noise PSD: properties
Total vnq power:
For the same ADC, increasing the sampling frequency reduces the PSD of the quantization noise

## Slide 7: Oversampling ADCs
LPF
rOS=Over-Sampling Ratio (OSR)
Nyquist
rate
Oversampling ADC

## Slide 8: Resolution increment in a pure oversampling ADC
Considering two ADCs with same VFS
ADC1: SQNR1, n1
ADC2: SQNR2, n2
Premise

## Slide 9: Resolution increment in a pure oversampling ADC
"data stream"
ADC1
Resolution improvement
same ADC
ADC2 (oversampling)

## Slide 10: Pure oversampling ADCs: limits
A minor limit:
The oversampling approach is based on the assumption that the quantization noise respects the uniform PSD model
If the input signal is a dc, the quantization noise superimposed on the data stream will be constant and then will be unaffected by the LPF. A similar problem occurs with signals that are slowly-varying and/or have a small magnitude.
constant input
constant datum

## Slide 11: Signal dithering
Dithering
Dithering consists in adding noise to the signal.
Noise makes the ADC switch across the two adjacent levels closer to Vin
The added noise must have spectral components out of the signal band so that it is rejected by the LPF

## Slide 12: The real limitation of the pure oversampling approach
The pure oversampling approach is highly inefficient !
Example:
To obtain 16 bits of resolution from a 12 bit ADC:
In order to obtain a resolution increment of a single bit, the sampling frequency must be incremented by a factor of 4

## Slide 13: The Delta-Sigma (D-S) ADC
The Delta-Sigma converter combines two principles:
Oversampling: fs>>2Bs
Noise shaping
It was introduced in 1960
The term "Sigma-Delta (S-D)" ADC is simply a synonym.

## Slide 14: Delta-Sigma principle
The Delta-Sigma modulator (1st order)
we imagine to start with Vint=0
Vint
Vdst
ideal DAC
Vfb = Vdst
Vfb

## Slide 15: Delta-Sigma principle
The digital filter averages the data stream that, in the example, contains only Vk and Vk+1 levels.
The average will be a value between the two levels and will be closer to Vin.than both Vk and Vk+1
In this example, value Vk appears more frequently than Vk+1. Then the average will be closer to Vk, as actually Vin is.

## Slide 16: Delta-Sigma principle
ve
vfb
The average of Ve, performed over a very long time, must be zero, otherwise the output of the accumulator would diverge.
If the LPF filter has a bandwidth small enough, it can extract the average of the data stream Dk with arbitrary accuracy. If the DAC is ideal (no distortion), then the average of Dk gives Vin with an arbitrary resolution.

## Slide 17: Delta-Sigma principle
What we have seen so far suggests that the delta-sigma modulator can produce a data stream that, once properly filtered, can yield Vin with a higher resolution than the original ADC.
Differently from the pure oversampling ADC, the delta-sigma is capable of producing the alternation of two adjacent codes (Vk, Vk+1) even with a dc signal without dithering. In the case of an input dc signal, the constant error vn is modulated (this is the origin of the name) and can be filtered out.
As in the oversampling approach, it is necessary to filter the output data stream, reducing the bandwidth to the minimum required by the signal spectrum. We will show that high resolution increments can be obtained with moderate OSRs.

## Slide 18: Analysis of a first order delta-sigma modulator
D-S modulator
H(z) is a discrete time transfer function, properly represented with its z-transform.
Linearized model of the modulator. The DAC is considered ideal; thus, it simply translates the voltage representation of Dst (vst) in an exactly corresponding analog voltage (vfb=vst)

## Slide 19
Analysis of a first order delta-sigma modulator

## Slide 20
Analysis of a first order delta-sigma modulator
accumulator

## Slide 21: Analysis of a first order delta-sigma modulator
A simple delay of one clock cycle
This is the equivalent of the derivative in the DT domain

## Slide 22: NTF in the frequency domain

## Slide 23: Output spectral density of the quantization noise
The uniform PSD model of the quantization noise is acceptable because the modulator continuously changes the input of the original ADC, sweeping across the whole range [-D/2, +D/2] of the quantization noise.
For more accurate analysis of second order effects, the limits of the uniform PSD model should be taken into account.

## Slide 24: Quantization noise PSD at the output of the D-S modulator
Sn-OS(f)

## Slide 25
Quantization noise PSD at the output of the D-S modulator
for f=fS/2, the argument of sin2 is p/2

## Slide 26: Output noise power in the Delta-Sigma ADC

## Slide 27: Output noise power in the Delta-Sigma ADC

## Slide 28: Resolution increment in the first-order D-S ADC

## Slide 29: Resolution increment in the first order D-S ADC
Every increment of rOS by a factor of 2 produces a resolution gain of 1 and 1/2 bit (1.5 bits).
This gain was only 1/2 bit in the pure oversampling ADC
Example
This OSR value is rather large, but also the gain in resolution is very large

## Slide 30: ADC and DAC non idealities in D-S ADC
The DAC should be linear because it is in the feedback path. The DAC noise (that includes also non-linearity errors) are simply summed-up to the input signal.
Electrical noise, offset and non-linearity errors of the ADC are shaped by the high pass NTF of the modulator, then the effect on the signal BW is negligible.
ADC
DAC

## Slide 31: Single-bit D-S ADC
As we have seen, the DAC linearity is a main issue of the D-S approach
A very elegant and widely used solution is the single bit D-S ADC
In the single bit D-S ADC the internal Nyquist-rate ADC is a single bit quantizer, i.e., a comparator
ADC-1 bit
DAC-1 bit
bit-stream

## Slide 32
Single-bit D-S ADC
bit-stream
A 1-bit DAC is inherently linear
The filter operates also
decimation (decimator filter)
fS
fout = 2BS << fS

## Slide 33: H(z) implementation (Single ended)
Classical, "parasitic insensitive" Switched Capacitor Integrator
Note: electrical noise and distortion of the DT integrator are not shaped by the NTF: careful design of the integrator is required.

## Slide 34: Higher order D-S ADCs
Example: second-order ADC
Two integrators 2nd order
Advantage: 2.5 bits are gained doubling the OSR (instead of 1.5 bits). Same final resolution with a much smaller OSR
The 2nd order D-S ADC is a very popular converter for sensor interfaces.