## Slide 1: Mixed-Signal Design Flow and Example of SAR ADC Design

## Slide 2: Mixed Signal Design Flow
System on a chip with distribution of analog and digital units
Digital control
unit
Analog units
Traditional mixed circuit system
(e.g. interface for a MEMS sensor)
Both are examples of Mixed Signal integrated circuits

## Slide 3: Possible design flows
Analog centric (or analog on top): the analog and digital units are designed with their proper tools and integration is performed using the analog tool.
Digital centric (or digital on top): the analog and digital units are designed with their proper tools and integration is performed using the (highly automated) digital tool.

## Slide 4: Analog Design Flow and examples of CAD tools
Schematic design
Electrical simulation
Layout design
Verification:
DRC
LVS
PEX
Virtuoso schematic editor
Analog Design Environment (ADE)
Spectre electrical simulator
Virtuoso layout editor
Assura
Calibre
CADENCE
Mentor
Graphics
PEX: Parasitic extraction (for post-layout simulations)

## Slide 5: Digital Design Flow and CADENCE tools
High level description
(HDL - RTL)
Logic Simulation
Gate-Level Synthesis
Automatic Place and Route
CADENCE “Genus”
CADENCE “Innovus”
CADENCE “Xcelium”
Text Editor (e.g. "Gedit")

## Slide 6: Mixed Signal Design Flow: Analog Centric Approach
Analog Schematic design
Mixed Signal system level design
("pen-and-paper", SIMULINK-SIMSCAPE, VHDL-AMS, Verilog-A ...)
High level description
(HDL - RTL)
Logic Simulation
Gate-Level Synthesis
Analog cells
Digital cells
Mixed Signal Schematic design
Electrical simulation
Mixed Signal simulation
digital netlists
Automatic Place and Route
Analog Layout
(mainly manual)
Layout of the Mixed Signal Circuit
(mainly manual)
Verification
Digital layout

## Slide 7: An Example: Design of a SAR ADC
High-level behavioural description of the SAR algorithm (e.g. MATLAB)
Transistor-level design and simulations of the comparator and the CDAC
    HDL description and digital simulations of the SAR control logic
    Mixed-signal simulations of the whole ADC
    Layout of the analog blocks / synthesis and place-and-route of the SAR logic

## Slide 8: Analog Design and Simulations (Spectre simulator)

## Slide 9: VHDL description of the SAR digital control block
VHDL Code
Digital simulations (XCELIUM)

## Slide 10: Mixed-Signal Simulations (ams simulator)
Config view of the testbench
Connect rules

## Slide 11: Mixed-Signal Simulations

## Slide 12: Digital synthesis (GENUS)

## Slide 13: Digital synthesis (GENUS)
RTL (Register Transfer Level) Description
(GENUS input)
Gate Level Description
(GENUS output)

## Slide 14: Automatic layout generation (Automatic Place and Route, P&R)
Standard cells:
Velirog description
Layout (LEF or GDS)
Gate level netlist:
Verilog description
Delay file
Automatic P&R tool
Automation script file
Layout (GDS)
Post P&R netlist (verilog)
In the P&R operation, the tool change the original network adding components that allow respecting the timing requirements (e.g. clock buffers)
The LEF format is more versatile than GDS, since it allows easy partial description (e.g. creation of layout abstract views, where only the information for the P&R are included

## Slide 15: Automatic Place-and-Route (INNOVUS)
Empty spaces between cells are covered by "filler" elements in the final layout. Fillers includes n-wells and other layers that improve continuity between cells

## Slide 16: Layout imported in Virtuoso
Abstract view of D Flip-Flop