## Slide 1: DAS: Data Acquisition Systems
A DAS is required to allow an electronic system to get information on the external environment
The development of extremely miniaturized DASs capable of detecting a large number of different and inhomogeneous quantities is currently urged by emerging fields, such as robotics, security and health care.
This is giving a significant contribution to the request for analog and mixed signal integrated SoCs
The design of a DAS involve architectures and specifications that recur in many other branches of analog and mixed signal microelectronic circuits.

## Slide 2: The electronic system and the enviroment
Electronic system
Electronic system

## Slide 3: Main blocks of an Electronic System
DAS (full acquisition operations)

## Slide 4: Elements of a DAS: a two-channel case

## Slide 5: Signal classification on the basis of quantization
Magnitude
Time

## Slide 6: Errors on the ideal transfer function
Nominal (ideal) case:
Once V is known, X can be known exactly:
Real case:
is the output error defined as: Videal - V
In an acquisition system, the error is not known in a deterministic way.
To find the input quantity (X) we can only apply the inverse of the nominal transfer function to the real output quantity (we do not know the real t.f.):

## Slide 7: RTI (Referred to Input) Error
Property of Inverse Functions
RTI Error

## Slide 8: RTI Error: Equivalent block diagram for small errors
If the first order approximation that we have seen holds, it is possible to use the following equivalent representation:
Ideal block
Equivalent representation
of the real block
Verification:
Then, the equivalent block behaves as the real block
Xe is the value of the input quantity X that nulls the output
In this case, the dc value of Xe is the input offset

## Slide 9: System performance vs type of errors
Offset
Gain error
Non-linearity errors
Noise
Dynamic errors
(finite response time)
System
Static Accuracy
System Resolution
System response speed

## Slide 10: Non-linearity errors
Generally, the maximum non-linearity error in the whole range of the input quantity X is indicated in the specifications
If the non-linear curve is well reproducible, the non-linearity error can be compensated for by means of a non-linear estimator.
For random non-linearities, individual multi-point trimming is necessary.

## Slide 11: Dynamic errors
Settling time tset:
Time required to have the
output voltage stay close
to the final value within
a given relative error
Typical error specs:
1 % (low accuracy)
0.01 % (high accuracy)

## Slide 12: Linear time and slew-rate time
Linear-time only
(all stages behave linearly)
Slew-rate only
(most of the transition time at least one stage is saturated)

## Slide 13: Noise and resolution
Samples in this range are compatible
with both the X and X+DX input.
Therefore, it is not guaranteed that
a difference DX can be recognized
Minimum difference DX that can be reliably detected:

## Slide 14: Noise: peak-to-peak, rms and standard deviation
Interval | Total interval width (xnp-p) | Probability | 1 - probability
±s | 2 s | 0.683 (68.3 %) | 0.317
±2s | 4 s | 0.954 (95.4 %) | 0.046
±3s | 6 s | 0.997 (99.7 %) | 0.003
±4s | 8 s | 0.999936 (99.9936 %) | 6.410-5
Xn-pp
If we sample the noise
xn, then the standard
deviation of the samples is:
Cf= crest factor
Our choice:
For gaussian noise

## Slide 15: The Dynamic Range (DR)
Xmax
Xmin
Xmax-Xmin=XFS
Signal range
Full scale (excursion)
dx generally is the resolution

## Slide 16: DR and maximum number of significant levels
Xmax
Xmin
XFS
dx
Fist level that the system can distinguish from Xmin
Number of distinguishable levels = DR
The presence of noise cause a sort of quantization of the analog signal, at least in terms of usable levels