## Slide 1: Single-Ended operational amplifiers
Voltage amplifiers
Very large DC gain
Stability over a wide range of negative feedback conditions.
High input impedance on both inputs
Differential input
Typical requirements

## Slide 2: Typical op-amp-based negative feedback loop
This is a design specification

## Slide 3: Requirement on the output impedance
Zout should be low enough to guarantee that A is large enough to maintain the relative error below the maximum value allowed in all the expected load conditions

## Slide 4: Example ADA4628 (Analog Devices)
Passing from RL=10kW to RL=2 kW the amplifier looses around 8 dB
A1
A2
RL1
RL2

## Slide 5: Output stages - specifications
Source
Sink

## Slide 6
Single supply case
In a single supply voltage circuit, the load cannot be connected to gnd (or Vdd) if we want a to impose both positive and negative voltages across it.
To achieve this result, the load should be applied across the amplifier output port and a proper constant voltage, typically equal to Vdd/2.
This voltage must be generated by a proper cell, starting from Vdd.

## Slide 7: Oputput stage classes
By subtracting two unipolar
currents, we obtain a bi-directional output current
constant Idev2

## Slide 8: Common source output stages: class-A case
Margins to the rails are now only a VDSAT, which is much smaller than a VGS.
The common source output stage has a practically rail-to-rail output swing

## Slide 9: Other info on the class-A common source
The input voltage is invariant to the supply voltages when it is referred to Vss: the preceding stage should provide an output with the same property
VGSn
-VGSp
I0
I0
p-version:
(the input signal is invariant when referred to Vdd)
n-version
class-A
class-A

## Slide 10: Small signal properties of the class-A common source stage

## Slide 11: Class-AB common source: principle of operation
Mn turns off
Mp turns off
push
pull
operating
point
class-AB control
(driver)

## Slide 12: Class-AB common-source output stages: maximum output currents
Different topologies are available for the class-AB driver. They differ for the maximum VGS that can be delivered to Mp and Mn and for the minimum supply voltage
Driver
bp , bn

## Slide 13: Class-AB common-source output stages: quiescent current
The driver must be able to set the quiescent current with a good accuracy, since IQ sets the operating point power consumption and the small signal performances of the stage
Quiescent condition:

## Slide 14: Frequency response requirements: closed loop gain (bA)
180°
90°
fp
f2
fm
0°
|bA|
|b(0)A(0)|
bA
f0bA
f3
f4
The phase margin (fm) is the main stability indicator
The closed loop configuration is stable for fm>0
However, fm must be significantly greater than 0 to guarantee:
Stability even against all possible PVT variations
A step response with reduced ringing and overshoot
Typically, we require: fm>70°

## Slide 15: Amplifier gain and loop gain: role of the b factor
180°
90°
fp
fm
0°
|bA|
bA
f0bA
In this case, f0bA represents the -3dB upper band limit of the closed loop transfer function.
f0 is the unity gain frequency of the amplifier, equal to GBW (Gain-BandWidth for a dominant pole response
resistor-only or capacitor-only feedback networks
we consider the case:
(for d.c. stability)

## Slide 16
Amplifier gain and loop gain: role of the b factor
f0b A
2
f0b A
1
b1
b2
fm
Worst case for stability:
maximum |b|: b= -1
b= -1
f0bA gets lower: smaller bandwidth for the closed loop transfer function.
fm increases: greater stability
Smallest phase margin
Unity gain configuration

## Slide 17: Example of non-unity-gain stable op-amp
Stability for gains for non-inverting amplifiers config.
The advantage is a large GBW

## Slide 18: Single non-dominant pole case
s | 0.5 | 1 | 2 | 3 | 5
fm | 26.6° | 45° | 63.4° | 71.6° | 78.7°
s is an important design parameter
design for
unity-gain stable
op-amps
frequent choice

## Slide 19: Design specifications for the amplifier response speed
Gain-BandWidth product (GBW)
For a single pole frequency response:
In a closed loop configuration, the upper
band limit is given by:
For the non-inverting amplifier:
The same relationships are approximately valid for dominant-pole
frequency responses
Slew rate (sR): this is the maximum slope that can be obtained from the output voltage. The slew rate affects the behavior for large and fast input transients
1.
2.
3.

## Slide 20: A possible set of specification for design of a CMOS op-amp
dc gain A0
Speed: Gain-Band-Width product (GBW) and Slew rate (sR)
Closed loop stability: e.g. phase margin in unity gain configuration and with a maximum capacitive load (CL)
Input referred voltage noise: Thermal : SvT, Flicker: kF=fSvF(f)
Offset (Input offset voltage: Vio)
Static power consumption (Isupply, minimum Vdd)
Maximum output current IOP-max, ION-max
Ranges: Input common mode range (CMR), output swing.
CMRR, PSRR
Area

## Slide 21: Design of an anolog cell: phases
Specifications
Choice of the topology
Device sizing
Number of stages, use of cascodes, amplifier class ...
We have to set the values of the Degrees of Freedom (DOFs): W, L, Ibias, VGS-Vt ...

## Slide 22: Operational amplifiers: number of stages
In the op-amp design terminology, the number of stages refer only to gain stages.
A gain stage is formed by a V-to-I converter and a network I-to-I that brings the output current(s) of the V-to-I converter to the output port.
V-to-I : two inputs n=2
two outputs m=2
I-to-I
single output:
k=1
Example

## Slide 23: Single stage op-amps
With very large Rout values, gains up to 100 dB can be obtained (cascode and regulated cascode architectures)
In the case of resistive loads, the gain falls down to
In the case of no resistive load (only capacitive load, as in switched-cap. circuits:
Includes the load brought by the feedback network

## Slide 24: Single stage op-amps with resistive load
In single gain stages, Gm coincides with the transconductance (gm) of a single device or is a linear combination of device transconductances
Can be as low as several tens of kW
In most practical cases, loading a single stage op-amp with an even moderate resistive loads means reducing the gain to very small values, not suitable for op-amp closed loop applications.

## Slide 25: Two-stage op-amps
(40 dB - 100 dB)
The resistive loads affects only the gain of the second stage.
Even in the case that the gain of the second stage falls down to a few units, the total dc gain remains as large as to be suitable for most closed-loop configurations.
The second stage is the output stage and must be designed to provide the required current and voltage ranges to the load.

## Slide 26: Considerations on the op-amp number of stages
Single stage op-amps: they can be designed to provide enough gain for a large variety of applications only in the case that the load and the feedback networks are capacitive (switched capacitor circuits). Their advantage is their simple frequency compensation and their power efficiency. Their stability increases with large capacitive loads.
Two-stage amplifiers: they are the most popular options for general purpose op-amps since they are suitable for both capacitive and resistive loads and can be designed to provide very large dc gains. Their stability decreases with large capacitive loads.
Three-stage amplifiers: this option is necessary when two-stage amplifiers cannot provide enough gain. This is the case, for example of very low supply voltages that prevent the use of cascodes. The gain of two-stage amplifiers can be too low also in the case of very fast op-amps, where the gain of each single stage is limited by the necessity to use short-length MOSFETs. Three stage amplifiers requires complicated frequency compensation strategies, such as the nested-Miller compensation combined with feed-forward paths (multi-path architectures)