## Slide 1: Comparators
ideal response
Symbol

## Slide 2: Continuous-time vs dynamic comparator
Continuous-time comparator:
Higher power consumption
Hystheresis
Output always valid
Dynamic comparator (or latched comparator):
Lower power consumption
No hysteresis
Need a clock signal
Vi1
Vi2
Vout
Vi1
Vi2
Vout
Vout
Vi1
Vi2
clk
With hystheresis
Without hystheresis

## Slide 3: Comparators: amplifier-based implementations
An amplifier with very high gain can be used as a comparator. Op-amp topologies can be used with no need of frequency compensation
a region exists
where the logical
level is undefined
since the comparator is used in open loop configuration or positive feedback.
In several application this may lead to unwanted stable or metastable states.
For slow-varying signals, threshold crossing may be too noisy
Note:

## Slide 4: Regenerative comparators: hysteresis
Thanks to the hysteresis, the comparator produces a valid output level across the whole input range
The hysteresis introduces an uncertainty band that reduces the accuracy but helps rejecting noise when the input voltage is close to zero.
Op-amp based Smith trigger.
Oversized solution for integrated cells
Low impedance on the non-inverting input
Drawbacks
Possible regenerative comparator

## Slide 5: Commercial products
Programmable hysteresis from 0 to 160 mV DVh depnding on current on pin HYS
No built-in hysteresis. The
datasheet suggests Schmitt trigger configuration
HYS input
The digital output has its own Vdd

## Slide 6: Compact comparator cell for Systems on a Chip
Four-transistor hysteresis cell
Cross-coupled MOSFETs
Load MOSFET
b=bC
b=bL
Load MOSFET
b=bL
Currents I1 and I2 varies with the input signal in such a way that:

## Slide 7: Analysis of the four-transistor hysteresis cell: starting point
Let us start from: I2=0 (I1=I0)
since:
Considering M4:
Then it is M1 that carries all current I1:
(M3 is on)

## Slide 8: Analysis of the 4-transistor cell
Design condition:
we size bL in such a way that:
The reason will be clear later
V1, V2

## Slide 9: Increasing I2
As I2 increases, I1 decreases of the same amount, then V1 decreases:
V2 increases:
V1, V2

## Slide 10: Increasing I2
As I2 progressively increases, V2 increases. Until V2 remains below the threshold voltage Vt, M2 and M4 are off
V1, V2

## Slide 11: V2 reaches the threshold
Let us check whether M3 is now in saturation (was in triode region at the beginning)
For the design condition mentioned earlier
For V2=Vt, M2 and M4 are still off. Then:
Since M3 is in saturation:
M3 is in saturation

## Slide 12: V2 reaches the threshold
Case of interest:
for
For bC>bL, V2 reaches the threshold when I2 has overcome the middle of the allowed range [0, I0]

## Slide 13: Starting from the other extreme
Repeating the same procedure but starting from the rightmost point (I1=0, I2=I0) we obtain a symmetrical behavior with V1 and V2 swapped.

## Slide 14: Putting the two behaviors together:
In this region, there are two possible states, depending on which extreme we started from
This means that there is hysteresis
Now we have to investigate what happens when the lower voltage hits the Vt line

## Slide 15: Phenomena that happen when V2 overcome Vt
M2 and M4 turn on (while M1 and M3 are still on)
Let us focus on M2
1. As M2 turns on, it start stealing current from M1
3. VGS3 =V1, then ID3 reduces, increasing the current that flows into M4
2. V1 decreases:
4. V2 increases:
5. VGS2 =V2, then ID2 increases further
Positive feedback loop

## Slide 16: Positive feedback loop: small signal analysis
Each half circuit is equivalent to an amplifier
Small signal equivalent circuit
Due to the presence of the rd's, the magnitude of A is slightly less than

## Slide 17: Positive feedback loop: dc instability
A1
A2
Positive feedback
When V2 overcomes Vt, all MOSFETs are on:

## Slide 18: The effect of positive feedback
Therefore, a stable condition cannot exist if all MOSFETs are on.
(dc instability)
V1 and V2 cannot be greater than Vt at same time in a stable condition
Then, when M1 is on, M4 is off and vice versa
Important condition

## Slide 19: The "click"
Proceeding from the left, when V2 overcomes the Vt line, the positive feedback makes the voltage evolve autonomously.
The new stable solution is the one we already found proceeding back from the right
M1,M3: on M2,M4 off
M2,M4: on M1,M3 off

## Slide 20: The two stable characteristics
Only one solution exists
(stable)
Three solutions exist:
2 stable
1 unstable (all devices are on)

## Slide 21: Non regenerative case (no hysteresis)
In this case, the positive feedback is unable to cause a real abrupt transition
A hysteresis is not present

## Slide 22: A simple comparator based on the 4-transistor hysteresis cell
We start with a p-version of the hysteresis cell
Currents I1 and I2 are derived from the input voltage vid=vi2-vi1 by means of a differential pair
Only one at a time between V1 and V2 is greater than the p-mos threshold voltage.
If V1> |Vtp|, V2<|Vtp| MA, MB and Mo2 are on, while Mo1 is off:
If V2> |Vtp|, V1<|Vtp|, only Mo1 is on:

## Slide 23: Calculation of the comparator upper thresholds
Using a linear approximation of the differential pair:

## Slide 24: Calculation of the comparator upper thresholds
In quiescent conditions:
Dividing the upper equation by the lower one

## Slide 25: Complete characteristics of the comparator

## Slide 26: Minimum achievable hysteresis
Make VTE1 as small as possible
Make rH just slightly larger than 1
However, other requirements impose to make rH significantly larger than 1, because:
The calculated |bA|=(rH)2 is overestimated, since we have neglected the rd's
Process error can make rH <1 if the margin to 1 is too small
The transition is faster with larger |bA|
A typical robust choice:
DVH as small as 50 mV
To obtain a small hysteresis

## Slide 27: How to obtain a comparator with very low hysteresis
The simplest solution is using a pre-amplifier:
In discrete time systems the amplifier offset can be cancelled with CDS
gain G:
The hysteresis is divided by the preamplifier gain (G)

## Slide 28: A simple low-frequency VCO based on comparator hysteresis
This comparator is designed to have a large hysteresis
When Vout=0, the capacitor is charged by IP
When Vout=1, the capacitor is discharged by IN
VR+VH
VR+VL
VC

## Slide 29: Calculation of the oscillator frequency
rise time =
fall time =
period =

## Slide 30: Implementation with "current starved" inverter
IP
IN
If IP = IN = Itune:
The frequency is proportional to the tuning current (CCO)
Using a linear voltage to current converter it is possible to make Itune to be proportional to a voltage, transforming the CCO into a VCO

## Slide 31: A simple voltage-to-current converter
OTA
The OTA, and M1 form a two-stage op-amp with output on node H, stabilized by CC (Miller compensation). The op-amp is closed as a buffer:
This circuit can be used also to produce constant currents from a single reference voltage

## Slide 32: StrongARM Comparator
First proposed as Sense Amplifier for SRAM (used in StrongARM microprocessor)
No static power consumption
Rail-to-rail outputs
Compare Vid = Vin+-Vin- on the rising edge of the clock signal
Clocked differential pair
Latch
Reset switches

## Slide 33: Reset Phase
0
0
0
Nodes P,Q, Vout+, Vout- are connected to Vdd through S1-S4
The input pair is off
Each reset phase, the comparator loses ‘memory’ of the previous cycle  No hystheresis

## Slide 34: Amplification Phase
1
1
1
S1-S4 go off, M7 goes on
The input pair is on
I1, I2 start discharging the parasitic capacitances CP, CQ at nodes P,Q
Depending on Vid=Vin+-Vin- node P is discharged faster/slower than node Q
I1
I2

## Slide 35: Amplification Phase
ICM
1
1
1
small Vid
Pseudo-differential pair
(when clk=1, M7 connects node S to gnd)
S
I1
I2
S

## Slide 36: Amplification Phase
1
1
1
I1
I2
Reset (clk=0)
Amplification phase (clk=1)
Amplification lasts until P,Q reaches Vdd-Vthn
gain A
Vid = Vin+-Vin- > 0

## Slide 37: Regeneration phase (1/2)
1
1
1
When voltages at nodes P,Q go lower than Vdd-Vthn, M3-M4 turn on
Cross-coupled pair M3-M4 introduces regeneration
Nodes P,Q keep discharging and Vout+, Vout- start discharging differently according to the unbalance of P and Q

## Slide 38: Regeneration phase (1/2)
1
1
1
Reset (clk=0)
Regeneration 1 (clk=1)
Amplification (clk=1)
Vid = Vin+-Vin- > 0

## Slide 39: Regeneration phase (2/2)
1
1
1
When Vout+ or Vout- goes lower than Vdd-|Vthp|, one between M5 and M6 turns on
Positive feedback of latch M3-M6 brings quickly one output to Vdd and the other to ground (rail-to-rail outputs)

## Slide 40: Regeneration phase (2/2)
1
1
1
Reset (clk=0)
Regeneration 2 (clk=1)
Amplification (clk=1)
Regeneration 1 (clk=1)
No static power consumption (M3 cuts off the current path from Vdd to ground)
Vid = Vin+-Vin- > 0
Vout+= Vdd
Vout-= 0

## Slide 41: (Next) Reset Phase
0
0
0
Reset (clk=0)
Reset (clk=0)
Amplification (clk=1)
Regeneration (clk=1)
S1-S4 recharge node P,Q, Vout+, Vout- to Vdd
Need of a latch to store the result of the comparison during the reset phase