## Slide 1: Digital to Analog Converters
Input: digital code
Output: analog signal
A clock can be present for synchronization reasons or to avoid glitches during data update
Ideal function:
unipolar output range
bipolar output range
D can be signed
e.g, two's complement
VFS
VFS
n= nominal resolution (in number of bits)

## Slide 2: DAC applications
Digital to analog signal reconstruction: e.g. audio and video signals, actuator control (e.g. control of motors, solenoids, piezoactuators
Sensor excitation: generation of bias voltages, sinusoidal waveforms, etc)
Direct Digital Synthesis (DDS) of waveforms for telecommunications
Trimming of analog blocks (e.g. offset nulling)
Feedback components in ADCs

## Slide 3: DAC performance parameters
DAC errors
Offset
Gain
Non-linearity
INL
DNL
Quantization error
Noise
DAC speed: settling time, sample per seconds (sps),
Power consumption
Maximum output current
Energy of the glitches

## Slide 4: INL, DNL
Ideal case
(absence of non-linearity errors)
real case
|DNL|> 1 LSB: non-monotonicity
INL

## Slide 5: DAC Architectures
R-2-R ladder
Resistor String
Current Steering
Switched Capacitors
Pros
Cons
Reduced number of
resistor of similar value
Potentially non-monotonic
Suffer from the on-resistance of the switches
Very large number of resistors
Guaranteed monotonic
Low power consumption
Very fast. No need for resistors. Can be designed to be always monotonic
Current output. Flicker Noise
Optimal power vs speed trade-off
The output may be not available in the whole clock cycle. Large glitches

## Slide 6: DAC resistor string
For any value of code D, only one switch at a time is on, selecting one of the 2n voltage levels produced by the resistive divider
If code D turns on a certain switch, code D+1 turns on the switch placed in position up, then the output voltage can only grow
The monotonicity is guaranteed
Digital decoder

## Slide 7: INL in a resistor string: a simple estimate
We consider a code that, in the ideal case, select the mid voltage:
Ideally
In a real case:

## Slide 8: INL and resistor matching
In an n-bit DAC, to have an |INL|<1 LSB, the relative matching errors should be:
Example: 12 bit DAC:
Example: 16 bit DAC:
Feasible, with large area occupation
Unfeasible. Requires complicated post-production trimming

## Slide 9: Current Steering DAC
It can be made monotonic-guaranteed by driving the 2n mosfets of the array with thermometric coding
It suffers from the same INL problem of the resistor string DAC
The current of mosfets that are not routed to the output (their bit is 0), is not interrupted but is routed to a constant voltage (Vk) to keep the mosfet ready to be connected to the output in a short time
I0
2I0

## Slide 10: Thermometric coding
2n devices
(always in parallel)
2n devices
thermometric coding
D
The first D lines are
set to 1
D devices
of the matrix are routed to the output
If D is incremented by one, one more device is routed to the output: Iout increases. Monotonicity is guaranteed
randomly placed
into the matrix
2n identical current sources I=I0

## Slide 11: Capacitive DAC
Capacitor bank has better matching properties than resistor string
Low-power solution (no static consumption in the capacitor bank)
Output not always valid
Troubles with C-2C solutions due to parasitic capacitance of the bottom plate

## Slide 12: DAC Comparison
 | Type | Accuracy | Current consumption | Speed
Voltage | Resistor string, R-2R | Up to 12 bit | 1 mA – 1 mA | Up to 100 MS/s (limited by buffer)
Current | Current steering, I-2I | Up to 10 bit | 10 mA – 30 mA | Up to 10 GS/s
Charge | Capacitor bank | Up to 14 bit | 1 nA – 10 mA | Up to 100 MS/s (limited by buffer)

## Slide 13: Analog to Digital Converters
Sampling:
Nyquist-Shannon sampling theorem
Aliasing
Quantization:
Quantization noise
Time-continuous Infinite levels
Time-discrete Finite number of levels
Analog-to-Digital converter

## Slide 14: ADC applications
Measurements and data acquisition
Industrial (control systems, PLCs, …)
Sensor integration (robotics, IoT, …)
Commercial electronics (mobile phones, video and audio devices, microcontrollers …)
High-speed communications (data link, IF conversion…)

## Slide 15: Analog to Digital Converters (ADCs)
The characteristic of an n-bit ADC
with no offset, gain, and non-linearity
errors (only quantization errors)
vin-dig must be the best approximation of vin, given the number of bit of D
It is useful to refer to the
equivalent voltage of D
LSB

## Slide 16: ADCs - Main Performances
Speed Resolution Power consumption
Signal Bandwidth
Affected by:
quantization noise
electrical noise
harmonic distortion
Depending on the ADC architecture:
Pipeline
SAR
Flash
Thermal noise limited
Effective Number of Bits
Signal to Noise And Distortion ratio
Sampling frequency
N: ADC resolution
Depending on fs:
Nyquist Rate ADCs
Oversampling ADCs

## Slide 17: Nyquist-Rate vs. Oversampling ADCs
Nyquist Rate ADC:
The output code depends only on the last conversion. Previous conversions do not affect the present code
Oversampling ADC:
The output code depends also on the previous history of sampled data.

## Slide 18: ADCs – Static Parameters
Offset error: difference between the actual ADC characteristic and the perfect ADC characteristic, evaluated at the zero transition
http://ww1.microchip.com/downloads/en/appnotes/atmel-8456-8-and-32-bit-avr-microcontrollers-avr127-understanding-adc-parameters_application-note.pdf
Gain error: difference between the last step midpoint of the actual ADC and the last step midpoint of the ideal ADC, after the compensation of the offset error

## Slide 19: ADCs – Static Parameters
DNL error: difference in the step width between the actual characteristic and the ideal one
http://ww1.microchip.com/downloads/en/appnotes/atmel-8456-8-and-32-bit-avr-microcontrollers-avr127-understanding-adc-parameters_application-note.pdf
INL error: vertical difference between the actual input-output characteristic and the ideal one, after the compensation of the offset and gain error

## Slide 20: ADCs – Static Parameters

## Slide 21: ADCs – Dynamic Parameters
SINAD=46.26 dB
THD=-58.67 dB
SINAD = 80.2 dB
SNR = 91.77 dB
Bs = 490 Hz (=fs/2048)
SNR=46.52 dB
THD = -80.51 dB
Bs = 250 MHz (=fs/2)
Nyquist-Rate ADC
Oversampling ADC
(or SNDR)
fs= 500 MHz
fs= 1 MHz

## Slide 22: Quantization noise in the frequency domain
Vin is a dc signal
Since the ADC samples the input data, the output frequency domain is
[-fs/2,+fs/2]
The vnq spectrum
is a Dirac delta
Vin is fast-varying signal
of magnitude >> LSB
Two extreme cases
uniform distribution

## Slide 23: The uniform power spectral density (PSD) model for the quantization noise
This model is very useful and simple but should be applied with much care.
In real cases, the quantization noise depends on the input signal, and so does its spectrum.
The uniform spectral density model is acceptable when the input signal has magnitude and/or frequency such that the output levels are changed in a fast and almost random way.
This happens when the average time spent by the signal on a single level is short (of the order of the sampling time).

## Slide 24: Signal to Noise Ratio and resolution
Input range of the ADC
Considering only quantization noise:

## Slide 25: Effective Number Of Bits (ENOB)
Distortion and SFDR (spurious free dynamic range)
PD=total power of the harmonics
Quantization and electrical noise
Also indicated with SNDR

## Slide 26: ADCs – Figure of Merits
Walden FoM:
Schreier FoM:
[dB]
[J/conv]

## Slide 27: Comparison of different topologies
Mismatch limit of passive component
https://web.stanford.edu/~murmann/adcsurvey.html

## Slide 28: Nyquist rate ADCs
Direct conversion:
  Flash converters
Counting and Integrating ADCs:
  Counting converters
  Dual-slope
Binary-Search Algorithm based:
  Successive approximation converters (SAR)
  Pipelined converters
N-bit ADC
1 cycle of comparison (fast but with low resolution)
2N cycles of comparison
(simple/accurate but slow)
N cycles of comparison
(good trade-off speed/resolution)

## Slide 29: A very common SAR ADC: the charge-redistribution ADC
preamplified comparator
capacitive DAC

## Slide 30: Reset phase
All capacitors are in parallel, with one terminal connected to the input voltage Vin.
The op-amp is closed
in unity gain
-vn
analog input signal Vin  0

## Slide 31: Sampling phase
The op-amp is placed in open loop configuration and the bottom plates of all capacitors are connected to gnd.
The voltage of the top plates (Vtop) is free to evolve (it is floating, no current comes from the OP to Vtop)

## Slide 32: Top voltage in the sampling phase
Reset
Sampling
The voltage on Ctot
does not change

## Slide 33: SAR phases
Sequence: SARn-1 ...... SAR0
Phase SARk begins by connecting the bottom plate of Ck to the reference voltage VREF through switch Sk
This causes a jump in voltage Vtop.
Bit k-th is the output of the composite comparator (Vb) at the end of phase SARk
If bk =0 Sk comes back to gnd, else it remains at VREF
composite comparator
Phase SARk

## Slide 34: Composite comparator
The gain of OA is so large that the offset and hysteresis of CMP has negligible impact on the composite comparator characteristics.
Vb
Vtop
ViA
VoA=A(ViA-vn)

## Slide 35: Phase SARk: calculation of the Vtop jump
All-capacitor network:
equivalent circuit for variations. Capacitors can be replaced by a resistors of value 1/C
DVtop at phase SARk

## Slide 36: Phase SARn-1
Decision for bit bn-1 (taken at time tn-1 = end of phase SARn-1)
Vb
from sampling phase

## Slide 37
Phase SARn-1
Subtraction of two noise samples taken at different times: constant and correlated components are rejected (CDS).
Neglecting noise / offset components, the condition becomes:
bn-1=1
bn-1=0
This is in conformity with the successive approximation algorithm
possible values
of Vin(ts) and resulting
value of bn-1

## Slide 38: Phase SARn-2
Switch Sn-1 goes back to gnd if bn-1=0
Otherwise, it remains to VREF
If Sn-1 comes back to gnd, it subtracts DVn-1 from Vtop
Decision : bit bn-2 =1 if:
Vb

## Slide 39: Decision for bn-2
if bn-1=1 Vtst(n-2)=
bn-2=1
bn-2=0
bn-2=1
bn-2=0
if bn-1=0 Vtst(n-2)=
Vtst(n-2)

## Slide 40: Generalization
At k-th step (phase SARk) , bit bk is determined from the comparison of Vin( ts ) with:
Increments applied in previous phases and
maintained only if the corresponding bits are 1
At any step the increment is halved
At the last phase, SAR0, the LSB (b0) is determined and the conversion is complete. The bits determined in the successive phases are stored inside a register of the control logic and can be retrieved at the end of conversion.

## Slide 41: Examples of conversion cycle
bn-1 = 1
bn-2 = 0