## Slide 1: Typical structure of a digital chip
Pad Frame
I/O circuits
Core (o internal) logic

## Slide 2: Recall to the letch-up phenomenon
Rsub
Rsub
Rwell
Rwell
In order to reduce the risk of latch-up, it is important to reduce the resistances between the parasitic BJT bases and the substrate and well tap

## Slide 3: Latch-up layout rules: core logic
Every part of a p-active area in an n-well must "see" at least one well-tap with a maximum distance R
Every part of an n-active area in the substrate (p-well) must "see" at least one substrate-tap with a maximum distance R

## Slide 4: I/O circuits: over-voltage risk
possible load / transmission
line equivalent circuit
I/O pad
Vdd
gnd
Vout
Ideal case
Real case
In I/O circuits, the output termination can exceed the Vdd or
gnd rails. This introduces additional risk of latch-up

## Slide 5: Injection of minority carriers
Well: bases of the pnp BJT (collector of npn BJT)
Substrate: bases of the npn BJT (collector of pnp BJT)
when Vout exceeds Vdd,
this diode is turned on
when Vout drops below gnd,
this diode is turned on

## Slide 6: Injection of minority carriers
Hole injection into the n-well
when Vout > Vdd
Electron injection into the substrate when Vout< 0
Injection of minority charge carriers into the parasitic BJTs bases may trigger the latch-up phenomenon

## Slide 7: I/O devices: Guard Rings
n+ (well tap)
p+ (sub. tap)
n-well
p+ (sub-tap)
vdd
gnd
vdd
gnd
gnd
vdd
I/O devices
n-well
p+ (sub. tap)
Guard rings are placed around the I/O devices in order to:
Reduce the resistance between drain/body diffusions to gnd (nMOS) or Vdd (pMOS)
Collect most of the minority carriers injected by one device before they reach neighboring devices
These guard rings further reduce the
effects of the I/O devices on the core
logic
I/O circuits require additional protection against latch-up

## Slide 8: Analog and mixed signal chips
For the analog section of a System on a Chip, it is not convenient or even impossible to divide the circuit into a core section and an I/O section.
However, the same rules illustrated for digital chips apply to the output devices of the analog cells (for example, operational amplifiers), which are connected to output pads. High density of substrate / well contacts, guard-rings and particular layout configurations are common practice for the output devices of analog circuits.