## Slide 1: Increasing the gain of the simple differential amplifier with mirror load
The gain is not improved
Trying to increase gm1 by increasing ID1 produces a corresponding decrease of Rout.
For many applications, the gain of the simple CMOS differential is not sufficient
We can increase Rout by reducing the lambdas, but this means very long MOSFETs, resulting in large area occupation and parasitic capacitances.
We need to increase Rout in a different way!

## Slide 2: Fist step: replace the simple current mirror with a cascode mirror
This increases Rup …
… but Rdown is not changed
Rout passes from rd/2 to rd and the gain is only doubled

## Slide 3: Second step: add a common-gate also to the differential pair: The cascode differential amplifier
We add a differential common gate stage (M3,M4) to the differential pair: forming a differential cascode stage
2rd2

## Slide 4: Cascode differential amplifier: Rout
Also in this amplifier, the current into Rdown is brought back to the output
The current into Rdown is doubled

## Slide 5
Cascode differential amplifier
If all devices have the same rd and gm:
Cascode
Differential
stage
I-to-I network
V-to-I network

## Slide 6: CMOS cascode amplifier: output range
Upper limit
|Vout-mirror |
As Vout gets higher than max(Vout), Rup decreases making the gain decrease

## Slide 7
CMOS cascode amplifier: output range
Lower limit
For an approximation of min(Vout) in weak inversion just add 100 mV
In strong inversion:

## Slide 8: Input common mode range
VC
VC

## Slide 9: Cascode amplifier: all ranges
Vk2 determines a trade-off between the input common mode range and the output swing
Vout
Vdd
Vss
max(Vout)=Vdd-|VMIN-cascode|
max(ViC)=Vk2 -VDSAT1
Vdd
Vss
Vk2
min(Vout)=Vk2 -VGS4+VDSAT4
min(ViC)=VSS +VMIN-tail+VGS1
Vic
Vout

## Slide 10: Adaptive Vk2

## Slide 11: Adaptive Vk2
The adaptive Vk2 does not solve the problem that, as ViC increases, the output swing gets smaller. The advantage is that the amplifier is more flexible and no trade-off on VK2 should be made in the design phase.
“Telescopic” amplifier
Same as in the case of a general cascode structure

## Slide 12: Removing the interaction between input and output range: The Folded Cascode
out
Folding
According to the folding mechanism, the signal (variations) initially travels from one rail to the other and then invert direction and goes back to the initial rail
Let us introduce a type-p common gate stage
Use an n-type current mirror to subtract the currents
Two current sources are required to bias the common source and common gate

## Slide 13: Folded cascode amplifier: device currents
Condition:

## Slide 14: Folded cascode: setting the correct I1 value
With a large input signal (|Vid|> VDMAX):
Quiescent point:

## Slide 15: Folded cascode: differential mode gain
M1
M2
M6
M7
M8
M9
M10
M11
Vk2
vp
ros
rd3
rd4
ip
Using a Norton equivalent circuit of the output port

## Slide 16: Folded cascode: output resistance (2)
vp2
M1
M2
M6
M7
M8
M9
M10
M11
Vk2
ros
rd3
rd4
ip2
vp1
ip1

## Slide 17: Folded cascode: output resistance (2)
RS7
2rd1
Rup
ros

## Slide 18: Folded cascode: output resistance (2)
Rdw
ros

## Slide 19: Folded cascode: output resistance (3)
If rd2=rd3=rd7=rd9=rd11 =rd
gm7=gm9=gm

## Slide 20: Folded cascode: differential mode gain
If rd2=rd3=rd7=rd9=rd11 =rd
gm7=gm9= gm1= gm
Compare with the “Telescopic” amplifier
… and with the simple amplifier with mirror load (non-cascode)

## Slide 21: Simple method to find if a terminal is inverting / non-inverting
Signal paths:
From G to D: inversion
From G to S: no inversion
From S to D: no inversion

## Slide 22: Ac, CMRR
vC
vC
It is possible to demonstrate that, for VD=0, voltage and currents in the amplifiers are symmetrical.
Then:
ros

## Slide 23: Folded cascode: output range
Vout-mirror
In strong inversion:
Lower limit
Upper limit

## Slide 24: Maximum Vk2
|VDS3|
Vk2 sets the voltage of M1-M3 and M2-M4 drains

## Slide 25: Input common mode range
M1 (M2) has the drain at a fixed voltage. If the gate voltage increases, M1 (M2) will eventually leave saturation
Minimum ViC: M1,M2 pair
Maximum ViC:

## Slide 26: The folded cascode as a single stage amplifier
I-to-I network (KI=1)
V-to-I network
(Gm1=gm1)

## Slide 27: Folded cascode: summary of properties
DC Gain: Slightly smaller than the telescopic amplifier (non-folded cascode) gain. May reach several thousands or even 104 (80 dB) with long mosfets. Larger than the gain of the cascade of two common source stages.
Ranges: In the the Folded cascode, the output range is not affected by the input common mode voltage. As a result, the input CM range and output range are much wider than in the telescopic amplifier.
Output range:
(swing)
Input CM range:
Approaches the Vdd rail
May approach the Vss rail if a wide swing mirror is used
Goes over the Vdd rail
The only critical limit

## Slide 28: The only true advantage of the telescopic amplifier
CS
CG
Current consumption (Isupply)
CS
CG
Current re-use
common-source
supply current
common-gate
supply current
The telescopic amplifier needs less current

## Slide 29
Example: Analog Devices ADA4530
Folded cascode with wide-swing current mirror (gate bias voltages are not indicated for simplicity)

## Slide 30: Example of BJT Op-Amp with a single folded cascode gain stage
Emitter-degenerated input pair
(improves input differential range, with benefits in terms of Slew-Rate
Wilson current mirror with emitter degeneration.
Class-AB emitter follower (gain  1)