## Slide 1: Output stages
Output stages for operational amplifier
Gain reduction due to loading:
output attenuation aout
The only requirement on Rout is that A is still >> 1 even with the lowest value of RL
A particularly low Rout is not a necessary specification for op-amps

## Slide 2
Example of commercial op-amp with high output resistance
RL=500 kW
RL=10 kW

## Slide 3: Specifications for an output stage
Source
Sink
Currents (sink and source)
Voltages (swing)
Vout-max
Vout-min
The output swing depends on the currents the stage has to feed to the load

## Slide 4: Examples
OPA 377 (Analog Devices)
Linear Tech.

## Slide 5: Output stage classes
By subtracting two unipolar
currents, we obtain a bi-directional output current
constant Idev2
Simple model of an output stage

## Slide 6: Typical class A case: low power efficiency
In a class-A stage, one of the two output devices operates at constant current
The maximum symmetrical current coincides with Idev 2, which is a constant bias current.
Therefore, the maximum (symmetrical) output current is smaller than the quiescent current absorption.

## Slide 7: Class – A source followers
The large margin to to Vdd makes it not suitable for rail-to-rail output stages (practically mandatory in modern, low voltrage applications)
The n-MOS source follower can be used as a negative voltage-shifter
Because the circuit that produces Vin (driver) uses the same Vdd

## Slide 8: P-type Source follower
Margin to Vss
(too large for typical supply voltages used in modern CMOS processes)
The p-MOS source follower can be used as a positive voltage shifter.

## Slide 9: Class-A source followers: output current limits
The positive output current (IOP) is limited only by the MOSFET size
The negative output current (ION) is limited by I0, which is the quiescent supply current
n source follower
p source follower
opposite condition: it is the positive current to be limited by I0,

## Slide 10: Source followers: summary
N-type: Large margin with respect to Vdd
Sink current limited by bias current
P-type: Large margin with respect to Vss
Source current limited by bias current
Class AB source followers (push-pull stages) remove the limitation on the output current but impose a large margin with respect to both rails (Vdd, Vss)
Source followers are avoided in amplifiers designed for low supply voltages and for large output swing

## Slide 11: Common source output stages: class-A case
P. Bruschi – Microelectronic System Design
11
Margins to the rails are now only a VDSAT, which is much smaller than a VGS.
The common source output stage has a practically rail-to-rail output swing

## Slide 12: Small signal properties of the class-A common source stage
P. Bruschi – Microelectronic System Design
12
The unipolar common source is a gain stage (inverting) that can be used also as output stage

## Slide 13: Class-A common source: maximum output current
The input voltage is invariant to the supply voltages when it is referred to Vss: the preceding stage should provide an output with the same property
VGSn
-VGSp
I0
I0
p-version:
(the input signal is invariant when referred to Vdd)
n-version
class-A
class-A

## Slide 14: Class-AB common source: principle of operation
14
Mn turns off
Mp turns off
push
pull
operating
point
class-AB control
(driver)

## Slide 15: Class-AB common-source output stages: maximum output currents
15
Different topologies are available for the class-AB driver. They differ for the maximum VGS that can be delivered to Mp and Mn and for the minimum supply voltage
Driver
bp , bn

## Slide 16: Class-AB common-source output stages: equivalent voltage source
Vdd
Vss
Vout
Vgp
Mn
Mp
Vgn
VB
This is equivalent to have a voltage source (battery) across the two gates.
For small signals:

## Slide 17: Class-AB common-source output stages: small signal gain
vgn and vgp must have the same sign to produce in-phase effects on vout
For:

## Slide 18
Two-stage operational amplifiers: examples

## Slide 19: Two-stage operational amplifier with class-AB output stage
Vgn
Vgp