## Slide 1: Planar n-MOSFET cross-section and layout
The designer introduces ideal geometrical values (L,W ..), while the electrical properties are determined by "effective" values:

## Slide 2: Simplified layout and cross-section ("designer view")

## Slide 3: MOSFET models
Models for accurate electrical simulations: BSIM models (Berkeley Short-channel IGFET Model), EKV (Enz, Krummenacher, Vittoz) ...
Models for "hand calculations": square law (strong inversion) exponential laws (weak inversion)
It is of primary importance to be able to manually perform first order device sizing and first order performance estimation.
Only very simple and intuitive model enable the designer to create cells that need only a final refinement and verification in the simulation phase
The simulator is useless if we do not know how to produce a circuit on scrap-paper. The simulator obeys to the law: garbage in – garbage out

## Slide 4: EKV Model
* “An analytical MOS transistor model valid in all regions of operation and dedicated to low-voltage and low-current applications” – Enz, C. C., Krummenacher, F., Vittoz, E. A. - 1995
Fully-analytical, physics based model focused on weak-inversion behaviour
All terminal voltages are referred to the bulk terminal voltage, exploiting the simmetry of the source and drain terminals
Supported by Spice simulators, requires only 18 DC parameters
Drawback: simplified expressions of short channel effects

## Slide 5: BSIM Models
Highly empirical models (BSIM3 DC models requires almost 100 parameters)
Standards for integrated circuit design, with accurate modeling of transistor’s behaviour (e.g.: channel length modulation and DIBL)
Currently maintained models: BSIM3 (until sub-100 nm nodes), BISM4 (from 0.13 um to 20 nm), BSIM-SOI, BSIM-CMG (Common Multi-Gate, for FinFET and 3-D transistors)…
* “BSIM: Berkeley Short-Channel IGFET Model for MOS transistor” – B.J. Sheu et al. - 1987

## Slide 6: MOSFET models: The n-MOSFET
From this point on, we will consider the behavior of the n-MOSFET, unless otherwise specified. In the end, we will suggest a simple way to transfer all the considerations made for the n-MOSFET to the p-MOSFET
In integrated circuits, the MOSFET is a four terminal devices: Drain, Source, Gate and Body. In discrete MOSFETs, the body is generally connected to the source internally.
S
G
B
D

## Slide 7: Large signal MOSFET model (n-MOSFET)
S
G
B
D
In DC, we will always assume:

## Slide 8: Source and Drain Symmetry (1)
The planar MOSFET is symmetric so that drain and source can be swapped with no consequences in the electrical characteristics.
Equations that use the source as a reference terminal for all relevant voltages can be applied only after finding which terminal is actually playing the role of the source.
In an n-MOSFET, the effective source is the terminal that has the lower voltage; the other one of the two, is the actual drain
In a p-MOSFET, the effective source is the terminal that has the higher voltage; the other one of the two, is the actual drain

## Slide 9: Source and Drain Symmetry (2)
With this definition, it is clear that in transient situations, the effective drain and source can swap, depending on the voltage assumed by the terminals.
In a schematic editor it is necessary to indicate which terminal is the drain and the source. These "conventional" terminals are used to mark all voltages for printing and plotting purposes. This choice do not affect the circuit behavior during the simulations.
Example

## Slide 10: Source and Drain Symmetry (3)
If the circuit has a clear static operating point (like most analog circuits), it is convenient to mark as source the terminal that in the operating point is actually working as the source. This will facilitate reading device voltages produced as textual or graphical outputs by the simulator.
Models like the EKV use the body as the reference for all voltages. In this way drain and sources are perfectly symmetrical also in the equations and there is no need to decide which one is actually working as the source.
Maintaining the distinction between source and drain is more intuitive and most models oriented to hand calculations are actually based on this choice.

## Slide 11: The IDS model: control voltages
primary effect
it is the wanted current control
secondary effects:
generally they are unwanted

## Slide 12: VGS, VBS and "overdrive voltage"
The voltage that really affects the current is the "useful" part of the VGS,
often called "overdrive voltage".
Body effect
g: body effect coefficient fS: surface potential

## Slide 13: More on body effect: example

## Slide 14: RSCE and RNCE
Reverse Narrow Channel Effect (RNCE): increasing of Vth with increasing channel width W
Reverse Short Channel Effect (RSCE): reduction of Vth with increasing channel length L

## Slide 15: IDS : operating zones on the basis of VDS
VDSAT
triode
saturation
VDSAT is a function of VGS-Vt
Triode: IDS is strongly dependent on VDS
Saturation: IDS shows a weak and almost linear dependence on VDS

## Slide 16: Operating zones on the basis of VGS-Vt
VDS>VDSAT
off
on
VGS<Vt
VGS>Vt
A rough picture:

## Slide 17: A more gradual picture: same characteristic with logarithmic y-axis
Vt+4VT
VT=kT/q
weak inversion
(sub-threshold)
stong
inversion
moderate inversion

## Slide 18: IDS: operating zones
 | VGS -Vt ≤ 0 | 0 ≤ VGS -Vt ≤ 4VT | VGS -Vt ≥ 4VT
VDS ≤ VDSAT | Triode – Weak Inversion | Triode – Moderate Inversion | Triode – Strong Inversion
VDS ≥ VDSAT | Saturation – Weak Inversion | Saturation – Moderate Inversion | Saturation – Strong Inversion

## Slide 19: VGS-Vt>4VT Strong inversion: IDS equations
VDS ≤ VDSAT (Triode)
VDS ≥ VDSAT (Saturation)
In some textbooks this term is omitted (VDSAT) for simplicity, but this cause a discontinuity between the triode and saturation region

## Slide 20: EKV model in weak inversion
m: subthreshold slope factor
k: channel divider
EKV model for w.i.

## Slide 21: EKV model in weak inversion
m: subthreshold slope factor
k: channel divider
EKV model for w.i.
Body effect
Body effect coefficient

## Slide 22: Drain-Induced Barrier Lowering (DIBL) Effect
Short-channel effect that reflects into a reduction of the threshold voltage with a larger drain-source voltage, due to the drain-body depletion region
Lower DIBL effect with longer channel length L
Halo implants reduce DIBL effects (but cause RSCE)

## Slide 23: DIBL Effect
lDIBL: DIBL coefficient (inversely proportional to L), typically 0.01 – 0.1
DIBL effect

## Slide 24
IDS simplified model in weak inversion
VDS < VDSAT ≈ 4VT
Triode region
VDS > VDSAT ≈ 4VT
Saturation region
Weak Inversion
(VGS < Vt)

## Slide 25
IDS operating regions
 | Weak Inversion (VGS -Vt ≤ 0) | Moderate Inversion (0 ≤ VGS -Vt ≤ 4VT) | Strong Inversion (VGS -Vt ≥ 4VT)
Current in Triode Region VDS ≤ VDSAT |  |  | 
Current in Saturation Region VDS ≥ VDSAT |  |  | 
Saturation Voltage VDSAT |  |  | 

## Slide 26: Temperature effects on MOSFET characteristics
Vt dominates
(ID increases with T)
b dominates
(ID decreases with T)
ZTC point

## Slide 27: MOSFET Leakage current
I1: pn Junction Reverse-Bias Current
I2: Subthreshold Leakage
I3: Tunneling into and through Gate Oxide
I4: Injection of Hot Carriers from Substrate to Gate Oxide
I5: Gate-Induced Drain Leakage
I6: Punchthrough
* Leakage Current Mechanisms and Leakage Reduction Techniques in Deep-Submicrometer CMOS Circuits – K.Roy et al. - 2003

## Slide 28: MOSFET Leakage current
Example: Sample-and-Hold
Vctrl = 0 V  S is open
Vctrl = 0 V  M is off (weak inversion)

## Slide 29: MOSFET Leakage current
L=180 nm, VGS = 0 V, VDS = 1.8 V

## Slide 30: MOSFET Small Signal model
effect of vbs
cgs, cgd, cgb, cbd, cbs : small signal capacitances
Let's start from the dc model (capacitances are removed)

## Slide 31: MOSFET small signal model: dc limit
small signal

## Slide 32: Body transconductance: gmb
gm
gmb
1
let's recall the gm definition

## Slide 33: Body transconductance: gmb
m ~ 1.2 gmb ~ 0.2gm
Example from simulation

## Slide 34: gm, gd in strong inversion
Triode region
gm
gd

## Slide 35: gm, gd in strong inversion
Saturation region
neglecting the dependence of VDSAT on VGS

## Slide 36: gm, gd in strong inversion

## Slide 37: gm, gd in strong inversion
Important parameter
for MOSFETs:
MOSFET
Self-gain

## Slide 38: Transconductance models in saturation
In strong Inversion:
!!!
only a few %
acceptable approximation, because we are studying gm, i.e the effect of VGS

## Slide 39: gm,gd in weak inversion
Exact result
Exact result

## Slide 40: gm,gd in weak inversion
VDSAT
ID
VD
VDSAT
gm
gd
VD
gm
gd
In saturation:
In triode:

## Slide 41
gm, gd everywhere: simulations
Strong inversion
VGS-Vt=0
VGS-Vt= -100 mV
VGS-Vt= 200 mV

## Slide 42
 | Triode (VDS ≤ VDSAT = VGS-Vt) | Saturation (VDS ≥ VDSAT = VGS-VT)
gm |  | 
gd |  | 
gm, gd everywhere
Strong inversion

## Slide 43
gm, gd everywhere
Weak inversion
 | Triode (VDS ≤ VDSAT = 4VT) | Saturation (VDS ≥ VDSAT = 4VT)
gm |  | 
gd |  | 

## Slide 44
gm/gd everywhere
 | Strong Inversion | Weak Inversion
gm/gd |  | 
Saturation (VDS > VDSAT)

## Slide 45: Unified model for transconductance in saturation
Strong Inversion
Weak Inversion
BJT
with
Strong inversion
Weak inversion
BJT
Definition of VTE
Important parameter for analog circuit design

## Slide 46: Effective Thermal Voltage: VTE
The smaller the VTE, the higher the gm that can be obtained with a given ID

## Slide 47: MOSFET Capacitance Model: gate related capacitances
estrinsic cap.
intrinsic cap..

## Slide 48: Estrinsic Capacitances
Localization of extrinsic
capacitances: along the
borders of the gate
L
W
D
S
G

## Slide 49: Intrinsic capacitances: The Meyer Model
 | Off (VGS << Vt) | Triode | Saturation
 | Off (VGS << Vt) | Triode | Saturation
Series of the oxide and depletion layer capacitances. Can be approximated with only the oxide cap COXWL

## Slide 50: Charge oriented models (Dutton and Ward model)
Limits of the Meyer Model:
Does not guarantee charge conservation
Capacitances are reciprocal
Important errors in circuits
using MOSFETs as
switches.
VB=0
VD
VS
VG
QG
QD
QS
Array of 9 capacitances
Cij are < 0 for i≠j (trans-capacitances)
Cij are > 0 for i=j (self capacitances)
Generally: Cij ≠ Cji
Dutt and Ward model

## Slide 51: Junction capacitances
W
D
S
G
LC

## Slide 52: MOSFET Transition Frequency
Ex.: S.I., Saturation

## Slide 53: MOSFET Transition Frequency in W.I, M.I. and S.I.
W.I.
S.I.
M.I.
UMC 180 nm CMOS Process

## Slide 54: MOSFET Transition Frequency in W.I, M.I. and S.I.
W.I.
S.I.
M.I.
UMC 180 nm CMOS Process

## Slide 55: MOSFET Transition Frequency in W.I, M.I. and S.I.
UMC 180 nm CMOS Process

## Slide 56: VTE and gm/ID in W.I, M.I. and S.I.
UMC 180 nm CMOS Process
27.4 mV
S.I.
W.I.
W.I.
S.I.
M.I.

## Slide 57: VTE and gm/ID in W.I, M.I. and S.I.
UMC 180 nm CMOS Process
S.I.
W.I.
W.I.
S.I.
M.I.

## Slide 58: VTE and gm/ID in W.I, M.I. and S.I.
UMC 180 nm CMOS Process
S.I.
W.I.

## Slide 59: gm/gd in W.I, M.I. and S.I.
S.I.
W.I.
UMC 180 nm CMOS Process
W.I.
S.I.
M.I.

## Slide 60: gm/gd in W.I, M.I. and S.I.
S.I.
W.I.
UMC 180 nm CMOS Process
W.I.
S.I.
M.I.

## Slide 61: gm/gd in W.I, M.I. and S.I.
S.I.
W.I.
UMC 180 nm CMOS Process

## Slide 62: Other non-idealities of the MOSFET behaviour
Gate-bias dependent mobility
mCox depends on VGS (decreases at high VGS)
(all devices)
Carrier velocity saturation
ID dependence on VGS in strong inversion
tends to become linear (instead of quadratic)
(Short channel devices). Again, appears as
a reduction of the mCox at high VGS
Gate current
May be due to tunneling (all devices) or hot electrons - hot holes (Short channel devices)
RSCE and RNCE
Vth depends on MOSFET dimension (W and L)
(Short channel devices).

## Slide 63: BJTs in integrated circuits: Vertical NPN
BiCMOS: CMOS + p-base and buried-layer
The n-pocket can be an n-well
The buried-layer a buried-well of a triple-well CMOS
Same as (b) but with the
Metal 1 removed
A diode between collector and
substrate is present capacitance
p-base
p-base
buried-L
buried-L

## Slide 64: The lateral PNP
Slower than vertical devices due to
large base series resistance (rbb')
and base-to substrate capacitance
Lower early voltage (VA), due to
non-optimal collector doping.
Larger than vertical devices for the same
current capability

## Slide 65: The substrate PNP: compatible with standard CMOS n-well processes
Limitation: The collector is
committed to the substrate,
(forced to VSS)

## Slide 66: BJT output characteristics
Saturation
Forward Active Region
VBE, VCE : control
voltages
IC, IB: dependent
currents

## Slide 67: BJT model in the forward active zone
Sometimes this expression is used
in order to refer to VBE and VCE as
control voltages:
For calculation of IC and IB in all operating zones (saturation, cut-off,
forward active, reverse active) the Ebers-Moll model should be used.

## Slide 68: BJT: small signal model
Small signal dc model
Equivalence with the MOSFET parameters
BJT
MOSFET

## Slide 69: BJT capacitances in forward active region (vertical npn)
Transition frequency

## Slide 70: BJTs in Integrated Circuit: instance parameters
minimum size BJT
("elemental" BJT)
parameter "area"
(dimensionless)
area
area
area=2 (,3, 4 ….)
area = integer
area=1.5
area may not be an
integer (not all PDKs
allow this)

## Slide 71: BJT sizing: Effect of the area parameter on the electrical parameters
Electrical effects of area parameter:
IS
VA
b
CJE
…..
area × IS
VA
b
area × CJE
…..
elemental BJT
elemental BJT with area
specified as an instance parameter

## Slide 72: BJT sizing: Gummel plot and beta plot
This refers to the
elemental BJT (area=1)
My BJT has to carry this current
(200 mA). The elemental BJT would
be damaged
Using a BJT with area=100 would be
equivalent to make the elemental BJT
work with a current 100 times smaller.
This corresponds to the operating point
given by the blue line
b
b
IC
Gummel Plot
Beta Plot
VBE