## Slide 1: Very basic rules to facilitate analysis / synthesis of integrated analog circuits
In these slides:
How to obtain the large signal equation of p-type transistors from n-type ones and a few intuitive views about both.
Basic expressions for the resistances seen from each terminal in notable single-transistor configurations.
The gmrd (gmro in BJTs) product
Power rails, floating rails and reference nodes

## Slide 2
From n-type transistors to p-type ones
We will start from MOSFETs and, at last, will briefly cite the case of BJTs. These considerations apply to the large signal behavior, since the small-signal equivalent circuits of n-type and p-type transistors are identical.

## Slide 3: From n-MOSFETs to p-MOSFETS
Apply this transformation:
And put it into the n-MOS equations:
Obtain the correct p-MOS equations!

## Slide 4
Useful examples: transition between triode and saturation region
Applying the transformation
N-MOS
P-MOS

## Slide 5: Again, on the triode-saturation transition: Strong Inversion
VG
VG-Vtn
VD
triode
saturation
N-MOSFET in Strong Inversion
Condition to keep the MOSFET in saturation
In order to keep an N-MOSFET in saturation VD cannot descend below the gate voltage (VG) reduced by Vtn
This picture represents a drain voltage that progressively decreases while the gate voltage is constant
Practical Rule

## Slide 6: Again on the triode-saturation transition: Strong Inversion
P-MOSFET in Strong Inversion
Condition to keep the MOSFET in saturation
VG
VG+|Vtp|
VD
triode
saturation
In order to keep a P-MOSFET in saturation VD cannot rise over the gate voltage (VG) increased by |Vtp|
Enhancement P-MOSFET

## Slide 7: The "natural" direction of the current in P-type transistors
This is equivalent to reverse the
conventional direction of the
drain current for P.MOSFETs
By this convention, the
drain current is positive
also in P-MOSFETs

## Slide 8: An intuitive view to deal with p-MOSFETs
always
in strong and moderate inversion
in strong inversion
for enhancement
p-MOSFETs
Passing from the gate to the source the voltage is increased by |VGS|
The voltage drop across
the mosfet, measured along the natural direction of ID is |VDS|

## Slide 9: From NPN BJTs to PNP ones
Transformations
IB
IC
These two can be
avoided if the opposite
convention for the current
direction is used

## Slide 10
Notable case of small signal resistances
In order to simplify the analysis of circuits including a large number of devices, it is important to keep in mind simple expressions of the resistances that are seen from one terminal of a transistor to gnd in different configurations.
In the next slides, cases of great importance for the synthesis of electronic circuits are recalled. The expressions may be complicated, and it is important to remember only the simplified forms and the broad conditions for which the approximations hold true

## Slide 11: The six basic (small signal) resistances: MOSFETS (for simplicity, body effect is neglected in these formulas)
exact result
Conditions for approximation
Diode-connected MOSFET

## Slide 12: The six basic (small signal) resistances: BJTs
exact result
Conditions for approximation
exact result
approximations

## Slide 13: Classification of resistances in analog circuits
 | Small | Medium-large | Large | Very large
MOSFETs | 1/gm | - | rd | (gmrd)rd
BJTs | 1/gm | rbe (hie) | r0 | hfero

## Slide 14
The gmrd product in MOSFETs (gmro in BJTs)
The gmrd product in MOSFETs and JFETs, or the equivalent gmro product in BJT, plays an important role in many circuit configurations.
For example, this product appears in the voltage gain expression of most topologies used to design high-gain amplifier stages. A large gmrd product is also beneficial for the output resistance of high-performance current sources.
In the next slides we will consider which are the factors that affect the gmrd (gmro) product.

## Slide 15: The gmrd product (in saturation region)
Large gmrd products are obtained for small VGS-Vt and large L
As a broad estimate, gmrd can be considered to be of the order of 100

## Slide 16: gmr0 for BJTs in active zone
gmr0 may easily reach 1000 (e.g. for VA=25 V)
gmr0 does not depend on the BJT operating point
(this is an important difference between BJT and MOSFETS)
This result is correct in the IC region where the exponential IC vs. VBE dependence holds
(see the Gummel Plot)
In general, the performance of BJT integrated circuits is affected by less degrees of freedom (DOFs) than CMOS ones. One of the reason is that, for a given temperature the gm /IC ratio is a constant (=1/VT). If there is the need to change this ratio, emitter degeneration is the simplest choice.

## Slide 17: Emitter degeneration (source degeneration)
Lower effective gm for the same ID (IC)
Higher equivalent ro
Higher input resistance (BJT)
reduced gm
voltage drop across RE in the operating point

## Slide 18
4. Power rails and floating rails
Each power rail is connected to a single terminal of the power supply. Power rails carry the supply currents to all blocks of the IC
If the currents that the floating rail provides to the circuits connected to it (U1 and U2) are too large, the voltage of the floating rail can be altered. In that case it is necessary to use an active circuit (e.g a voltage buffer) to create the floating rail.
16 V
-16 V
0 V
3.3 V
Low voltage
domain
High voltage
domain

## Slide 19: Reference node for voltages: power supply invariance
Output voltage of circuit A, referred to Vdd (complementary to VoA)
Output voltage of circuit A, referred to gnd
Input voltage of circuit B, referred to gnd
Input voltage of circuit B, referred to Vdd

## Slide 20: Invariance of input and output voltages with respect to supply voltage
Depending on the topology of a given block (A)
Input.
The real input signal is Vi
The real input signal is Vi-C
(The internal currents and output voltages do not vary if the real input is constant even if Vdd varies)
Output.
For a constant input voltage:
Vo is independent of Vdd
Vo-C is independent of Vdd

## Slide 21: Example: n-MOS common source amplifier with resistive load (unipolar)
When referred to the gnd rail, the output voltage of this amplifier is not invariant with respect to the the power supply voltage (Vdd).
On the other hand, the complementary voltage
Vo1-c is invariant with respect to the supply voltage.
Invariant
Non-Invariant

## Slide 22: Example: cascade of two n-mos common source stages
Vout
wrong configuration!
ID2 (and then Vout) is strongly dependent on Vdd. This means a very low PSSR. For large Vdd variations, the operating point of M2 can be altered in an not acceptable extent.

## Slide 23: Example: cascade of two complementary common source amplifiers
correct configuration!
N-stage
P-stage
The N-stage:
requires an input voltage (Vi1) that is invariant when referred to gnd.
Produces a voltage that is invariant when referred to Vdd
The P-stage:
requires an input voltage (Vi1) that is invariant when referred to Vdd.
Produces a voltage that is invariant when referred to gnd
P-type and N-stages can be cascaded with low sensitivity to Vdd (high PSSR)