## Slide 1: Voltage amplifiers: number of inputs and outputs
Unipolar:
single input
single output (single-ended, S/E)
Differential:
differential input,
single output (single-ended, S/E)
Fully Differential:
differential input,
differential output

## Slide 2: Voltage Amplifiers: gains

## Slide 3: Differential amplifiers: parameters
Input voltage ranges:
Input differential range (maximum VID (VD) to maintain an acceptable input-output linearity
Input common-mode range:
Interval of VC values where the amplifier behaves as designed
Output voltage range
(Output voltage swing)
Outside the output range the amplifier stop working correctly (e.g. the output voltage tends to saturate)
Linear response
(with input offset voltage)

## Slide 4: Differential amplifiers: role of the input common mode range
In the ideal case:
We have:
The voltage follower operates correctly only for Vin within the CM range
Another condition is clearly that Vout is within the output range
Example: voltage follower (buffer amplifier)
Then the conditions for correct operation are:

## Slide 5
Single Stage Voltage Amplifiers
The first component converts the input voltage (single or differential) into a current (single or differential)
The second component is a current processing network, that takes the input currents and applies simple linear operations such as:
Addition and subtraction
Addition of constant currents
Multiplication by a constant gain factor
The processed currents are finally conveyed to an output resistance (Rout) and converted back to a voltage (Vout). In most cases, Rout is not a physical resistor, but is the output differential resistance of the I-to-I network.
For this reason, one of the function of the I-to-I network is increasing the output resistance to increase gain
example
example
small-signal output voltage
Vout
V-to-I
I-to-I
I2
I1
Vin
Rout
Iocc

## Slide 6: Differential amplifier with resistive loads
Small signal analysis
Differential mode:
Single-ended case:
Fully-differential case:

## Slide 7: Common mode Analysis
This, actually, is not an ideal current source.
It has a finite output resistance = ros If it is implemented by a simple current mirror, ros= rd otherwise it can be even higher
The source voltage practically follows the common mode variations. VS is VC shifted by VGS

## Slide 8: Common mode gain and CMRR
output voltages
Single-ended case
Considering that generally I0 is produced by a simple current mirror, ros=rd, then CMRR~40 dB,
This CMRR is not sufficient for many applications

## Slide 9: Common mode gain and CMRR
Fully differential case
is a relative matching error ~ 0.01
Adequate for most applications

## Slide 10: BJT case
In the case of a BJT differential amplifier, the expressions are exactly the same as for the MOSFET case.
The only important difference is the presence of a base current that is drawn from the voltage sources that provide Vi1 and Vi2. In terms of small signal analysis, this base current is the cause of a finite input resistance that may result in an input attenuation if the signal voltage sources (Vi1, Vi2) have a significant internal resistance.
IB1
IB2
Equivalent circuit of
the input terminals

## Slide 11: Maximum gain for a given supply voltage
single ended
fully-differential
nominal case:
RD1=RD2=RD
RDID is the static voltage drop across resistors RD. It cannot exceed the total supply voltage VDD-VSS
Example: VTE=50 mV, VDD-VSS=3 V:
|Add | < 60
With a BJT: VTE=VT=25 mV:
|Add | < 120
To get the highest gain for a given supply voltage it is convenient to bias the MOSFETS with the smallest VTE.

## Slide 12: Offset voltage of differential amplifiers with resistive load
We can consider the difference of VGS as the matching error between two nominally identical circuits: M1,RD1 and M2,RD2
Nominally identical
circuits
MOSFET case - fully-differential - Strong inversion
posynomial
form

## Slide 13: Offset voltage of differential amplifiers with resistive load
MOSFET case - fully-differential
A
B
This is a generic expression of VD, corresponding to a given value of
This expression gives Vio for the particular value that results in Vout=0

## Slide 14: Offset voltage of differential amplifiers with resistive load
MOSFET case - fully-differential
defining:
Imposing Vout=0 is the same as imposing DZ=0
RDID is the average value and cannot be zero

## Slide 15
Offset voltage of differential amplifiers with resistive load
MOSFET case - fully-differential

## Slide 16: Role of the design parameters
LR
WR
L
W
To be made as small as possible, to reduce sVio
Small offset means large silicon area

## Slide 17: Offset voltage of a BJT differential amplifier with resistor load

## Slide 18: Offset voltage of a BJT differential amplifier with resistor load
Minimum size BJT (elemental BJT) of the process
Small offset means large silicon area

## Slide 19: Temperature drift of the input offset voltage: BJT case
These terms are practically temperature independent (ratios of homogeneous quantities)

## Slide 20: A method to reduce the offset voltage and its drift
By trimming the resistors, I can null the offset. In this way, also the temperature drift is nulled.
This is an advantage of the BJT amplifier. Trimming the offset of a MOSFET differential amplifier does not null the drift.
Example: vio=1 mV
T=300 K

## Slide 21: Example: the OP07
Resistors are varied by laser trimming to null the offset
In this way, also the offset drift is strongly reduced
The base currents of the input devices (Q1,Q2) are reproduced by Q3 and Q4 and than fed back to the input terminals by mirrors Q8,Q6 and Q7,Q5. This approach allows to reduce the input bias currents.

## Slide 22: OP07 vs mA741
mA741
OP07

## Slide 23
How is the amplifier offset when the single ended option is chosen?
Single ended (S/E): device parameters do not appear as differences: the output voltage is affected mainly by global errors
The single ended case is subjected to a much larger offset!
Compare with the fully-differential case: the output voltage depends only on matching differences