## Slide 1
CMOS differential amplifier with resistive load: limitations
The S/E version has a poor CMRR (large Ac) and large input offset voltage
Both the S/E and fully-diff. versions reach low voltage gains at small supply voltage
Problem 1: Consider the output voltage in the fully-differential case with no resistor mismatch:
The drain current difference appears:
This reduces Ac (ID1 and ID2 tend to be equal for only common mode applied) and the output voltage for VD=0 is affected only by matching errors.
Solution for a S/E amplifier: produce the current difference (ID1-ID2) and then put it into a single resistor. Problem 2: Do not use a passive component for the resistor

## Slide 2
CMOS differential amplifier with current mirror load
ID1+ID2
Iocc =ID1-ID2
ID1
ID1
We need a S/E output port
High CMRR (> 80 dB)
High gain (~ 40 dB) even at low supply voltages (Vdd-Vss).
Specifications
Vdd
M3
M4
Vout
I0
Vss
Vi1
Vi2
M1
M2
ID2
ID1

## Slide 3: Subunits of the amplifier with mirror load
V-to-I
I-to-I
I2
I1
Vin
Rout
Iocc
I1
I2

## Slide 4: Operating point : Vid=0
Symmetrical stimulus, but ….
The circuit is not symmetrical

## Slide 5: Demonstration of the exact symmetry of the electrical solution for Vid=0
M1 and M2
M3 and M4
With fixed VGS and VBS, ID is a monotone function of VDS (or |VDS| for a p-MOS.

## Slide 6: Demonstration of the exact symmetry of the electrical solution for Vid=0
Proof by contradiction:
Contradiction
Let us suppose:
From Kirchhoff #2:
We want to demonstrate that:

## Slide 7: Demonstration of the exact symmetry of the electrical solution for Vid=0
K
Repeating the procedure for ID1<ID2 we get another contradiction; thus, the only possible solution is:
For Vid=0, the electrical solution is perfectly symmetrical

## Slide 8: Differential mode gain
Norton equivalent circuit
of the output port
Small-signal equivalent circuit
iric
Circuit for Rout calculation

## Slide 9: Differential mode gain: Rout calculation.
For the superposition theorem:
Case 1:
Case 2:
Case 1:
Case 2:

## Slide 10: Differential mode gain
The gain is of the order of
Independently from the supply voltage

## Slide 11: Differential mode gain
In order to obtain a large differential-mode gain it is necessary to:
Set VTE to a small value
Use long MOSFETs (small l)
In strong inversion. Minimum VTE=50 mV
In weak inversion.
VTE 35-40 mV

## Slide 12: Common mode gain
vc
vc
Is it possible??
As in the case of differential input voltage, we can try to use the Norton equivalent circuit of the output port.

## Slide 13: Common mode gain
The problem occurs when we calculate iocc. Placing a short circuit across the output port, disrupts the symmetry:
vc
vc

## Slide 14: Common mode gain
It is possible to exactly calculate iocc, taking into account the actual id1/id2 ratio and id4/id3 ratio ….
… but this is a very tedious approach
There is a much simpler way:
Let us remove the short circuit and directly calculate vout. Now , for vid=0, the circuit is symmetric again and, in particular: vk=vout
vc
vc
vk

## Slide 15: Common mode gain
vc
vc
vk
for ros=rd
(worst case: the tail is the output branch of a simple current mirror)
and considering all gm's and rd's equal for simplicity
A CMRR of 80 dB can be easily reached

## Slide 16: Large-signal dc transfer function
In strong inversion
For VD=0:

## Slide 17: Large-signal dc transfer function
gm1
Vout variations for small VD variations around the origin

## Slide 18: Moving away from the origin, step by step
In the first step, Vout moves along the tangent calculated in the origin
When VD and Vout get far from the operating point, the parameters of the small signal models change and the slope of the tangent change as well

## Slide 19: Large-signal dc transfer function
VD
Vout(0)
VDQ
VDQ+DVD
Vout(VDQ)
Vout(VDQ)+DVout
Vout
VDQ
VDQ+DVD

## Slide 20: Approximate dc transfer characteristic
Example: Ad=100, Vdd-Vss=5V DVD<50 mV
VDMAX
-VDMAX
Vout
VD
Vdd
Vss
Vout(0)

## Slide 21
Practically constant and equal to gm1
M4 enters triode region and rd4 drops down
M2 enters triode region and rd2 drops down
Vout
VD
Vdd
Vss
Vout(0)

## Slide 22: Minimum output voltage
VD in the linear zone is at most
a few tens mV
VC varies between VSS and VDD
We can neglect VD/2 with respect to VC

## Slide 23: Minimum output voltage
Strong inversion
Weak inversion

## Slide 24: Complete dc transfer characteristic
VD
Vout
Vdd
Vss
Vout(0)=Vdd-|VGS3|
max(Vout)=Vdd-|VDSAT4|
min(Vout)=VC -VGS2+VDSAT2
VC -VGS2
Slope=Ad
Vout gets close to M1,M2 source voltage when VDS2 approaches zero (M2 is in deep triode region)
=VS2
Vout approaches Vdd when ID2 approaches zero and M4 gets in deep triode region

## Slide 25: Minimum supply voltage Vdd-Vss
VoutS
VDS1
|VDS3|
Example: VMIN=100 mV
VDSAT2=100 mV
|VGS3|=0.5 V

## Slide 26: Input common mode range
Lower limit
As VC is progressively decreased, also VS decreases at the same pace and eventually the voltage across the current source I0 will get smaller than the minimum value VMIN. From that point on, I0 will rapidly decrease, turning off the stage.

## Slide 27: Input common mode range
Upper limit
As VC is progressively increased, also VS increases at the same pace. Since Vout=VK =VD2 = VD1 is fixed, eventually VDS1 and VDS2 will drop below the saturation voltage.
Vk

## Slide 28: Input common mode range
The input common mode voltage can get even slightly higher than Vdd
This difference can be >0 because:
(Vt1 is affected by body effect
if M1 and M2 body is at VSS)
These overdrive voltages can be made equal by design, so they cancel each other