## Slide 1: Voltage references
Voltage references are used for:
Providing an absolute reference voltage for ADCs and DACs
Providing an absolute reference voltage for stimulating sensors or other external devices that require precise control voltages and/or currents.
Creating constant bias voltages (and currents) when required
Voltage references are blocks that produce an output voltage that is independent of PVT variations:
V: Supply voltage
T: Temperature
P: Process errors

## Slide 2: Possible reference voltage sources
Zener Diodes
Problems:
Require additional process steps, but only a small number of components are required for each chip (not convenient)
Available voltages are > 3 V
Temperature stability is poor for VZ ≠ 5-6 V
The reference voltage generated by a Zener diode is noisy (very wide band noise)
Band-gap circuits

## Slide 3: Band-gap voltage reference: principle of operation
CTAT
CTAT: Complementary To Absolute Temperature
PTAT
PTAT: Proportional To Absolute Temperature
VBG
We start with a DIODE (BJT) biased with
a current IC

## Slide 4: Band-gap voltage reference: determination of parameter b and estimate of the output voltage
We have to determine the value of b, for which:
Example:
Good news!
This voltage is compatible with low-supply voltage circuits

## Slide 5: Band-Gap voltage reference: theory
It is not necessary that IC is temperature-independent
constant
constant
constant
Gray, Hurst, Lewis, Meyer, "Analysis and design of analog integrated circuits" 4th edition, 2001 J.Wiley & Sons
VG0

## Slide 6: Band-Gap voltage reference: theory
The name "band-gap" of this reference voltage comes from VGO, which is the dominant part
VGO is numerically equivalent to Eg0 measured in eV
The derivative of VBG depends on temperature
Let us calculate the derivative of VBG with respect to temperature

## Slide 7: Band-Gap voltage reference: theory
We impose that the derivative of VBG is zero at a given temperature T0
This is possible, since b is a free parameter that can be chosen to obtain this result.
Typically: a=1

## Slide 8: Band-gap voltage reference: calculation result
T0=300 K
T0=323 K
1 mV
T (Kelvin)
VBG (V)
-20 °C
+100 °C

## Slide 9: Band-Gap voltage: a CMOS compatible Circuit
Part 1: PTAT current generator
neglecting the effects
of VDS on ID :
I1
I2
I is proportional to T (PTAT) and independent of Vdd.
Substrate PNPs
Q1
Q2
Q2
Q2
Q2
Q2
Q2
Q2
Q2
Common centroid
layout
For n=8

## Slide 10: Band-Gap voltage: a CMOS compatible Circuit
I
I
I
Biased with I
a=1

## Slide 11: Deriving a temperature sensor from the Band-Gap circuit
Adding this branch, we can obtain a voltage proportional to the absolute temperature, which can be conveniently used to monitor the chip temperature.
I
I
I
I

## Slide 12: PTAT current generator: multiple stable states
I1
I2
fNL
I2=I1
P1 is the correct operating point. P2 (null currents) is stable because the two mirrors have very small gains around the origin.
P1
P2
A start-up circuit is necessary to prevent the circuit from being trapped into P2
Positive feedback loop

## Slide 13: Mention to another very popular bandgap circuit
Due to virtual short circuit:
(voltages across R1 and R2)
We choose R1=R2
I1
I2
op-amp