## Slide 1: Sensor systems: general considerations (2)
What is the input of a sensor system?
Non-electrical quantities ( e.g. temperature, pressure, acceleration, flow, concentration of chemical species... )
but also:
Electrical quantities that characterize a device or a process: impedance, current, charge ...
Biopotentials (ECG, EEG , etc)

## Slide 2
Sensor systems: general considerations (2)
What does a sensor system do?
Environment
Examples: a house, a vehicle, air or water in open spaces, the soil, a living body ....
quantity of
interest: x
Sensor system
Representation of x
(a voltage, a number ...)
human
comprehension
machine (for automation tasks)
End users
Information flow

## Slide 3: Sensor systems: general definitions (3)
Information flow in a sensor system
Environment
sensor(s)
probe(s)
Electrical
Non-electrical
AFE
Analog Front-End
Digital Processing
Linear Filtering
Data Interpretation
Data compression
Display
Communication
Storage
Analog domain
Digital Domain
ADCs

## Slide 4: System partitioning
A complex sensor system can be formed by a large number of different partially independent components. In some cases the sensor system can be distrubuted in a large volume and include tens or hundreds of sensors.
In other cases the system can be relatively simple and small in size.
For this reason, in the system level design phase, it is important to organize the sensor system in a hyerarchical way, deciding at which level the above depicted operations must be performed

## Slide 5: Sensor systems: a possible hierarchy
Sensors / Probes
AFE + ADC
Digital preprocessing
Communication
(wired)
Sensor modules
Embedded System
(e.g. MCU)
Communication
(wired or wireless)
Sensor nodes
High performance digital processing unit
Complex Human - Machine Interface
High-capacity data storage
World-scale
communication
High level sensor system
Sensor nodes
Sensor module
Simplified Human-Machine Interface
Data logging

## Slide 6: Example 1: Pulse oximeter A simple, complete sensor system
Sensor probe, AFE, ADC = Sensor module
Digital Processing
Human Interface (simplified)
Communication
Performs the functions of sensor node

## Slide 7: Example 2: Integrated 9 axis inertial sensor (sensor module or smart sensor)
3-axis accelerometer
3-axis gyroscope
3-axis magnetometer
SPI -I2C communication lines

## Slide 8: Example 3, a complex case: sensor system in an airplane
High level computing machine
Sensor node
Includes different sensor modules
(air speed, air temperature, angle of attack) and implements complex communication protocols.
To reduce wiring, there is a tendency towards wireless comunication between sensor nodes

## Slide 9: Example 4: Wireless Sensor Network
Sensor Nodes
Can be equipped with different sensor types or simply replicate the same sensor set in different locations (distributed sensing)
Network: Multi-hop communication protocol
Sink
High level computing machine: PC, smartphone, emebedded computer

## Slide 10: Example of a sensor node for WSN
Libellium wasp-mote
Multi-protocol wireless communication
https://www.libelium.com/iot-products/waspmote/
Sensor module
(air quality)