## Slide 1: Magnetic sensors
Magnetic field:
H : Magnetic field strength. Unit: A/m)
B : Magnetic flux density (magnetic induction) Unit: Tesla (T)
Non-SI unit, still commonly used: Gauss: 1 Gauss = 100 mT
In a medium of magnetic permeability m:
Vacuum permeability m0= H/m (H=Henry).

## Slide 2: Example of electric field magnitude
Earth's magnetic field: 25 to 65 mT
IM
H
r
Magnetic field produced by a current
Example:
m=m0 (air, vacuum ...)
IM=1 A, r=10 cm
B=20 mT
General purpose permanent magnets (e.g. "refrigerator magnets")
B=5-20 mT
Inside the gap of loudspeaker magnets:  1 T
Refrigerator
magnets

## Slide 3: Applications of magnetic sensors
Magnetic compass:
Aid to navigation
Orientation finding
Accuracy improvement of IMUs (inertial measurement units)
Proximity sensors
Angular position sensors
Contactless current measurements

## Slide 4: Magnetic sensors: market
By Type (in automotive)
By Application
Hall
AMR
TMR
GMR
3-D Hall

## Slide 5: Types of magnetic sensors
Detection Limit
Earth's magnetic field
Heart and Brain
magnetic field

## Slide 6: Search Coil
B
A ferromagnetic nucleus can be used to concentrate the field lines, increasing the sensitivity
The search coil needs the magnetic flux to be variable.
Constant magnetic fields can be measured only mechanically rotating or vibrating the coil.
AC Fields only!

## Slide 7: Hall sensors
Basic Hall effect:
Discovered by Edwin Hall in 1879
I
Conductor or
semiconductor plate
Electrical
current
q: charge of the charge carrier (can be positive or negative)
v: charge carrier velocity
B: Magnetic induction field
F: Lorentz Force
Positive
charge
carriers
Negative
charge
carriers
The force has the same direction

## Slide 8: Hall effect: formation of the Hall voltage
W
x
y
Stationary conditions:

## Slide 9: Hall Voltage
L
W
d
x
y
z
The Hall effect can be used to determine the carrier mobility m

## Slide 10: Case of negative charges:
The Hall voltage change sign if the sign of the charge charrier is changed
The Hall effect can be used to determine if the main charge carries are holes or electrons

## Slide 11: Hall Voltage: a more practical expression
L
W
d
x
y
z
The Hall voltage is proportional to both the magnetic field (B) and the bias current (I)
For this reason, the sensitivity is generally expressed in:
V / (A T)
"Volt per Ampere Tesla"

## Slide 12: Examples of Hall voltage magnitude
L
W
d
d=1 mm
(possible thickness of an interconnection
layer in an Integrated circuit)
Copper:
n-Si with ND=10-16 cm-3 : n