## Slide 1: Sensor systems: general definitions (1)
What is the input of a sensor system?
Non-electrical quantities ( e.g. temperature, pressure, acceleration, flow ... )
but also:
Electrical quantities that characterize a device or a process: impedance, current, etc.
Biopotentials (ECG, EEG , etc)

## Slide 2: Sensor systems: general definitions (2)
Information flow in a sensor system
Environment
sensor(s)
probe(s)
Electrical
Non-electrical
AFE
Analog Front-End
ADCs
Digital Processing
Linear Filtering
Data Interpretation
Data compression
Display
Communication
Storage
Analog domain
Digital Domain

## Slide 3: System partitioning
A complex sensor system can be formed by a large number of different partially independent components. In some cases the sensor system can be distrubuted in a large volume and include tens or hundreds of sensors.
In other cases the system can be relatively simple and small in size.
For this reason, in the system level design phase, it is important to organize the sensor system in a hyerarchical way, deciding at which level the above depicted operations must be performed

## Slide 4: Sensor systems: a possible hierarchy
Sensors / Probes
AFE + ADC
Digital preprocessing
Communication
(wired)
Sensor modules
Embedded System
(e.g. MCU)
Communication
(wired or wireless)
Sensor nodes
High performance digital processing unit
Complex Human - Machine Interface
High-capacity data storage
World-scale
communication
High level computing machine
MCU-based Sensor nodes
Sensor module
Simplified Human-Machine Interface
Data logging

## Slide 5: Example 1: Pulse oximeter A simple, complete sensor system
Sensor probe, AFE, ADC = Sensor module
Digital Processing
Human Interface (simplified)
Communication
Performs the functions of sensor node

## Slide 6: Example 2: Integrated 9 axis inertial sensor (sensor module or smart sensor)
3-axis accelerometer
3-axis gyroscope
3-axis magnetometer
SPI -I2C communication lines

## Slide 7: Example 3, a complex case: sensor system in an airplane
High level computing machine
Sensor node
Includes different sensor modules
(air speed, air temperature, angle of attack) and implements complex communication protocols.
To reduce wiring, there is a tendency towards wireless comunication between sensor nodes (WSN= wireless sensor network)

## Slide 8: Example 4: Wireless Sensor Network
Sensor Nodes
Can be equipped with different sensor types or simply replicate the same sensor set in different locations (distributed sensing)
Network: Multi-hop communication protocol
Sink
High level computing machine: PC, smartphone, emebedded computer

## Slide 9: Sensor / object interaction
The physical object is a solid, liquid or gaseous to which the quantity to be measured belongs
It can be a very simple object (e.g. a single-piece mechanical part) or a complex object, like the human body or a chemical reactor
The sensing operation requires the sensor / probe to interact with the physical object.
The sensor package (housing) must be designed to enable the required interaction and, at the same time, protect the sensors

## Slide 10: Sensor - object interaction
The interaction can be contactless (e.g. IR thermometer) or with contact (e.g. a thermocouple temperature probe).
Protection of the sensing elements is particularly important, for example, when the physical object is in liquid phase (liquid flow sensors, ion concentration sensors) or it is a corrosive gas.
Example: a liquid pressure sensor (10-bar resistant, usable for depth meters)
LPS33HW
Insulating gel:
Avoid direct contact with the liquid but ….
2) Transmit pressure from the liquid to the MEMS chip

## Slide 11: Electrical connection and continuity
A particular aspect that have to be assessed is the degree of electrical contact between the sensor terminals and the physical object
Only capacitive coupling
(AC coupling)
Only resistive coupling
C: order of pF
VISO (maximum that the barrier can withstand)
The presence of a dc path can be unwanted (defective insulation) or necessary

## Slide 12: Examples
H2O
conductivity probe
terminals
Probe for the measurement of the water conductivity
(used to monitor the quality of water supplies)
In this case, electrical continuity is necessary to perform the measurement
ceramic or plastic
insulator
thermocouple
(or thermistor)
metal case
liquid
Electrical continuity is not necessary, but a leakage conductance between the sensor terminal and the liquid can develop when the insultaor properties degrade with time
Temperature probe