## Slide 2: Outline
fault tolerant computing: why and what
computer-based systems: faults and failures
forms of redundancy:
- Hardware redundancy
- Information redundancy
- Timing redundancy
- Software redundancy
effectiveness of fault tolerance

## Slide 3: Fault tolerant computing: why and what
Computers are increasingly used in safety-critical systems:
- transport (automotive, railways, aerospace, ...)
- medicine
- process control
- ....
Future safety-critical systems will be more automated and more dependent on computers
Fault tolerant computing:
the ability of the system to deliver the expected functionality during its operational life also in case of malfunctions ( important in safety-critical systems, systems whose failure may result in death or serious injury to people, loss or serious damage of equipment, or environmental harm)

## Slide 4: Transport systems: Aerospace
Fly-by-wire (FBW) system: all commands and signals are transmitted electrically along wires.
These signals are sent to flight-control computers (FCS) that reconvert the electrical impulses into instructions for control surfaces like wing flaps or the tail.
http://www.aviationcoaching.com/wp-content/uploads/2015
/08/fly-by-wire-system.jpg
Earliest aircraft: controlled by the pilot using the steel cables, pulleys and hydraulic actuators

## Slide 5: Transport systems: Automotive
Over 80 different embedded processors, interconnected with each other.
Key ECUs (Electronic Control Unit):
Engine Control Modul (ECM)
Electonic Brake Control Module (EBCM)
Transmission Control Module (TCM)
Vehicle Vision System (VVS)
Navigation Control Module (NCM)
…
Sensing and Computing in Cars
Main vehicle control systems replaced with electronic controls (no physical connection):
throttle - Electronic Throttle Control
brakes - Brake-by-Wire
steering - Steer-by-Wire

## Slide 6: Fault tolerant computer-based systems
For a computer based safety-critical system, the safety of the system depends strongly on its computers.
Faults are unexpected events that may compromise the system functionality
Faults in computer systems:
hardware faults (e.g., stack-at 0 of a line, memory cell bit flip)
software faults (e.g., a bug in the code)
General questions: How to build dependable computer-based systems. Can we justifiably trust the dependability of such systems?

## Slide 7: Fault tolerant computer-based systems
1. a system is as strong as its weakest component
Hw and sw systems relaying on hidden components
2. small hidden faults may have large effects (digital machine)
Computer failures differ from failures of other equipment
Subtler failures than “breaking down” or “stopping working”, ..
The computer is used to store information: there are many ways information can be wrong, many different effects both within and outside the computer

## Slide 8: Chain of threats: Faults -> Errors -> Failures
Taken from [Avizienis et al. 2004]

## Slide 9: Replication
Make available
- two or more copies of data item that may be corrupted
- a mechanism that compares them and declares an error if they differ
The two copies must be unlikely to be corrupted together and in the same way
  Examples: Duplicated circuitry, Transmit messages twice, Store data in two separate places (e.g. mirrored disks)
Replication: can have a very important impact on a system in the area of performance, size, weight, power consumption and others

## Slide 10: Redundancy in fault tolerant computing
HARDWARE REDUNDANCY
Physical replication of hw (the most common form of redundancy)
The cost of replicating hw within a system is decreasing because the costs of hw is decreasing
INFORMATION REDUNDANCY
Addition of redundant information to data in order to allow fault detection and fault masking
TIME REDUNDANCY
Attempt to reduce the amount of extra hw at the expense of using additional time
SOFTWARE REDUNDANCY
Tolerating faults in software

## Slide 11
HARDWARE REDUNDANCY

## Slide 12: Hardware redundancy
Passive fault tolerant techniques
use fault masking to hide the occurrence of faults
rely upon voting mechanisms to mask the occurrence of faults
do not require any action on the part of the system / operator
generally do not provide for the detection of faults
Active fault tolerance techniques
use fault detection, location and recovery
detect the existence of faults and perform some actions to remove the faulty hw from the system require the system to perform reconfiguration to tolerate faults
common in applications where temporary, erroneous results are acceptable while the system reconfigures (satellite systems)
Hybrid approach
very expensive
often used in critical computations in which fault masking is required to prevent momentary errors and high reliability must be achieved

## Slide 13: Passive fault tolerance technique:TMR
1. Triple Modular Redundancy (TMR) – fault masking
Module 1
Module 3
Module 2
Voter
output
Triplicate the hw (processors, memories, ..) and perform a majority vote to determine the output
- 2/3 of the modules must deliver the correct results
- effects of faults neutralised without notification of their occurrence
- masking of a failure in any one of the three copies
Good for transient faults
For permanent faults, since the faulty module is not isolated, the fault tolerance decreases
Voter is a single point of failure

## Slide 14: Cascading TMR with triplicated voters
The effect of partitioning of modules (A, B, C) is that the design can withstand
more failures than the solution with only one large triplicated module
The partition cannot be extended to arbitrarily small modules, because reliability improvement is bounded by the reliability of the voter
Triplicated voters: voter errors propagates only of one step
Taken from [Siewiorek etal., 1998]

## Slide 15: TMR: the Voter
Difficulties
Delay in signal propagation:
- due to the voter
- due to multiple copies synchronisation
Trade-off : achieved fault tolerance vs hw required
Reliable Voters
Hardware voters are bit voters that compute the majority on n input bits. Optimal designs of hardware voters with respect to circuit complexity, number of logic levels, fan-in and fan-out and power dissipation
1 bit voter
OUT = AB + BC + AC

## Slide 16: Problems with voting procedure on analog signals
using multiple analog to digital convertes and performing bit-by-bit voting on their digital output is not satisfactory
The three results from the analog to digital converters may not completely agree, for example, they could produce a result which differs for the least-significant bit even if the exact signal is passed through the same converter
perform voting in the analog domain:
 average the three signals  choose the mean of the two most most similar signals
 choose the median of the three signals (pseudo voting)

## Slide 17: N-Modular Redundancy
2. NMR N is made an odd number
Coverage: m faulty modules, with N = 2m +1
5MR: tolerates 2 faulty modules
7MR: tolerates 3 faulty modules
……..
Module 1
Module 3
Module 2
Module 5
Module 4
Voter
output

## Slide 18: Active hw redundancy
Duplication with comparison scheme (Error detection)
Two identical pieces of hw (Module1 and Module 2) are employed
they perform the same computation in parallel
when a failure occurs, the two outputs are no more identical and a simple comparison detects the fault Then the comparator (hw component) selects the correct output and reconfigure the switch to select the correct value
the comparator must select the correct value
Module 1
Module 2
output
input
comparator
switch
Dual-modular redundancy
(also Duplex system)

## Slide 19: Active hw redundancy: the comparator
Assumption: the two copies must be unlikely to be corrupted together in the same way
The comparator applies checks to select the correct output
Coding
Self-checking circuitry
Reversal Checks Assumption: the specified function of the system is to compute a mathemathical function F and the function has an inverse function F’, such that F’(F(x))=x Check: let output = F(input). Compute F’(output) and verify that F’(output) = input
Specification checks (use the definition of “correct result”) Example: Specification: find the solution of an equation Check: substitute results back into the original equation
- Reasonableness Checks Divide by 0 Acceptable ranges of variables Acceptable transitions Probable results
…………..
Types of checks

## Slide 20: Active hw redundancy: the comparator
Problems
need to check if the output data are valid. The comparator may not be able to perform an exact comparison, depending on the application area (digital control applications)
faults in the comparator may cause an error indication when no error exists (false postive) or possible faults in duplicated modules are never detected (false negative)
Coverage
detects all single faults except those of the comparison element
Advantages
simplicity, low cost, low performance impact of the comparison technique, applicable to all levels and areas

## Slide 21: Active redundancy
2. Stand-by sparing (error detection, reconfiguration)
input
output
Module 1
Module 2
Module n
error detection
error detection
error detection
switch
.
.
.
Part of the modules are operational, part of the modules are spares modules (used as replacement modules)
The switch can decide no longer use the value of a module (fault detection and localization). The faulty module is removed and replaced with one of the spares.
hot spares the spares operate in synchrony with the on line modules, and they are prepared to take over
warm spares the spares are running but receive inputs only after switching
cold spares the spares are unpowered until needed to replace a faulty module
As long as the outputs agree, the spares are not used.

## Slide 22: Different schemes can be implemented
- A module is a duplex system, pairs connected by a comparator
- Duplex systems are connected to spares by a switch
- As long as the two outputs agree, or the comparator can detect the right value, the spare is not used. - Otherwise, the comparator signals the switch that it is not able to compute the right value and the switch operates a replacemnet using the spare.
input
output
Module 1
Module 2
switch
Module 1
Module 2
comparator
comparator
spare
Pair-and-spare approach
Pair results are used in a spare arrangment. Spare components at coarser granularity.
Not all four copies must be synchronised (only the two pairs)

## Slide 23: Hybrid approaches
Combine both the active and passive approaches
Very expensive in terms of the amount of hw required to implement a system
Applied in commercial systems, safety critical system (aviation, railways, …)
NMR with spares (Reconfigurable NMR):
Modules arranged in a voting configuration
- spares to replace faulty units
- rely on detection of disagreements and determine the module(s) not agreeing with the majority

## Slide 24: Reconfigurable NMR
N redundant module configuration (active modules)
Voter (votes on the output of active modules)
The Fault detection units 1) compares the output of the Voter with the output of the active modules 2) replaces modules whose output disagree with the output of the voter with spares
Fault detection
unit
SWITCH
(select N
out-of N+M)
output
Module 1
Module N
Spare
Module 1
Spare
Module M
Voter
. .
Active
units outputs
Disagreement
detection
. .
.
.
.
.
Reliablity as long as the spare pool is not empty
Coverage TMR with one spare can tolerate 2 faulty modules
(mask the first faulty module; replace the module; mask the second faulty module)

## Slide 25: Hw redundancy techniques: summary
Key differences
Passive: rely on fault masking
Active: rely on error detection, location and recovery
Hybrid: emply both masking and recovery
Passive provides fault masking but requires investment in hw (5MR can tolerate 2 faulty modules)
Active has the disadvantage of additional hw for error detection and recovery, sometimes it can produce momentary erroneous outputs
Hybrid techniques have the highest reliability but are the most costly (3MR with one spare can tolerate 2 faulty modules)

## Slide 26
INFORMATION REDUNDANCY

## Slide 27: Coding
Information is represented with more bits that strictly necessary: says, an n-bit information chunck is represented by
n+c= m bits
Among all the possible 2m configurations of the m bits, only 2n represent acceptable values (code words)
if a non-code word appears, it indicates an error in transmitting, or storing, or retrieving …
Parity code
for each unit of data, e.g. 8 bits, add a parity bit so that the total number of 1’s in the resulting 9 bits is odd
Set of
code words
Set of all
possible words
2n
2m
10100000 1
byte
parity
bit
10100100 1
not a codeword
communication
channel
sender node
receiver node
one bit flip
Two bit flips are not detected

## Slide 28: Coding
Separable code: a code in which the original information is appended with new information to form the codeword. The decoding process consists of simply removing the additional information and keeping the original data
Nonseparable code: requires more complicated decoding procedures
Parity code is a separable code
Additional information can be used for error detection and may be for error correction
Codes
encoding: the process of determining the c bit configuration for a n bit data item
decoding: the process of recovering the original n bit data from the m bit total bit

## Slide 29: Examples of codes
3-bit words – 4 code words
4-bit words – 8 code words
Parity-code
4-bit words – 8 code words
boxed words: code words
odd parity

## Slide 30: Examples of codes
m/n code: m bit equal to 1
4-bit words - 4 code words
2/4 code
CD - complemented duplication
4-bit words - 6 code words

## Slide 31: Distances and data spaces
Hamming distance between two data items: count the number of bits that are different
A code such that the Hamming distance between two code words is > k will detect all errors that flip up to k bits
Memories of computer systems. Parity bit added before writing the memory. Parity bit is checked when reading.
Useful distance measures depend on type of data and faults
Bank account numbers should be such that mistyping a digit does not credit the wrong account.
010
011
110
100
101
001
000
111
Parity-code: Hamming distance 2
undetectable
detectable

## Slide 32: Codes for error correction
correctable
correctable
uncorrectable
The corrupted data is closer to the correct data than to any other code word
Hamming distance 3:
detects 1 or 2 bits errors
correct 1 bit error
A code such that the minimum Hamming distance is k will detect up to k-1 single bit errors
Minimum Hamming distance: minimum distance between two code words
A code such that the minimum Hamming distance is k will correct up to d errors, where k = 2d +1

## Slide 33: Arithmetic codes
An arithmetic code guarantees that
if inputs are code words and the operation is performed correctly results are code words too
Arithmetic
operation
Implementation of the arithmetic operation (hardware or software) must be modified to operate on the code
The set of code words of an arithmetic code A is closed with respect to a specific set of operations.
A(b*c) = A(b) * A(c ) where * is one of a set of operations
3N codes
Multiply the data by 3 (this add 2 bits of redundancy)
Error checking is performed by confirming that the received word is divisible by 3

## Slide 34: Checksumming
applied to large block of data in memories
coverage: single fault
dn
dn-1
d2
d1
rn
rn-1
r2
r1
Original data
Received data
Checksum on
Original data
Checksum on
received data
Received version
of checksum
compare
checksum for a block of n words is formed by adding together all of the words in the block modulo-k, where k is arbitrary (one of the least expensive method)
- the checksum is stored with the data block
- when blocks of data are transferred (e.g. data transfer between mass-storage device) the sum is recalculated and compared with the checksum
- checksum is basically the sum of the original data
Code word = block + checksum

## Slide 35: Checksumming
Disadvantages
- if any word in the block is changed, the checksum must also be modified at the same time
- allow error detection, no error location: the detected fault could be in the block of s words, the stored checksum or the checking circuitry
- single point of failures for the comparison and encoder/detector element
Different methods differ for how summation is executed

## Slide 36: Error correcting codes -ECC
Two-dimensional parity
1 0 1 …. 0 1
0 0 1 …. 1 1
1 1 1 …. 0 0
1 0 0 …. 0 0
k words
n-bit words
column
parity
row
parity
Odd parity
0
parity error
parity error
Error location is possible for single-bit error: one error in the row parity vector, one error in the column parity vector
A single-bit error in the parity column or parity row column is detected
Single-error correcting code (SEC): detect and correct 1-bit error

## Slide 37: Hamming Code (I)
Parity bits spread through all the data word
Parity bit pj covers all bits whose position has the j least significant bit equal to 1
Each data bit is included in a unique set of 2 or more parity bits, as determined by the binary form of its bit position
Taken from: http://en.wikipedia.org/wiki/Hamming_code#Hamming_codes
Data bits
all other bit positions
(number the bit positions starting from 1: bit 1, 2, 3, etc..)
Parity bits
all bit positions that are powers of two : 1, 2, 4, 8, etc.

## Slide 38: Hamming code (II)
Parity bit p1 covers all bit positions which have the least significant bit set: bit 1 (the parity bit itself), 3, 5, 7, 9, etc.
Parity bit p2 covers all bit positions which have the second least significant bit set:
bit 2 (the parity bit itself), 3, 6, 7, 10, 11, etc.
Parity bit 4 covers all bit positions which have the third least significant bit set:
bits 4–7, 12–15, 20–23, etc.
Parity bit 8 covers all bit positions which have the fourth least significant bit set:
bits 8–15, 24–31, 40–47, etc.
Taken from: http://en.wikipedia.org/wiki/Hamming_code#Hamming_codes

## Slide 39: Hamming code (III)
Overlap of control bit: a data bit is controlled by more than one parity bits
Minimum Hamming distance: 3
Double-error detection code
Single-error correction code
SEC-DED code
Taken from: http://en.wikipedia.org/wiki/Hamming_code#Hamming_codes

## Slide 40: Self checking circuitry
Necessity of reliance on the correct operation of comparators and code checkers that are used as hard-core for fault tolerant systems
Self-checking circuit given a set of faults, a circuit that has the ability to automatically detect the existence of the fault and the detection occurs during the normal course of its operations
Typically obtained using coding techniques: circuit inputs and outputs are encoded (also different codes can be used)
Basic idea:
fault free + code input -> output: correct code word
fault + code input -> output: (correct code word) or (non code word)

## Slide 41: Self checking circuitry
Self-testing circuit: if, for every fault from the set, the circuit produces a noncode output for at least one code input (each single fault is detectable)
Fault-secure circuit: if, for every fault from the set, the circuit never produces a incorrect code output for a code input (i.e. correct code output or noncode output)
Totally self-checking (TSC): if the circuit is self-testing and fault-secure

## Slide 42: two-input TSC comparator
two signal input comparator (A, B)
output equal to 0 if inputs are equal; 1 otherwise
Fault assumption:
single fault
stuck-at-1/stuck-at-0 of each line in the circuit
Coding: 1/2 (dual-rail signal: coded signal whose two bits are always complementary)
A B C
0 0 0
0 1 1
1 0 1
1 1 0
A
B
C
A : A1 A2
0 : 0 1
1 : 1 0

## Slide 43: two-input TSC comparator
0
1
1
0
0
1
Taken from:[Siewiorek et al., 1998]
output 0 if inputs are equal; 1 otherwise
Fault free
A =0, B =1 different input
m=1, n =1, q=0
o = 0, p=1, r= 1
c2=0
c1=1
c1c2: code word
Output = c1 = 1 correct
1
1
0
1
0
1

## Slide 44: two-input TSC comparator
0
1
1
0
0
1
Taken from:[Siewiorek et al., 1998]
output 0 if inputs are equal; 1 otherwise
Faulty:
A=0, B=1 different input
m: stuck-at-0
c2 = 1
c1 = 1
c1c2: non code word
Output = error
1
1
0
1
0
1

## Slide 45: two-input TSC comparator
0
1
1
0
0
1
Taken from:[Siewiorek et al., 1998]
output 0 if inputs are equal; 1 otherwise
Faulty:
A=0, B=1 different input
m: stuck-at-1
c2=0
c1=1
c1c2: code word
output = c1 = 1 correct
1
1
1
0
1
0

## Slide 46: two-input TSC comparator
For each fault, there exists at least one input configuration such that the output is a non code word
If the output is a code word, the output is correct
Taken from:[Siewiorek et al., 1998]

## Slide 47: n-input TSC comparator
n-input TSC comparator: tree of two input self checking comparators

## Slide 48
TIME REDUNDANCY

## Slide 49: Time redundancy techniques (I)
Attempt to reduce the amount of extra hw at the expense of using additional time
Repetition of computations
- compare the results to detect faults
- re-execute computations (disagreement disappears or remains)
good for transient faults no protection against permanent fault - problem of guaranteeing the same data when a computation is executed
Computation
Computation
Encode
Data
Decode
result
Store
result
Compare
results
Store
result
time t0
time t0+d
Data
Data
error

## Slide 50: Time redundancy techniques (II)
Use a minimum of extra hw to detect also permanent faults - encode data before executing the second computation
Example: data transmitted over a parallel bus
- stuck at of a line of the bus
t0: transmit original data
t0+d : transmit complement data
When a fault occurs: received data not complements of each other
t0 : 1 0 1 1 -> 1 0 0 1
t0+d : 0 1 0 0 -> 0 1 0 0
Transmission error free, each bit line alternate between a logic 1 and a logic 0 (alternating logic)
line stuck at 0

## Slide 51
SOFTWARE REDUNDANCY

## Slide 52: Faults in the software
Software is subject to
design flaws: - mistakes in the interpretation of the specification that the software is supposed to satisfy (ambiguities) - mistakes in the implementation of the specification: carelessness or incompetence in writing code, inadequate testing
operational faults: incorrect or unexpected usage faults (operational profile)
sw
input
output

## Slide 53: Faults in the software
Design flaws:
  hard to visualize, classify, detect, and correct.
  closely related to human factors and the design process, of which we don't have a solid understanding
only some type of inputs will exercise that fault to cause failures. Number of failures depend on how often these inputs exercise the sw flaw
apparent reliability of a piece of software is correlated to how frequently design faults are exercised as opposed to number of design faults present

## Slide 54: Software redundancy
Due to the large cost of developing software, most of the software dependability effort has focused on
fault prevention techniques and testing strategies
Multi-version approaches
replicate the software mainly used in safety-critical systems (due to cost)

## Slide 55: Multi-version approaches
Software diversity
a simple duplication and comparison procedure will not detect software faults if the duplicated software modules are identical
Independent generation of N >= 2 functionally equivalent programs, called versions, from the same initial specification.
Upon disagreement among the versions?
- retry or restart (fault containment)
- trasition to a predefined safe state
- reliance on one of the versions

## Slide 56: N-version programming (I)
independently developed versions of design and code
Technique: independent design teams using different design methodologies, algorithms, compilers, run-time systems and hardware components
- vote on the N results produced
Program
Inputs
Program
Inputs
Program
Version 1
Program
Version N
Program
Version 2
Voter
Program
Outputs
.
.
.
.

## Slide 57: N-version programming (II)
Disadvantages
-cost of software development
-cost of concurrent executions -potential source of correlated errors, such as the original specification. Specification mistakes: not tolerated
Practical problem
in implementing the software Voter for comparing the results generated by the copies because of the differences in compilers, numerical techniques and format conversions.

## Slide 58: N-version programming (II)
Software voter (single point of failure)
not replicated: must be simple and verifiable
must assure that the input data vector to each of the versions is identical
must receive data from each version in identical formats or make efficient conversions must implement some sort of communication protocol to wait until all versions complete their processing or recognize the versions that do not complete

## Slide 59: N-self-checking programming
N versions of the program are written
each version is running simultaneously and includes its acceptance tests
The selection logic chooses the results from one of the programs that passes the acceptance tests
Tolerates N-1 faults (independent faults)
Program
Version 1
Program
Version N
Acceptance
tests
Accepptance
tests
Selection
Logic
.
.
Program
Inputs
Program
Outputs
Program
Inputs
based on acceptance tests rather than comparison with equivalent versions

## Slide 60: Design diversity
Cannot adopt the hardware analogy and assume versions fail independently
Empirical evidence that there will be common faults There is evidence that diversity delivers some improvement over single versions
Related faults may result from dependencies in the separate designs and implementations (example: specification mistakes)
Design diversity

## Slide 61: Design diversity
Functional diversity
Assign to independent software versions diverse functions that compute the same task
For example, in a plant, diverse measurement signals, actuators and functions exists to monitoring the same phenomenon
Diverse functions
for example, functions that ensure independently that the plant safety targets are met.

## Slide 62: Recovery-block technique
Basic structure: Ensure T By P
else by Q
else error
Accettability of the result is decided by an acceptance test T. Primary alternate P, secondary alternates Q
variables global to the block automatically checkpointed if they are altered within the block
the primary alternate is executed and subjected to an acceptance test to detect any error in the result. If the test is passed, the block is exited; otherwise the content of the recovery cache pertinent to the block is reinstated, and the second alternate is executed.
This cycle is executed until either an alternative is successful or no more alternatives exist. In this last case an error is reported.
checkpoint
Acceptance
test
based on an one acceptance test and a single alternate is run at a time

## Slide 63: Recovery-block technique
Combines elements of checkpointing and backup
Primary
Version
Secondary
Version N-1
Secondary
Version 1
Program Outputs
.
.
.
.
Program Inputs
N-to-1
Program
Switch
Acceptance
Tests
Test Result
- checkpoint: a copy of the current state for possible use in fault tolerant techniques
- releases the programmer from determining which variables should be checkpointed and when
- linguistic structure for recovery blocks requires a suitable mechanism for providing automatic backward error recovery.

## Slide 64: Checkpointing: basic issues
- may be taken automatically (periodically) or upon request by program
- resetting the system and process state to the state stored at the latest checkpoint needs mechanisms in run-time support (rollback)
- need to be correct (consistency of checkpoints)
- need eventually to be discarded
- overhead of saving system state (minimize the amount of state information that must be saved)
x
1
2
3
a
b
4
5
c
6
d
Process A
Process B
Process C
e
Checkpoint
x
Error
Message passed
domino effect

## Slide 65: Effectiveness of fault tolerance
Example: Stable storage
RAID (Redundant Arrays of Independent Disks) technology
disk organization techniques that manage a large numbers of disks, providing a view of a single disk of high capacity and high speed by using multiple disks in parallel, and high reliability by storing data redundantly

## Slide 66: Magnetic disk
Read failure
  To deal with read failure, computes and attaches checksums to each sector to verify that data is read back correctly
  If data is corrupted, with very high probability stored checksum won’t match recomputed checksum
Write failure
  Ensure successful writing by reading back sector after writing it

## Slide 67: RAID
Redundant information stored on multiple disks to recover from failures
Mirroring
Coding: Block-Interleaved Parity
Disk
Mirrored Disk
block 8
block 4
block 0
block 9
block 5
block 1
block 10
block 6
block 2
block 11
block 7
block 3
parityblock 8-11
parityblock 4-7
parityblock 0-3
Block-level striping
Parity block on a diferent disk for toleranting disk failure

## Slide 68: RAID
block 17
block 13
block 16
block 12
block 18
block 14
block 19
parityblock 11-15
parityblock 15-19
block 8
block 4
parityblock 0-3
block 15
block 9
parityblock 4-7
block 0
parityblock 8-11
block 5
block 1
block 10
block 6
block 2
block 11
block 7
block 3
Coding: Block-Interleaved Distributed Parity

## Slide 69: RAID
…
Disk1
Disk2
Disk7
Disk8
1 0 0 0 1 1 0 1
Byte
0 0 1 0 0 1 1 1
Byte
10
00
Disk1
Disk2
Disk3
Disk4
10
00
Disk5
Disk6
Disk7
Hamming(7, 4)
Coding: Hamming code
Bit-level striping

## Slide 70: Conclusions
Fault tolerance uses replication for error detection and system recovery
Fault tolerance relies on the independency of redundancies with respect to the process of fault creation and activations
Fault masking will conceal a possibly progressive and eventually fatal loss of protective redundancy
Practical implementations of masking generally involve error detection (and possibly fault handling), leading to masking and error detection and recovery

## Slide 71: Conclusions
When tolerance to physical faults is foreseen, the channels may be identical, based on the assumption that hardware components fail independently
When tolerance to design faults is foreseen, channels have to provide identical service through separate designs and implementation (through design diversity)