## Slide 1
Cinzia Bernardeschi
Department of Information Engineering
University of Pisa
cinzia.bernardeschi@ing.unipi.it
Dependability:basic concepts and definitions

## Slide 2
is a global concept that subsume the usual attributes of reliability, availability, ... (justifiably trusted service)
cover the entire range of computing and communication systems, from individual logic gates to network of computers with human operators and users (computer-based systems)
Dependability

## Slide 3
System function what the system is intended for. It is given by the input-otput relation
Basic concepts
System service the system service is the behaviour of the system as it is perceived by its user(s) - correct if the delivered service fulfills the system function - incorrect otherwise
system
input
output

## Slide 4
The threats to dependability
System failure a system failure occurs when the system service deviates from fulfilling the system function
Error:
that part of the system state which is liable to lead to subsequent failure. An erroneous state may be exited before leading to failure
Fault:
the adjudged or hypothesized cause of an error physical defect, imperfection, logical flaws in some hw/sw component

## Slide 5
A fault is active when it produces an error:
- an internal fault which was previously dormant and which has been activated by the computation process
- an external fault, for example, a violation of the operating procedure
An error may be latent or detected:
- latent when it has not been recognised
- detected by a detection algorithm or mechanism (ERROR DETECTION)
Fault latency the length of time between the occurrence of a fault and the appearance of an error due to that fault
Error latency the length of time between the occurrence of an error and the appearance of the resulting failure
Faults/Errors

## Slide 6
A failure occurs when an error passes through the system user interface and affects the service delivered by the system
Component failure fault for the system which contains the component and is seen by the other components with which it interacts
The failure modes of the failed component become fault types for the components interacting with the failed component
Chain of faults / errors / failures
fault  error  failure
|
fault  error  failure

## Slide 7
Assume the sensor reporting the speed at which the main turbine is spinning breaks, and reports that the turbine is no longer spinning.
The failure of the sensor injects a fault (incorrect data) into the system.
 This fault causes the system to send more steam than required to the turbine (error), thus over-speeding the turbine and activating the safety mechanism that shuts down the turbine to prevent damaging it.
Example
sensor
Control system
hw fault
sensor failure
incorrect data
control system fault

## Slide 8
Fault-tolerant system System that can continue to deliver a correct service in the presence of hw/sw faults
System repair
a transition of the system from incorrect to correct service
Time to failure measure of the time between two failures Expected value of the time to failure is referred to as Mean Time To Failure (MTTF)
Time to repair
measure of the time to repair Expected value of the time to repair is referred to as Mean Time To Repair (MTTR)

## Slide 9
Reliability: continuity of correct service a measure of the continuous delivery of correct service the reliability of a system as a function of time, R(t), is the conditional probability that the system performs correctly throughout the interval of time [t0, t], given that the system was performing correctly at time t0.
Availability: readiness for correct service a measure of the alternation between delivery of correct service and imcorrect service the availability of a systems as a function of time, A(t), is the probability that the system is operating correctly and is available to perform its functions at the instant of time t.
Dependability attributes
A. Avizienis, J.C. Laprie, B. Randell, C.E. Landwehr. Basic Concepts and Taxonomy of Dependable and Secure Computing. IEEE Trans. Dependable Sec. Comput. 1(1): 11-33 (2004)

## Slide 10
Safety: absence of catastrophic consequences on the users and the environment a measure of the time to catastrophic failure the safety of a systems as a function of time, S(t), is the probability that no catastrophic failures occur during [t0, t]
Integrity: absence of improper system alterations
Maintainability: ability to undergo modifications and repairs a measure of the time to restoration
Confidentiality: the absence of unauthorised disclosure of information

## Slide 11
Security is a composite of the attributes of confidentiality, integrity, and availability
- availability for authorised actions only
- confidentiality
- integrity with “improper” meaning “unauthorised”
Security

## Slide 12
Safety critical systems systems in which the computer is serving a critical function that cannot be suspended even for the duration of a repair (as in railway-signalling control systems, flight computers on aircrafts, ...)
we need to have sufficient confidence that the system will fail - sufficiently infrequently or
- with sufficiently low probability during a particular length of time
Examples of Reliability requirements in safety critical systems
- less than 10-9 “catastrophic failure conditions” per hours of operation (excluding sw faults) in civil transport airplanes
- less than 10-12 per hours for urban trains
- ............
Safety critical systems
From: B. Littlewood, L. Strigini, “Validation of ultra-high dependability for software-based systems”, ACM, 1993.

## Slide 13
resilience builds on the initial definition of dependability and cover the ability to successfully accommodate unforeseen environmental perturbations or disturbances
A shorthand definition of Resilience is:
- the persistence of dependability in spite of continuous changes
Resilience
consider large, networked, evolving, systems either fixed or mobile, with demanding requirements driven by their domain of application
Ubiquitous systems

## Slide 14
The term refers to the explicit use of resilience information (metadata) during systems development or within the running system. -> development of techniques and design processes that treat resilience explicitly.
The resilience-explicit computing approach will involve
collecting and manipulating dependability and security meta-data
representation and selection of explicit resilience policy at run-time
Applications may use the metadata provided by monitoring services to implement their own policies, e.g., by selecting resources based on reliability metrics
Resilient-Explicit Computing
ReSIST NoE – Resilience for Survaivability in IST – A European Network of Excellence
Resilence Knowledge Base: incorporate a representation of the relationships amongst the various dependability and security terms
Resilience Ontology:a dependability and security ontology

## Slide 15
Faults and their manifestations

## Slide 16
CAUSE
  Component defects
manufacturing imperfections/ component wear-out / electronic components corrosion of the metal
  External disturbance
radiation / electromagnetic interference / operator mistakes
  Specification mistakes
hw specification /sw specification/ incorrect algorithms
  Implementation mistakes implementation is the process of transforming hw specs into the physical hw and sw specs into the code
Characteristics of faults: CAUSE / EXTENT / NATURE / DURATION

## Slide 17
According to their CAUSE, we distinguish between
  independent faults attributed to different causes
  related faults - attributed to a common cause single power supplies, clocks, specifications, …
EXTENT
Specifies whether the fault is localised to a given hw or sw module or globally affects the hw, the sw, or both
NATURE (the type of fault)
  Hw fault
fault in the analog/digital circuitry
  Sw fault
incorrect hw/sw designs or coding mistakes

## Slide 18
DURATION (the length of time a fault is active)
Permanent a continuous and stable fault. It remains in existence if no corrective action is taken
 Reflects an irreversible physical change or inadequacy in the design of the system
An example of a permanent fault would be a VLSI chip with a manufacturing defect, causing one input pin to be stuck high.
  Transient a fault that can appear and disappear within a very short period of time
 From temporary enviromental conditions or some design faults.
For example, a voltage spike might cause a sensor to report an incorrect value for a few milliseconds before reporting correctly

## Slide 19
  Intermittent a fault that appears, disappears and then reappears repeatedly
 It is a fault that is occasionally present due to unstable hw or varying hw/sw states. (a function of load activity or inadequacy in the design of the system)
Intermittent/Transient faults mainly differ for the possibility of applying repair
Intermittent faults are potentially detectable and repairable by replacement or redesign
Transient faults are due to temporary enviromental conditions and are incapable of repair (the hw is physically undamaged)

## Slide 20
Characteristics of failures:
DOMAIN / USER PERCEPTION / SEVERITY
Failure mode of the system or of a component of the system
DOMAIN
  value failures
  timing failures
USER PERCEPTION
  all users perceive consistent failures
  users perceive inconsistent failures (Byzantine failures)

## Slide 21
SEVERITY (CONSEQUENCES UPON THE SYSTEM ENVIRONMENT)
  benign failures consequences of the same order of magnitude of the benefit from the service
  catastrophic failures
Temporal relationship between multiple failures:
  Simultaneous failures within some predefined time window
  Sequential failure

## Slide 22
Systems hierarchy to manage complexity of computer systems
Different dimensions of a reliability framework:
- physical levels in a digital system
- time in the system’s life (from concepts through manufacturing and operation)
Reliable Computer Systems.
D. P. Siewiorek R.S. Swarz, Prentice Hall, 1992
Computer designers and programmers would be students of reliability and so do computer system users

## Slide 23
Physical levels in a digital system
Circuit level
resistors, capacitors, inductors, power sources, diodes transistors
Logic level
Switching circuit
Flip-flops, latches, gates, ...
Register transfer
Data registers, operators... Hardwired control and microprogramming
Program level
High-level language
Software: operating systems, application systems
ISP (assembler)
memory state, instruction state, address calculation, ...
PMS (Processor, Memory, Switch)
i/o devices, memory, processor, communications (complete system)

## Slide 24
Time in the system’s life
Specification and design
Prototype
Manufacture (HW)
Code (SW)
Installation
Operational life
Error sources
Algorithm design, formal specification
Algorithm design Wiring and assembly
Assembly Component failure
Component failure Operator errors
Environmental fluctuation
Wiring and assembly Component failure
Code generation Interpretation of the spec

## Slide 25
Physical
defect
Incorrect
design
Unstable
environment
Unstable
hardware
Operator
mistake
Transient
fault
Intermittent
fault
Permanent
fault
Errors
Service
failures
In Reliable Computer Systems.
D. P. Siewiorek R.S. Swarz, Prentice Hall, 1992
Possible source of errors and service failure

## Slide 26
Failure rate distributions

## Slide 27
Hardware Reliability
Software Reliability
System Reliability
Software and hardware have basic differences that make them different in fault causes and failure mechanisms.
Reliability

## Slide 28
Consider the time to failure of a system or component. It is not exactly predictable - random variable.
Approaches to quantitative evaluation of failure rate, Mean Time To Failure (MTTF), Mean Time To Repair (MTTR), reliability analysis, availability analysis, maintainability, safety, …
Quantitative evaluation of Reliability
probability theory

## Slide 29
Reliability of a component
X a random variable representing the time to failure of a component
FX(t) cumulative distribution function FX(t) = P(X <= t)
Reliability of the component at time t is given by
RX(t) = P[X > t] = 1 –P[X <= t] = 1 –FX (t)
Unreliability of the component at time t is given by
QX(t) = P[X <= t] = FX (t)
Failure rate at time t probability that a component that has not yet failed, fails in the interval (t, t+t) as t->0
zX(t) = P[X(t, t+t) | X>t] hazard rate function

## Slide 30
Hardware
Failure rate is dependent upon time; however electronic components have a period where z(t) is constant z(t) is assumed to have constant value in the useful life period
 generally given in number of failures for hours = 1/2000, then one failure every 2000 hours
if z(t) = then
R(t) = e –t
the exponential relation between reliability and time is known as exponential failure law
Hazard function = z(t) = 
Reliability function = R(t) = e –t

## Slide 31
1. Design Maturity Testing estimate the mean time to faiure (MTTF) for a new product before the product is committed (a set of devices are observed for a prolonged time)
2. Incoming Inspection attempt to cull weak or defective components prior to assembly into subsystems (bathtub-shaped curve, infant mortality period)
3. Process Maturity Testing (PMT)
- assembler, fabricate, inspect, test newly manufactured products that may contain some latent defects built in by the process that produced them (infancy for the device)
Manufacturing stage

## Slide 32
Hardware
Distribution models for permanent faults
MIL-HBDK-217 (Department of Defence) is a model for chip failure. Statistics on electronic components failures are studied since 1965 (periodically updated).
Typical component failure rates in the range 0.01-1.0 per million hours.
Failure rate for a single chip :
= τLτQ(C1τT τV + C2τE)
τL = learning factor, based on the maturing of the fabrication process
τQ = quality factor, based on incoming screening of components
τT = temperature factor, based on the ambient operating temperature
and the type of semiconductor process
τE = environmental factor, based on the operating environment
τV = voltage stress derating factor for CMOS devices
C1, C2 = complexity factors, based on the number of gates, or bits for
memories in the component and number of pins.

## Slide 33
Commercially available databases - Military Handbook 217 - Telcordia, - PRISM User’s Manual, - International Eletrotechnical Commission (IEC) Standard 61508
- PDS method ..............

## Slide 34
Software Reliability
What is software reliability?
the probability of failure-free software operation for a specified period of time in a specified environment
sw
input
output
Software is subject to
design flaws: - mistakes in the interpretation of the specification that the software is supposed to satisfy (ambiguities) - mistakes in the implementation of the specification: carelessness or incompetence in writing code inadequate testing
incorrect or unexpected usage faults (operational profile)

## Slide 35
Design faults are hard to visualize, classify, detect, and correct.
Design faults are closely related to human factors and the design process, of which we don't have a solid understanding
Software Faults

## Slide 36
Software Failures
a flaw not discovered and corrected during testing, may possibly lead to a failure during system operation
if the sw has faults only some type of inputs will exercise that fault to cause failures
number of failures depend on how often these inputs exercise the sw
-> Apparent reliability of a piece of software is correlated to how frequently design errors are exercised as opposed to number of design faults present
there are also software failures caused by hardware faults

## Slide 37
The failure behaviour of sw is primarly controlled by two factors:
the number of faults in the sw being evaluated The higher the number of faults, the higher the probability that the system will fail within time t
the operational profile of the execution The failure of software also depends on the environment in which it is executing
The observation of failures occurs as a random process

## Slide 38
Software reliability is not a direct function of time. Electronical and mechanical parts may become old, and wear-out with time and usage. Software DOES NOT wear-out during its life. Software DOES NOT change over time unless intentionally changed or upgraded
As a software is used, design faults are discovered and corrected. Consequently, the reliability should improve, and the failure rate should decrease BUT corrections could cause new faults
Software Reliability

## Slide 39
SOFTWARE RELIABILITY EVOLUTION
identify periods of reliability growth and decrease
upgrades imply feature upgrades, not upgrades for reliability.
From “Software Reliability”,
J. Pan, Carnegie Mellon University, 1999

## Slide 40
in the last phase, software does not have an increasing failure rate as hardware does. In this phase, software is approaching obsolescence; there are no motivations for any upgrades or changes to the software. Therefore, the failure rate will not change.
in the useful-life phase, software will experience a drastic increase in failure rate each time an upgrade is made. The failure rate levels off gradually, partly because of the defects found and fixed after the upgrades.
Even bug fixes may be a reason for more software failures, if the bug fix induces other defects into software
SOFTWARE RELIABILTY EVOLUTION

## Slide 41
From “Software Reliability”, J. Pan, Carnegie Mellon University, 1999
Reliability upgrades drop in software failure rate, if redesign or
reimplementation of some modules with better engineering approaches

## Slide 42
Modeling techniques based on observing and accumulating failure data and analyzing them with statistical inference
Software Reliability models
Experimental evaluation of dependability
FAULT INJECTION / MONITORING / ANALYSIS OF DATA

## Slide 43
operational phase monitor computer errors and failures and analyse measured data to quantify system dependability characteristics
  Error-logging software in operating systems - information on transient errors, automatic recovery ...
  Human-manual logging
- information on failure diagnosis, ...
MONITORING
ANALYSIS OF DATA
Statistical techniques used in the analysis of data obtained from fault injection or from operational system monitoring
Collected data and experience are valuable guides to know what is the valuable fault model at each level

## Slide 44
monitoring and recording naturally occurring errors and failures in the system while it is running under user workloads
analysis of such measurements can provide valuable information on actual error/failure behaviour and all measurable dependability metrics (failure and recovery rates, reliability, availability)
BUT
the analysis is limited to detected errors
Operational phase

## Slide 45
A global software reliability analysis method
(From Karama Kanoun, ReSIST network of Excellence Courseware “Software Reliability Engineering”, 2008 http://www.resist-noe.org/)

## Slide 46
Summary
For Hardware
databases with reliability parameters are widely used
databases must be studied to analyze their capability to provide failure rates and they should be used with caution
need to combine data from different sources to estimate reliability parameters
-> Failure rate estimate using Hierarchical Bayesian method

## Slide 47
Due to the nature of software, no general accepted mechanisms exist to predict software reliability before the software is built
Important empirical observation and experience
Good engineering methods can largely improve software reliability
Software testing serves as a way to measure and improve software reliability
Unfeasibility of of completely testing a software module: defect-free software products cannot be assured
Databases with software failure rates are available but numbers should be used with caution and adjusted based on observation and experience
For Software

## Slide 48
Dependability and security tree
From: A. Avizienis, J.C. Laprie, B. Randell, C.E. Landwehr. Basic Concepts and Taxonomy of Dependable and Secure Computing.IEEE Trans. Dependable Sec. Comput. 1(1): 11-33 (2004)

## Slide 49
From: A. Avizienis, J.C. Laprie, B. Randell, C.E. Landwehr. Basic Concepts and Taxonomy of Dependable and Secure Computing.IEEE Trans. Dependable Sec. Comput. 1(1): 11-33 (2004)
Fault / error/ failure chain

## Slide 50
Means to attain dependability

## Slide 51
combined use of methods classified into:
    1. fault prevention avoid the the introduction of faults 2. fault tolerance tolerate faults providing a service complying with the specification in spite of faults (“prevent system failures” )
3. fault removal
reduce the presence of faults (number,seriouness, ...)
4. fault forecasting
estimate the present number, the future incidence and the consequences of faults
The means to attain dependability

## Slide 52
Fault prevention

## Slide 53
Fault prevention techniques
are intended to keep faults out of the system
Prevention of development faults is an an obvious aim for development methodologies both for software and hardware
  Software quality - Rigorous development process (information hiding, modularization, use of strong typed programming languages, ......)
  Reliable Hw
Application of formal methods as fault prevention technique

## Slide 54
Formal methods
are a fault avoidance technique which can increase dependability by removing errors at the requirements, specification and design stages of development
can deliver correctness (that is adherence to some requirements)
formal methods can deliver correctness in presence of anticipated faults

## Slide 55
in addition to the standard behaviour of the system, faults and failure modes must be modeled
Different approaches in the literature
- standard process algebras (equivalence relations)
- (ad hoc) process algebras and bisimulation relations
- model checking
- traces and FDR
- theorem proving
- program transformations
- temporal logics
- ……..
Formal methods /faults /failures
A. Francalanza, M. Hennessy. “A theory of system behaviour in the presence of node and link failure” Inf. Comput. 206(6): 711-759, 2008
K. Björkman et al., Verification of Safety Logic Design by Model Checking, NPIC&HMIT, 2009.

## Slide 56
Assumption:
consider a set of anticipated faults
-> study fault tolerance to these faults
Problems:
- monotonicity having proved that the system tolerates several faults, the system tolerates any combination of them
- state explosion
- faults and failure modes
- module duplication due to fault tolerant techniques
Formal methods/faults/ failures

## Slide 57
Given two processes P and Q, they are called observational equivalent
if and only if a weak bisimulation exists which relates the initial states of the LTSs which describe their behaviour and we write P  Q.
P = system function (correct behaviour)
Q = system behaviour under a set of anticipated faults
Q  P means that no observer can distinguish between the two processes, despite Q being affected by faults
is observational equivalence between the behaviour of the fault free system and that of the system affected by faults a good relation?
-> Bisimulation is not fault-monotonic
T. Janowski. On Bisimulation, Fault-Monotonicity and Provable Fault-Tolerance. Proc. 6-th Int. Conference on Algebraic Methodology and Software Technology, LNCS 1349, 1997.
Process algebras & observation equivalence

## Slide 58
Example: the alternating bit protocol
Scope of the protocol: reliable communication over a medium which may omit messages
P = ?in.!out.P
S: Sender R: Receiver A, B channels
L= {a, b, c, d}: internal channels
Bit value i and i: control the flow of messages and acknowledgements
Q (S | A | B | R)/L
anticipated faults MAY or MAY not occur
-> anticipated faults MUST NOT occur
S, R, A, B fault-free
P Q
S, R, A, B with faults
S, R with faults A, B fault-free
P Q
P Q

## Slide 59
duplication
omission

## Slide 60
Fault tolerance

## Slide 61
Fault tolerance techniques
ability of the system to deliver a correct service after the occurrence of faults (failure avoidance)
Why fault tolerance techniques?
even with the most careful fault avoidance, faults will eventually occur and result in a system failure
Fault tolerance
carried out via error detection and system recovery, fault masking (systematic usage of compensation)
Redundancy
Can have a very important impact on a system in the area of performance, size, weight, power consumption and others
Fault tolerant techniques use redundancy to counteract the effects of faults

## Slide 62
From: A. Avizienis, J.C. Laprie, B. Randell, C.E. Landwehr. Basic Concepts and Taxonomy of Dependable and Secure Computing.IEEE Trans. Dependable Sec. Comput. 1(1): 11-33 (2004)

## Slide 63: Redundancy
HARDWARE REDUNDANCY
Physical replication of hw (the most common form of redundancy)
The cost of replicating hw within a system is decreasing because the costs of hw is decreasing
INFORMATION REDUNDANCY
Addition of redundant information to data in order to allow fault detection and fault masking
TIME REDUNDANCY
Attempt to reduce the amount of extra hw at the expense of using additional time
SOFTWARE REDUNDANCY
Fault detection and fault tolerance implemented in sw

## Slide 64
HARDWARE REDUNDANCY

## Slide 65
Hardware redundancy
Passive techniques
- use fault masking to hide the occurrence of faults
- rely upon voting mechanisms to mask the occurrence of faults
- do not require any action on the part of the system / operator
- generally do not provide for the detection of faults

## Slide 66
Triple Modular Redundancy (TMR) fault masking
Module 1
Module 3
Module 2
Voter
output
(From Design and Analysis of Fault-tolerant Digital Systems
B. W. Johnson, , Addison-Wesley 1989)
Triplicate the hw (processors, memories, ..) and perform a majority vote to determine the output of the system
 effects of faults neutralised without notification of their occurrence
 masking of a failure in any one of the three copies
Sometimes some failures in two or more copies may occurr in such a way that an error is avoided:
Example
- stuck at 1 in a module line; stuck at 0 in another copy; the voted result is correct (compensating failures)
- failure at location 127 in a memory; failure at location 10 in another copy; the voted result is correct

## Slide 67
processor 1
processor 3
processor 2
Voter
Voter
Voter
memory 1
memory 2
memory 3
(From Fault-Tolerant Computer System Design
D. K. Pradhan, Prentice Hall, 1996)
Difficulties:
Delay in signal propagation:
- due to the voter
- due to multiple copies synchronisation
Trade-off the achieved fault tolerance vs the hw required
Voter: if the Voter fails, the complete system fails  Voter is a single point of failure
Triple Modular Redundancy (TMR)
Triplicated Voters in a TMR configuration

## Slide 68
Problems with voting procedure:
- hardware Voter or software Voter?
- the three results may not completely agree
for example, analog to digital converters could produce a result which differs for the least-significant bit even if the exact signal is passed through the same converter
mid-value select technique choose a value from the three selecting the value that lies between the remaining two
other techniques .....
N-Modular Redundancy with Voting
- n is made an odd number
- more module faults can often be tolerated
- 5MR tolerates two module faults
Triple Modular Redundancy (TMR)

## Slide 69
Hardware redundancy
Active techniques (dynamic approach)
- fault detection, location and recovery
- detect the existence of faults and perform some actions to remove the faulty hw from the system
- require the system to perform reconfiguration to tolerate faults
- common in applications where temporary, erroneous results are acceptable while the system reconfigures (e.g. satellite systems)

## Slide 70
Comparator
Error signal
Module 1
Module 2
output
input
 no method for determining which component is faulty
- two identical pieces of hw are employed
- they perform the same computation in parallel
- when a failure occurs, the two copies are no more identical and a simple comparison detects the fault
Duplication with comparison scheme - fault detection

## Slide 71
Problems:
related faults in duplicated modules are never detected (independent failure assumption is reasonable for hw)
the comparator may not be able to perform an exact comparison, depending on the application area (digital control applications)
faults in the comparator may cause an error indication when no error exists
incomplete use of the resource (example, duplicated computer, two processors performing the same task with loss of half the available computing power)
Advantages:
Simplicity, low cost, low performance impact of the comparison technique, applicable to all levels and areas
Coverage:
 detects all single faults except those of the comparison element
Duplication with comparison

## Slide 72
One module is operational, while one or more modules serve as spares
When a fault is detected and located, the faulty module is removed and replaced with one of the spares.
hot standby sparing: the spares operate in synchrony with the on line modules, and they are prepared to take over at any time
cold standby sparing: the spares are unpowered until needed to replace a faulty module
 power consumption vs time to perform initialization prior to bringing the module into active service
Standby sparing

## Slide 73
Comparator
input
Reconfiguration
unit
output
Module 1
Module 2
Spare
Module 1
Error report
Pair-and-a-spare approach fault detection, location and recovery
Two modules operate in parallel at all times and their results are compared to provide the error detection capability
Reconfiguration process can be viewed as a switch that accepts the module’s outputs and error reports, and provides the comparator with the output of two modules.
As long as the two outputs agree, the spares are not used. When a miscompare occurs, the switch uses the error reports from the modules to first identify the faulty module and then select a replacement module. Both modules are replaced if the faulty module is not identified (two spare are needed)
combines duplication with comparison and standby sparing

## Slide 74
Hardware redundancy
Hybrid techniques
Combine both the active and passive approaches
Very expensive in terms of the amount of hw required to implement a system
Applied in safety critical applications in which fault masking is required to prevent momentary errors and high reliability must be achieved

## Slide 75
NMR with spares (Reconfigurable NMR):
- modules arranged in a voting configuration
- spares to replace faulty units
- rely on detection of disagreements and determine the module(s) not agreeing with the majority
TMR with one spare:
Mask the first module fault; after replacement, mask the second module fault
Passive NMR:
Requires 5 modules to provide fault tolerance to two module faults

## Slide 76
Fault detection
unit
input
Reconfiguration
Unit
(select N
out-of N+M)
output
Module 1
Module N
Spare
Module 1
Spare
Module M
Voter
. .
. .
Active
units outputs
Disagreement
detection
. .
. .
.
.
.
.
NMR with spares
(From Design and Analysis of Fault-tolerant Digital Systems
B. W. Johnson, , Addison-Wesley 1989)

## Slide 77
Key differences
Passive: rely on fault masking
Active: rely on error detection, location and recovery
Hybrid: emply both masking and recovery
Passive provides fault masking but requires investment in hw
Active uses less hw but has the disadvantage of producing momentary erroneous outputs
Highest reliability using hybrid techniques which are the most costly
Hw redundancy techniques: differences

## Slide 78
INFORMATION REDUNDANCY

## Slide 79
Information redundancy techniques
mapping data into new representations containing redundant information
Code: a means of representing data using a set of rules
binary code: code in which the symbols representing data are 0 / 1
encoding : the process of determining the corresponding codeword for a particular data item
decoding: the process of recovering the original data from the codeword
Error-detecting and correcting codes
create a binary code for which the code words are a subset of the total combination of 0 / 1
basic idea of error-detecting codes: errors introduced into a codeword will force it in the range of illegal combinations
basic idea of error-correcting codes: the codeword is structured so that it is possible to determine the correct codeword from the corrupted one
e.g. single-bit (double-bit, …) error detecting/correcting codes

## Slide 80
Information redundancy techniques
Set of
code words
Set of all
possible combinations
Separable code: a code in which the original information is appended with new information to form the codeword. The decoding process consists of simply removing the additional information and keeping the original data
Nonseparable code: requires more complicated decoding procedures
Metric relative to code efficiency:
the ratio of the number of code words to the total number of possible combinations
Hamming distance, the number of bit positions on which two codewords differ
Distance of a code is the minimum Hamming distance Represents the number of independent, single bit errors that the code can detect
distance 2: detects 1 bit error
e.g. Assume two bits and let 00 be a codeword. The unique other codeword is 11. 01 and 10 are not codewords
distance 3: detects 1 or 2 bit error correct 1 bit error

## Slide 81
Parity codes
010
011
110
100
101
001
000
111
Parity codes: single bit parity codes require the addition of an extra bit to a binary word such that the resulting codeword has either an even or an odd number of 1
odd parity: all code words have an odd number of 1
(see the boxed words in figure)
The minimum distance between code words is 2
Any distance of 1 results in a non codeword, this represents single bit errors
 any single error is detectable
 no double bit errors are detectable
even parity: non boxed words, another code with the same coverage
Memories of computer systems. Parity bit added before writing the memory. Parity bit is checked when reading.

## Slide 82
M-of-N codes
Codewords of n bits
m and only m bits are 1
conceptual simplicity
 encoding, decoding and detection difficult to perform
Easiest way (separable code): i-of-2i code
i bits of information
append i bits such that exactly i 1
 codewords: 2i bits
encoding: counting the number of 1; look in a table the bits to append
decoding: remove the appended bits
distance: 2
Coverage: all single errors, multiple unidirectional errors
Redundancy: 100%
Example
2-of-4 code (6 codewords)
set of valid words:{1100, 1010, 1001, 0101, 0011, 0110}

## Slide 83
Checksums
dn
dn-1
d1
d0
rn
rn-1
r1
r0
Original data
Received data
Checksum on
Original data
Checksum on
received data
Received version
of checksum
compare
(From Design and Analysis of Fault-tolerant Digital Systems
B. W. Johnson, , Addison-Wesley 1989)
when blocks of data must be transferred (data transfer between mass-storage device)
checksum is added to the block of data to achieve error detection
checksum is basically the sum of the original data
checksum for a block of s words is formed by adding together all of the words in the block modulo-n, where n is arbitrary.

## Slide 84
Disadvantages
- if any word in the block is changed, the checksum must also be modified at the same time
- allow error detection, no error location: the detected fault could be in the block of s words, the stored checksum or the checking circuitry
- single point of failures for the comparison and encoder/detector element
Different methods differ for how summation is executed
single-precision checksum:
n bit data, n bit checksum
sum of the data modulo 2n (overflow 2n ignored)
double-precision checksum:
n bit data, 2n bit checksum
sum of the data modulo 22n (overflow 22n ignored)
....
Checksums

## Slide 85
- Cyclic codes
any shift around of a codeword will produce another codeword
(burst erroros)
- Arithmetic codes
invariants for a set of arithmetic operations
( A(b*c) = A(b) * A(c) )
- Hamming-error-correction codes
based on overlapping parity
- ...........
Other codes

## Slide 86
Self checking logic (I)
Necessity of reliance on the correct operation of comparators and code checkers
 Design of comparators and code checkers capable of detecting their own faults (checking the checker)
Self-checking circuit: a circuit that has the ability to automatically detect the existence of the fault and the detection occurs during the normal course of its operations
Typically obtained using coding techniques: circuit inputs and outputs are encoded (also different codes can be used)
Basic idea:
Fault free + input codeword  output codeword
Fault  invalid output (output that is not a codeword) (the fault can be detected)
Self-testing circuit: a circuit such that each single fault is detectable
Exists one input codeword such that when a single fault is present, an invalid output is produced

## Slide 87
TIME REDUNDANCY

## Slide 88
Time redundancy techniques
Computation
Computation
Encode
Data
Decode
result
Store
result
Compare
results
Store
result
time t0
time t0+d
Data
Data
error
attempt to reduce the amount of extra hw at the expense of using additional time
Repetition of computations
- execute computations and compare the results to detect faults
- re-execute computations (disagreement disappears or remains)
 good for transient faults no protection against permanent fault problem of guaranteeing the same data when a computation is executed (after a transient fault system data can be completely corrupted)
- encode data before executing the second computation use a minimum of extra hw to detect also permanent faults

## Slide 89
Time redundancy techniques
Example
- errors in data transmitted over a parallel bus
- stuck at 1 or 0 of a line of the bus
t0: transmit original data
t0+d : transmit complement data
When the fault occurs:
received data not complements of each other
t0 1 0 1 1 -> 1 0 0 1
t0+d 0 1 0 0 -> 0 1 0 0
stack at 0
Alternating logic: transmission error free, each bit line should alternate between a logic 1 and a logic 0

## Slide 90
SOFTWARE REDUNDANCY

## Slide 91
management of faults originating from the design and implementation of software components
Due to the large cost of developing software, most of the software dependability effort has focused on fault-avoidance techniques
Software redundancy may occur in many forms:
- add extra lines of code to check the magnitude of a signal, or a routine to test a memory by writing and reading locations
- replicate the complete program
Software redundancy techniques

## Slide 92
Consistency checks
- uses a priori knowledge about the characteristics of information to verify its correctness
Examples:
-range of a signal
-address generated by the computer in the address range of the available memory
-detection of invalid instruction codes (n bit to represent 2k legal instruction codes: 2n -2k are illegal)

## Slide 93
Capability checks
- to verify that a system possess the capability expected
Examples:
-is the ALU working well? execute specific instructions on specific data and compare the result with the expected one (written in a ROM memory)
-in a multiprocessor, are processes working properly? Are they capable of communicating?
-memory test: write and read some locations

## Slide 94
Software diversity
  replicate the complete program
  a simple duplication and comparison procedure will not detect software faults if the duplicated software modules are identical
VERSIONS: Independent generation of N >= 2 functionally equivalent programs, called versions, from the same initial specification.
Two-version systems N = 2
Upon disagreement among the versions?
- retry or restart (fault containment)
- trasition to a predefined safe state
- reliance on one of the versions

## Slide 95
N-version programming
Program
Inputs
Program
Inputs
Program
Version 1
Program
Version N
Program
Version 2
Voter
Program
Outputs
.
.
.
.
(From Fault-Tolerant Computer System Design
D. K. Pradhan, Prentice Hall, 1996)
independently developed versions of design and code
Technique: independently design teams utilizing different design methodologies, algorithms, compilers, run-time systems and hardware components
vote on the N results produced
Related faults may result from dependencies in the separate designs and implementations

## Slide 96
Disadvantages:
-cost of resources
-cost of concurrent executions
-potential source of correlated errors, such as the original specification. Specification mistakes are not tolerated (fault avoidance)
Practical problem in implementing the software Voter for comparing the results generated by the concurrent copies because of the differences in compilers, numerical techniques and format conversions.

## Slide 97
N-self-checking programming
- based on acceptance tests rather than comparison with equivalent versions
- N versions of the program are written
- each version is running simultaneously and includes its acceptance tests
- the selection logic chooses the results from one of the programs that passes the acceptance tests
- tolerates N-1 faults (independent faults)
Program
Version 1
Program
Version N
Acceptance
tests
Accepptance
tests
Selection
Logic
.
.
Program
Inputs
Program
Outputs
Program
Inputs
(From Fault-Tolerant Computer System Design
D. K. Pradhan, Prentice Hall, 1996)

## Slide 98
Cannot adopt the hardware analogy and assume versions fail independently
Empirical evidence that there will be common faults
There is evidence that diversity delivers some improvement over single versions
Design diversity

## Slide 99
From: A. Avizienis, J.C. Laprie, B. Randell, C.E. Landwehr. Basic Concepts and Taxonomy of Dependable and Secure Computing.IEEE Trans. Dependable Sec. Comput. 1(1): 11-33 (2004)

## Slide 100
Compensation can be applied either on demand or systematically, at predetermined times or events, independently of the presence or absence of errors
Strategy: FAULT MASKING
loss of protective redundancy -> FAULT MASKING AND RECOVERY
Rollback/Rollforward error recovery are invoked on demand, after error detection has taken place
Error handling

## Slide 101
Error handling
Rollforward - Forward recovery transform the erroneous state in a new state from which the system can operate correctly
Rollback - Backward recovery bring the system back to a state prior to the error occurrence - Checkpointing
- Recovery block
Backward and forward recovery are not exclusive they can be combined if the error persists

## Slide 102
Forward error recovery
Requires to assess the damage caused by the detected error or by errors propagated before detection
Example of application:
real-time control systems, an occasional missed response to a sensor input is tolerable
The system can recover by skipping its response to the missed sensor input.

## Slide 103
some subset of the system state is saved at specific points during program execution (that is necessary to the continued successful execution)
Backward error recovery Checkpointing
x
1
2
3
a
b
4
5
c
6
d
Process A
Process B
Process C
e
Checkpoint
x
Error
Message passed
Cooperating checkpointing processes
Rollback: resetting the system and process state to the state stored at the latest checkpoint.

## Slide 104
Loss: computation time between the checkpointing and the rollback; data received during that interval
overhead of saving system state/computation time for rollback
Basic issues:
- selecting checkpoints to minimize the amount of state information that must be saved
- deciding which information must be backed up
restraining multiple rollbacks that arise when multiple concurrent processes communicate with each other (domino effect)
Checkpointing

## Slide 105
Backward error recovery Recovery block
Basic structure: ensure T by P
else by Q
else error
Each recovery block contains variables global to the block that will be automatically checkpointed if they are altered within the block.
Upon entry to a recovery block, the primary alternate is executed and subjected to an acceptance test (T) to detect any error in the result. If the test is passed, the block is exited. If the test is failed or the alternative fails to execute, the content of the recovery cache pertinent to the block is reinstated, and the second alternate is executed. This cycle is executed until either an alternative is successful or no more alternatives exist. In this case an error is reported.
Only one single implementation of the program is run at a time
Accettability of the result is decided by an acceptance test T
checkpoint
Acceptance
test

## Slide 106
(From Fault-Tolerant Computer System Design
D. K. Pradhan, Prentice Hall, 1996)
Primary
Version
Secondary
Version N-1
Secondary
Version 1
Program Outputs
.
.
.
.
Program Inputs
N-to-1
Program
Switch
Acceptance
Test
Test Result
A single acceptance test
Combines elements of checkpointing and backup
Minimizes the information to be backed up
Releases the programmer from determining which variables should be checkpointed and when
Backward error recovery: Recovery block

## Slide 107
The classes of faults that can actually been tolerated depends on the fault assumptions that is being considered in the development process and thus relies on independence of redundancies with respect to the process of fault creation and activation
Physical faults: assumption that hardware components fail independently
Development faults:
channels implement the same function via separate design and implementations (DESIGN DIVERSITY)
The measure of effectiveness of any given fault tolerant technique
Fault Tolerance Coverage

## Slide 109
Fault removal

## Slide 110
Fault removal techniques
2. Diagnosis: diagnosing the fault which prevented the
verification conditions from being fulfilled (nature, location)
1. Verification: checking whether the system adheres
to properties (conditions), specific to the considered system
3. Correction: performing the necessary corrections
fault passivation, fault removal, ……………………
1. During system developement: three steps: verification / diagnosis / correction
Check that the fault removal had no undesired consequences (nonregression verification)

## Slide 111
Verification
Static techniques (without excercising the system)
- on the system itself, in the form of static analysis (data flow, complexity, compiler checks, ..) or theorem proving
- on a model of the system behaviour (Petri nets, finite state automata, ...) leading to model checking
Dynamic techniques (exercising the system):
- symbolic execution
- testing

## Slide 112
Testing: The software is exercised by a selected set of inputs (test data) to discover possible malfunctions. Testing exaustively a system with respect to all its inputs is generally impractical
Testing techniques may be grouped by their criteria for data
selection:
Structural (white-box): the choice of test data is driven by our
knowledge of the internal structure of the software, i.e., we try to
exercise (probe) the various parts of the software.
Functional (black-box): the choice of test data is driven by our
knowledge of the requirements.
- Statistical testing: test data are selected according to a
statistical distribution of the input data.

## Slide 113
Symbolic execution:
The input variables are assigned symbolic values (say, x) instead of numeric ones. A symbolic interpreter applies the program statements to the input variables and computes the output values as symbolic (i.e., algebraic or logical) expressions that can be checked for compliancy with the program specification.

## Slide 114
Verification approaches

## Slide 115
Fault injection
testing that necessitates faults or errorrs to be part of the test patterns
design phase simulated fault injection at different levels (the electrical level, the logical level, the functional level)
prototype phase
physical faults injected at hardware level (logic, electrical faults) and at software level (code or data corruption)
real systems
produce information on error latency, error detection, error propagation, error recovery, system reconfiguration but it can study only artificial faults

## Slide 116
Fault removal techniques
2. during the operational phase of the system’s life
1. corrective maintenance: remove faults which have produced one or more errors and have been reported
2. preventive maintenance: removing faults before they produce errors:
- check for physical faults appeared since the last preventive maintenance actions
-check for design faults having led to errors in other similar systems

## Slide 117
Fault forecasting

## Slide 118
Fault forecasting techniques
by performing an evaluation of the system behaviour with respect to fault occurrence and activation
Evaluation
- qualitative: identify, classify the failure modes of the event combination that would lead to system failure e.g. determining the minimal pathset of a fault tree conducting a failure mode. Failure Mode and Effect Analysis (FMEA)
- quantitative or probabilistic: aims to evaluate in terms of probabilities the extent to which some of the attributes of dependabilityare satisfied, measures of dependability e.g. Markov chains, stochastic Petri nets
- modeling - evaluation

## Slide 119
Depends on:
Effectiveness of the fault tolerant mechanisms with respect to fault assumptions (e.g. stack at faults, ...)
Fault assumptions that differ from the faults really occurring in operation lack of fault assumption coverage due to / \
failed components not behaving as assumed common cause failures | conservative fault assumption Byzantine faults
Fault Tolerance Coverage

## Slide 120
Common cause failure

## Slide 121
Distributed controllers communicate each other by hardwired connections or communication networks
Hw/Sw components must be reliable
Communications/networks must be reliable
  tolerant to hw failures and to the effect of communication traffic on the ability of the net to fulfill its functions
  Intrusion tolerant
Digital control systems are distributed control system with hundreds of components: CPUs, memories, PLCs, CPs, BUSes, communication networks, ...
Digital Control systems

## Slide 122
REDUNDANCY
    The digital control system is implemented using several redundant channels
    Redundancy is used within a channel
    Common Cause Failures (CCFs)
Redundancy at the channel level and within each channel usually employs identical components
Digital control systems must be fault tolerant

## Slide 123
Redundant system:
Voter
output
intra-channel redundancy
redundant
channels
  The system can fail if two channels fail concurrently

## Slide 124
Standard IEC 62340, Nuclear power plants. Instrumentation and control systems important to safety. Requirements for coping with common cause failure (CCF). December 2007
.
Common Cause Failure
a failure of two or more structures, systems or components due to a single specific event or cause
Note 1: the coincidental failure of two or more structures, systems or components is caused by any latent defiency from design or manufacturing, from operation or maintenance errors, and which is triggered by any event induced by natural phenomenon, plant process operation or an action caused by man or by any internal event in the I&C system
Note 2: coincidental failure is interpreted in a way which covers also a sequence of system or component failures when the time interval between failures is too short to set up repair measures
CCF definition
-> dependencies

## Slide 125
Dependencies related to communications components of digital systems communicate through buses, hardwired connections, networks
Propagation of failures through communication devices:
- intra-channel failure propagation (transmission of incorrect signals between redundant sub-systems)
- inter-channel failure propagation (redundant channels connected through hardwiring or a communication network)
- inter-system failure propagation (from one system to another)
Dependencies associated with digital systems

## Slide 126
Dependencies related to support systems digital control systems depend on AC or DC power,....
Dependencies related to sharing of HW hw components may be shared by other components - Voters may receive signals from several channels within a system and sensors may send signals to several systems
- same hw may be used to implement systems with different functions

## Slide 127
- the system must have a fault;
- a triggering event must activate the fault;
- channels that are supposed to be independent must be affected concurrently;
- the result must have an affect on safety
Condition for CCF to occur
  U.S.NRC position: for digital protection systems there is still the possibility of a CCF that needs to be evaluated
Note that the relation between the number of faults and
the failure probability depends on the prediction of triggering mechanisms
Multiple systems must share the same fault(s) and be susceptible to the same trigger concurrently

## Slide 128
  REDUNDANCY
  DIVERSITY
  INDEPENDENCE
  different kinds of diversity on the assumption of maximal independence of redundant channels realizing design versions
Digital control systems
defense-in-depth approach

## Slide 129
From “The standard IEC 62340 Nuclear Power Plant – I&C system important to safety – requirements for coping with CCF”, A. Lindner, H-W Bock, NPIC&HMIT 2009, American Nuclear Society.
Scheme of a digital safety I&C system

## Slide 130
Scheme of a fourfold redundant safety I&C system comprising two independent I&C systems A and B
The channels of independent systems and the systems are spatially separated
The systems A and B can be designed by
  different Programmable Logical Controllers
  different set signals
  different I&C functions
Replicas have different starting time to avoid failures triggered by the same runtime

## Slide 131
Basic concepts:
- Prevention of specification errors is only possible by individual specifications of physically different functions
- Existence of diverse measurement signals, actuators and functions in the plant system
Diverse functions: functions that ensure independently that the plant safety targets are met
Diverse functions have to be assigned to independent systems
Functional diversity

## Slide 132
Distinguishing between
  CCF of the Operating System sw - a robust OS platform design with mature operating history ensures that the OS failure probability is minimal - OS fails because of interference from application sw
  - hypothetical failure assumed to cause a catastrophic failure of all of the processing computers
  CCF of the application sw failure that may affect: - sw functions - groups of related sw functions common to redundant computer processors and share algoritms, sensor inputs, and signal trajectories
  OS may limit the propagation and severity of application sw CCF
CCF of software

## Slide 133
  Strictly cyclic operation the system is always active and processing the same amount of data
  -> an actual system demand puts no more stress on the OS than any other cycle
  Static memory allocation and asynchronous operations - avoid interference between OS and application program data due to dynamic memory allocation;
  - avoid faults in releasing system resources and time dependencies due to internal system clock
  Constant loading of communication avoids that special loading taxes the OS capacity (e.g. increased network traffic)
  We obtain - predicatble OS performance
    - OS behaviour that is free from interference from application programs
    - OS failure does not depend on plant conditions

## Slide 134
  • independent communication networks for redundant channels and diverse systems,
  • no uncontrolled external network connections,
  • physical separation and independence of redundant channels and diverse systems,
  • simple OS,
  • separation of OS software and application software,
  • fault-tolerant design of application software (do not propagate missing/erroneous data),
  • fail-safe operation upon software error detection,
  • fiber optics (no propagation of energy-related failure),
  • deterministic program execution,
  • strictly cyclic processing,
  • asynchronous operation,
  • no real-time clock,
  • watchdog monitoring,
  • static memory allocation, (no dynamic memory allocation),
  • constant bus loading (processing and communication buses), and
  • no process-driven interrupts.
Criteria for safety-related digital control design
From: B. Enzinna, L. Shi, S. Yang, Software Common-Cause Failure Probability Assessment, NPIC&HMIT 2009

## Slide 135
• The software development process is robust and of high quality,
• The OS platform and its software development life cycle process are mature,
• Rigorous V&V methodology is used,
• Configuration management after deployment is robust (including control of software versions, setpoint changes, spares),
• Standardized software development tools and function libraries,
• Exclusive use of pre-defined and rigorously qualified function block libraries for application programming,
• Clearly defined rules for use of the software functional blocks (including exception handling),
• Thorough coverage of pre-operational testing,
• Comprehensive exception handling,
• Deterministic program execution,
• Strictly cyclic operation, and
• OS defensive measures
DEFENSE against application sw CCF
From: B. Enzinna, L. Shi, S. Yang, Software Common-Cause Failure Probability Assessment, NPIC&HMIT 2009

## Slide 136
A common definition:
Verification checks an implementation against its specification.
Are we making the product right?
Validation checks a product (final or intermediate) against its
intended requirements.
Are we making the right product?
V&V methodology

## Slide 137
Strategy to cope with CCF
1) Reduce the probability of latent systematic faults incorporated in the redundant channels
2) Reduce the probability that mechanisms exist which could trigger coincidentally latent systematic faults
3) Reduce the probability that a single failure in one channel propagates to other channels (failure propagation)
Quantitative assessment of CCF -> combined probability of the above conditions

## Slide 138
Redundancy, diversity and independence are basic concepts of a defense-in-depth approach for digital control in safety critical systems:
1. redundancy alternative systems and components are included, so that any one can perform the required function if the others fail
2. diversity for a particular function, two or more redundant systems or components with different attributes are included in the design. In practice, it may mean using different components based on different designs and principles, from different vendors
3. independence prevents the propagation of failures and common cause failures due to common internal plant hazards. Independence is achieved by electrical isolation, physical separation and independence of communications between systems
Defense-in-depth approach
more …..

## Slide 139
A. Avizienis, J.C. Laprie, B. Randell, C.E. Landwehr. Basic Concepts and Taxonomy of Dependable and Secure Computing. IEEE Trans. Dependable Sec. Comput. 1(1): 11-33, 2004 D.P. Siewiorek, R.S. Swarz, Reliable Computer Systems.Prentice-Hall International, 1992
B. W. Johnson, Design and Analysis of Fault-tolerant Digital Systems, Addison-Wesley 1989
D. K. Pradhan , Fault-Tolerant Computer System Design, Prentice Hall, 1996
M. Lyu (Ed.): Handbook of Software Reliability Engineering, McGraw Hill, 1996 available on line: http://www.cse.cuhk.edu.hk/~lyu/book/reliability/
L. Strigini and B. Littlewood, Validation of Ultra-High Dependability for Software-based Systems, Communications of the ACM, Vol. 36, No. 11, November 1993.
“The standard IEC 62340 Nuclear Power Plant – I&C system important to safety – requirements for coping with CCF”, A. Lindner, H-W Bock, NPIC&HMIT 2009, American Nuclear Society.
B. Enzinna, L. Shi, S. Yang, Software Common-Cause Failure Probability Assessment, NPIC&HMIT 2009
References