## Slide 2: Outline
Reliability and Availability modelling
Exponential failure law for the hardware
Combinatorial models
  Series/Parallel
  Fault Trees
State based models: Markovian models
  Discrete time Markov chain
  Continuus time Markov chain

## Slide 3: Quantitative evaluation of Dependability
Faults are the cause of errors and failures. Does the arrival time of faults fit a probability distribution? If so, what are the parameters of that distribution?
Consider the time to failure of a system or component. It is not exactly predictable - random variable.
Evaluation of Failure rate, Mean Time To Failure (MTTF), Mean Time To Repair (MTTR), Reliability (R(t)), Availability (A(t)) function
probability theory

## Slide 4: Definition of dependability attributes
Reliability - R(t) conditional probability that the system performs correctly throughout the interval of time [t0, t], given that the system was performing correctly at the instant of time t0
Availability - A(t)
the probability that the system is operating correctly and is available to perform its functions at the instant of time t

## Slide 5: Definitions
f(t) =
dt
dQ(t)
dt
- dR(t)
=
Failure rate function λ(t)
the failure rate λ(t) at time t is defined by the number of failures during Δt in relation to the number of correct components at time t
l(t) =
R(t)
f(t)
=
dt
- dR(t)
R(t)
1
Failure probability density function f(t)
the failure density function f(t) at time t is the number of failures in Dt
Reliability R(t)
Unreliability Q(t)
Q(t) = 1 – R(t)

## Slide 6: Hardware Reliability
l(t)
l
Taken from: [Siewiorek et al.1998]
l(t) constant > 0 in the operational phase
Constant failure rate l
(usually expressed in number of failures for million hours)
= 1/200 one failure every 2000 hours
Early life phase: there is a higher failure rate due to the failures of weaker components (result from defetct or stress introduced in the manufacturing process). Wear-out phase: time and use cause the failure rate to increase.
l(t) is a function of time (bathtub-shaped curve )

## Slide 7: Hardware Reliability
Constant failure rate
l(t) = l
Reliability function
R(t) = e–t
Probability density function
f(t) = e–t
the exponential relation between reliability and time is known as exponential failure law
time
R(t)
l(t) =
R(t)
f(t)
=
dt
- dR(t)
R(t)
1

## Slide 8: Time to failure of a component
Time to failure of a component can be modeled by a random variable X
FX (t) = P[X<=t ] (cumulative distribution function)
FX (t) unreliability of the component at time t
Reliability of the component at time t
R (t) = P[X > t] = 1 – P[X <= t] = 1 – FX (t)
R(t) is the probability of not observing any failure before time t

## Slide 9: Time to failure of a component
l = 1/2000 0.0005 per hour
MTTF = 2000 time to the first failure 2000 hours
Mean time to failure (MTTF)
is the expected time that a system will operate before the
first failure occurs (e.g., 2000 hours)
Failure in time (FIT)
measure of failure rate in 109 device hours
1 FIT means 1 failure in 109 device hours
MTTF =

## Slide 10: Failure Rate
Commercially available databases - Military Handbook MIL-HDBK-217F - Telcordia, - PRISM User’s Manual, - International Eletrotechnical Commission (IEC) Standard 61508
- …
- Handbooks of failure rate data for various components are available from government and commercial sources.
- Reliability Data Sheet of product

## Slide 11: Distribution model for permanent faults
MIL-HBDK-217 (Reliability Prediction of Electronic Equipment -Department of Defence) Statistics on electronic components failures studied since 1965 (periodically updated). Chip failure rates in the range 0.01-1.0 per million hours
l= τLτQ(C1τT τV + C2τE)
τL = learning factor, based on the maturity of the fabrication process
τQ = quality factor, based on incoming screening of components
τT = temperature factor, based on the ambient operating temperature
and the type of semiconductor process
τE = environmental factor, based on the operating environment
τV = voltage stress derating factor for CMOS devices
C1, C2 = complexity factors (based on number of gates, or bits for memories and number of pins)

## Slide 12: Model-based evaluation of dependability
State space representation methodologies: Markov chains, Petri-nets, SANs, …
a model is an abstraction of the system that highlights the important features for the objective of the study
Methodologies that employ combinatorial models: Reliability Block Diagrams, Fault tree, ….

## Slide 13
Combinatorial models

## Slide 14: Combinatorial models
offer simple and intuitive methods of the construction and solutions of models
Assumptions:
independent components
each component is associated a failure rate
model construction is based on the structure of the systems (series/parallel connections of components)
inadequate to deal with systems that exhibits complex dependencies among components and repairable systems

## Slide 15: Combinatorial models

## Slide 16: Combinatorial models
If the system does not contain any redundancy, that is any component must function properly for the system to work, and if component failures are independent, then
the system reliability is the product of the component reliability, and it is exponential
- the failure rate of the system is the sum of the failure rates of the individual components

## Slide 17: Combinatorial models
( ) =
N
i
N!
(N-i)! i!
Binomial coefficient

## Slide 18: Combinatorial models
If the system contain redundancy, that is a subset of components must function properly for the system to work, and if component failures are independent, then
the system reliability is the reliability of a series/parallel combinatorial model

## Slide 19: Combinatorial models
Series/Parallel models
An example:
Multiprocessor with 2 processors and three shared memories

## Slide 20: TMR versus Simplex system
RTMR > Rm if Rm > 0.5
i=0
3
i
(e –lt )3-i (1- e –lt )i
Simplex system
failure rate of module m
Rm = e –lt
Rsimplex = e –lt
TMR system
RV(t) = 1
RTMR = S 1
= (e –lt )3 + 3(e –lt )2 (1- e –lt )
Taken from: [Siewiorek et al.1998]
V
m1
m2
m3
2 of 3
m

## Slide 21: TMR: reliability function and mission time
Taken from: [Siewiorek et al.1998]
Rsimplex = e –lt
MTTFsimplex =
TMR system
RTMR = 3e –2lt -2e –3lt
MTTFTMR =
TMR worse than a simplex system but
TMR has a higher reliability for the first 6.000 hours
TMR operates at or above 0.8 reliability 66 percent longer than the simplex system
S shape curve is typical of redundant systems: above the knee the redundant system has components that tolerate failures; after the knee the system has exhausted redundancy
-
=
<

## Slide 22: Hybrid redundancy with TMR
Symplex system
l failure rate m
Rm = e –lt
Rsys = e –lt
Hybrid system
n=N+S total number of components
S number of spares
Let N = 3 RSDV(t) = 1
failure rate of on line comp
failure rate of spare comp
The first system failure occurs if 1) all the modules fail; 2) all but one modules fail
RHybrid = RSDV(1- QHybrid)
RHybrid = (1 – ( (1-Rm)n + n(Rm)(1-Rm)n-1 ))
RHybrid(n+1) – RHybrid(n) >0
adding modules increases the system reliability under the assumption RSDV independent of n
Taken from: [Siewiorek et al.1998]
SDV
m1
m2
mn
...

## Slide 23: Hybrid redundancy with TMR
Hybrid TMR system reliability RS vs individual module reliability Rm
System with standby failure rate equal to on-line failure rate
TMR with one spare is more reliable than simplex system if Rm>0.23
S is the number of spares
RSDV =1
System with standby failure rate equal to 10% of on line failure rate
TMR with one spare is more reliable than simplex system if Rm>0.17
Taken from: [Siewiorek et al.1998]

## Slide 24: Fault Trees
Consider the combination of events that may lead to an undesirable situation of the system
Describe the scenarios of occurrence of events at abstract level
Hierarchy of levels of events linked by logical operators
The analysis of the fault tree evaluates the probability of occurrence of the root event, in terms of the status of the leaves (faulty/non faulty)
Applicable both at design phase and operational phase

## Slide 25: Fault Trees
Describes the Top Event (status of the system) in terms of the status (faulty/non faulty) of the Basic events (system’s components)
G0
G3
E1
E2
G2
AND
E4
E3
G4
E5
TOP EVENT
GATE SYMBOL
EVENT SYMBOL
OR
OR
OR

## Slide 26: Fault Trees
Components are leaves in the tree
Component faulty corresponds to logical value true, otherwise false
Nodes in the tree are boolen AND, OR and k of N gates
The system fails if the root is true
AND
OR
2 of 3
AND gate
OR gate
K of N gate
True if all the components are true (faulty)
True if at least k of the components are true (two or three components) (faulty)
True if at least one of the components is true (faulty)
C1
C2
C3
C1
C2
C3
C1
C2
C3

## Slide 27: Fault Trees
Top event
OR
AND
AND
M1
M3
M2
P1
P2
Example
Multiprocessor with 2 processors and three shared memories
-> the computer fails if all the memories fail or all the processors fail

## Slide 28: Conditional Fault Trees
Example
Multiprocessor with 2 processors and three memories: M1 private memory of P1, M2 private memory of P2, M3 shared memory.
AND
AND
OR
AND
OR
Top event
system
Assume every process has its own private memory plus a shared memory
Operational condition: at least one processor is active and can access to its private or shared memory
repeat instruction: given a component C whether or not the component is input to more than one gate, the component is unique

## Slide 29: Conditional Fault Trees
If a component C appears multiple times in the FT
Qs(t) = QS|C Fails(t) QC(t) + QS|C not Fails(t) (1-QC(t))
where
S|C Fails is the system given that C fails
and
S|C not Fails is the system given that C has not failed
If the same component appears more than once in a fault tree, the independent failure assumption. We use conditioned fault tree is violated

## Slide 30: Minimal cut sets
TOP
G1
AND
1
2
3
4
5
OR
1. A cut is defined as a set of elementary events that, according to the logic expressed by the FT, leads to the occurrence of the root event.
2. To estimate the probability of the root event, compute the probability of occurrence for each of the cuts and combine these probabilities
Cut Sets
Top = {1}, {2} , {G1} , {5} = {1}, {2} , {3, 4} , {5}
Minimal Cut Sets
Top = {1}, {2} , {3, 4} , {5}

## Slide 31: Minimal cut sets
QSi(t) = probability that all components in the minimal cut set Si are faulty
QSi (t) = q1(t) q2(t) … qni(t) with Si ={1, 2, …, ni }
The numerical solution of the FT is performed by computing the probability of occurrence for each of the cuts, and by combining those probabilities to estimate the probability of the root event
Minimal Cut Sets
Top = {1}, {2} , {3, 4} , {5}
TOP
G1
AND
1
2
3
4
5
OR
Assumption: independent faults of the components

## Slide 32: Minimal cut sets
QTop (t) = QS1 (t) + … + QSn (t)
n number of mininal cut sets
Minimal Cut Sets
Top = {1}, {2} , {3, 4} , {5}
TOP
G1
AND
1
2
3
4
5
OR
S1
= {1}
S2
= {2}
S3
= {3, 4}
S4
= {5}

## Slide 33: Fault Trees
Identification of critical path of the system
  - Definition of the Top event
  - Minimal cut set (minimal set of events that leads to the top event)
Analysis:
- Failure probability of Basic events
- Failure probability of minimal cut sets
- Failure probability of Top event
- Single point of failure of the system: minimal cuts with a single event

## Slide 34
State-based models

## Slide 35: State-based models
Characterize the state of the system at time t:
- identification of system states
- identification of transitions that govern the changes of state within a system
Each state represents a distinct combination of failed and working modules
The system goes from state to state as modules fail and repair
The state transitions are characterized by the probability of failure and the probability of repair

## Slide 36: Markov model
graph where nodes are all the possible states and arcs are the possible transitions between states (labeled with a probability function)
Reliability model
0
1
1-pf
pf
pf
pr
1-pr
Availability model
1-pf
1
1
0

## Slide 37: Markov models
Main points: - systems with arbitrary structures and complex dependencies
- assumption of independent failures no longer necessary
- can be used for both reliability and availability modeling
Markov models (a special type of random process) :
  Basic assumption: the system behavior at any time instant depends only on the current state (independent of past values)

## Slide 38: Markov process
In a general random process {Xt }, the value of the random variable Xt+1 may depend on the values of the previous random variables
Xt0 Xt1 ............Xt
Markov process
the state of a process at time t+1 depends only on the state at time t, and is independent on any state before t
Markov property: “the current state is enough to determine the future state”

## Slide 39: Markov chain
A Markov chain is a Markov process X with discrete state space S
We consider only homogeneous Markov chains
- discrete-time Markov chains (DTMC) / Continuous-time Markov chains (CTMC)
The probability of transition from state i to state j does not depend by the time. This probability is called pij
A Markov chain is homogeneous if it has steady-state transition probabilities

## Slide 40: Transition probability matrix
If a Markov process is finite-state, we can define the transition probability matrix P (nxn)
pij = probability of moving from state i to state j in one step
row i of matrix P: probability of make a transition starting from state i
column j of matrix P: probability of making a transition from any state to state j

## Slide 41: Discrete-time Markov chain (DTMC)
    pi(t) = P{Xt = i}
State occupancy vector at time t p(t) = p(0) Pt
Probability that the Markov process is in state i at time-step t
= (p1 , …, pn )
p(0)
(0)
(0)
State occupancy vector at time t p(t) = [p0(t), p1(t), p2(t) , …]
p(1) = p(0) P
Initial state space distribution
A single step forward
State space distribution
System evolution in a finite number of steps computed starting from the initial state distribution and the transition probability matrix

## Slide 42: Limiting behaviour
A Markov process can be specified in terms of the state occupancy probability vector p and a transition probability matrix P
p(t) = p(0) Pt
The limiting behaviour of a DTMC depends on the characteristics of its states. Sometimes the solution is simple
The limiting behaviour of a DTMC (steady-state behaviour)
lim p(t)
t→∞

## Slide 43: Time-average state space distribution
For periodic Markov chains
doesn’t exist (caused by the probability of the periodic state)
Compute the time-average state space distribution, called
1 2
1 0 1
2 1 0
p(0) = (1,0)
p(1) = p(0) P p(1) = (0,1)
p(2) = p(1) P p(2) = (1,0)
………..
P=
1
2
p(0) =(1,0)
state i is periodic with period d=2
1
1
lim p(t)
t→∞
lim
t→∞
t
p *
=
p *

## Slide 44: Simplex system
0
1
1-pf
pf
State 0 : working
State 1: failed
pf
Failure probability
{Xt } t=0, 1, 2, …. S={0, 1}
all state transitions occur at fixed intervals
probabilities assigned to each transition
The probability of state transition depends only on the current state
1-pf
pf
0
1
P =
current
state
next
state
0
0
1
1
- pij = probability of a transition from state i to state j
- pij >=0
- the sum of each row must be one

## Slide 45: Simplex system with repair
0
1
1-pf
pf
pr
1-pr
State 0 : working
State 1: failed
pf
pr
Repair probability
Failure probability
1-pf
pf
pr
1- pr
P =
current
state
next
state
0
0
1
1

## Slide 46: Simplex system with repair
State j can be made an trapping state with pjj = 1
0.9
0.1
0.5
0.5
[p0(0), p1 (0)] = [ 1, 0]
[ 1, 0]
= [ 0.9, 0.1]
[p0(1), p1(1)] =
initial state: working
0
1
1-pf
pf
pr
1-pr

## Slide 47: Simplex system with repair
probability of being in a state after 1 time-step
1-pf
pf
pr
1- pr
[p0(n), p1(n)] = [p0(n-1), p1(n-1)]
n
1-pf
pf
pr
1- pr
[p0(n), p1(n)] = [p0(0), p1(0)]
probability of being in a state after n time-steps
0
1
1-pf
pf
pr
1-pr

## Slide 48: Continuous-time Markov model
state transitions occur at random intervals
transition rates assigned to each transition
Markov property assumption
the length of time already spent in a state does not influence either the probability distribution of the next state or the probability distribution of remaining time in the same state before the next transition
These assumptions imply that the waiting time spent in any one state is exponentially distributed
Thus the Markov model naturally fits with the standard assumptions that failure rates are constant, leading to exponential distribution of interarrivals of failures

## Slide 49: Simplex system with repair
state 0: working
state 1: failed
l failure rate
m repair rate
Continuous time
Transition matrix P: transition rate
Probability of being in state 0 or 1 at time t+Dt
Taken from: [Siewiorek et al.1998]
:
P =

## Slide 50: Simplex system with repair
Performing multiplication, rearranging and dividing by Dt, taking the limit as Dt approaches to 0:
probability of being in state 0 at time t+Dt
[p0(t+Dt), p1(t+Dt)] = [p0(t), p1(t)]
= -lp0(t) + mp1(t)
= lp0(t) - mp1(t)

## Slide 51: Simplex system with repair
The set of equations can be written by inspection of a transition diagram without self-loops and Dt’s
T matrix
The change in state 0 is minus the flow out of state 0 times the probability of being in state 0 at time t, plus the flow into state 0 from state 1 times the probability of being in state 1.
Continuous time Markov model graph
[]= [p0(t), p1(t)]
Taken from: [Siewiorek et al.1998]

## Slide 52: Simplex system with repair
A(t)
p0(t) probability that the system is in the operational state at time t, availability at time t
The availability consists of a steady-state term and an exponential decaying transient term
Taken from: [Siewiorek et al.1998]

## Slide 53: Availability as a function of time
l = 0.001
m = 0.1
The steady-state value is reached in a very short time
Taken from: [Siewiorek et al.1998]

## Slide 54: Continuous-time Markov models: Reliability
failed state as trapping state
Single system without repair
T =
Continuous time Markov model graph
lDt = state transition probability
l = failure rate
We can prove that:
Reliability
Unreliability
p0(t) = e –t
p1(t) = 1 - e –t

## Slide 55: TMR system with repair
Rates: l and m
Identification of states:
3 processors working, 0 failed
2 processors working, 1 failed
1 processor working, 2 failed
Reliability R(t) = 1- p2(t)
p(0) = [1, 0, 0]
T =

## Slide 56: Comparison with nonredundant system and TMR without repair
Taken from: [Siewiorek et al.1998]

## Slide 57: Dual processor system with repair
A, B processors Rates: l1, l2 and m1, m2
Identification of states:
A, B working
A working, B failed
B working, A failed
A, B failed
Rates: l1= l2 and m1=m2
Availability
A(t) = p0(t) + p1(t) + p2(t)
A(t) = 1- p3(t)
p(0) = [1, 0, 0]
T =
Availability
A(t) = 1- p2(t)
Taken from: [Siewiorek et al.1998]

## Slide 58: Dual processor system with repair
steady-state availability
Steady state value
Taken from: [Siewiorek et al.1998]

## Slide 59: Reliability model
p(0) = [1, 0, 0]
Reliability R(t) = 1- p2(t) R(t)=p0(t) + p1(t)
making state 2 a trapping state
T =
Taken from: [Siewiorek et al.1998]

## Slide 60: TMR system with repair
Rates: l and m
Identification of states:
3 processors working, 0 failed
2 processors working, 1 failed
1 processor working, 2 failed
Reliability R(t) = 1- p2(t)
p(0) = [1, 0, 0]
T =
Taken from: [Siewiorek et al.1998]

## Slide 61: Comparison with nonredundant system and TMR without repair

## Slide 62: Conclusions
Quantitative dependability evaluation
- guiding design decisions
- assessing systems as built - mandatory for safety critical systems
Model construction techniques
- scalability challenge
- decomposition/aggregation approaches
High-level modelling formalisms
  Stochastic petri Nets
  Stochastic Activity networks
Tools: Sharpe, SPNP, Mobius, etc …..
The overall model is decoupled in simpler and more tractable submodels, and the measures obtained from the solution of the sub-models are then aggregated to compute those concerning the overall model