## Slide 1: Modelling & Simulation for Autonomous Systems Workshop 15-16 June 2016 Using AUTOSAR high-Level specifications for the synthesis of security components in automotive systems
Sensing and Computing in Cars
Given an AUTOSAR specification with secured communications, a script, written in Python, has been developed to automatically add security software components (Filters) to the system according to the security properties defined for the communication in the AUTOSAR model. The security requirements are implemented by using the services provided by the Crypto Service Manager (CSM).
The script take as input an AUTOSAR XML (ARXML) file and generates a new one that implements the security requirements specified at the design level.
Example: Vehicle Position communication link between GPS and PathPlanning:
GPSFilter: filter on the sender side
PathPlanningFilter: filter on the receiver side
Both filters use CSM primitives for MAC Generation/Verification (Integrity) and Encryption/Decryption (Confidentiality)
Vulnerability on Autonomous Vehicles
Physical Access
Close-Proximity
Remote-Access
Main security issues:
Data Integrity (assuring the accuracy and consistency of data)
Data Confidentiality (preventing from unauthorized disclosure)
AUTOSAR (AUTomotive Open System ARchitecture)
A standard (www.autosar.org) to create an open and standardised software architecture for automotive systems allowing for the exchange and integration of software components on a standardised platform.
Use case Scenario
Extending AUTOSAR for Security
Automatic Generation of Security Components
Conclusions
This paper advocates the modelling of security issues in the early phases of system design.
Extensions to AUTOSAR for expressing the trust level of components and the security requirement of communications has been introduced.
A tool has been implemented that automatically generates filters that implement the security issue on communications by using the CSM services.
The tool is intended to be used to ease the work of system designers and to avoid oversight caused by the complexity of the AUTOSAR standard.
Autonomous Vehicles
Array of sensors needed to provide the autonomous system with situational awareness about the physical world. Embedded processors use this information to make appropriate decisions about what actions the autonomous system should perform.
Position information from GPS, together with object and road position information coming from sensors are forwarded to Path planning, Lane keeping and Lane Departure warning. These functions, in turn, produce commands for steering, throttle and brakes, for which integrity must be preserved. The low-level control systems for actuators arbitrate among these incoming requests and determine the final actuation commands.
References
Acknowledgment
This work has been developed under the framework of the European project SAFURE (Safety And Security By Design For Interconnected Mixed-Critical Cyber-Physical Systems) under grant agreement No 644080.
A.M. Wyglinski, X. Huang, T. Padir, L. Lai, T. R. Eisenbarth, and K. Venkatasubramanian. Security of autonomous systems employing embedded computing and sensors. Micro, IEEE, 33(1):80–86, 2013.
E. Guizzo. How Google’s self-driving car works. IEEE Spectrum Online, October, 18, 2011.
M. Di Natale and A. Sangiovanni-Vincentelli. Moving from federated to integrated architectures in automotive: The role of standards, methods and tools. 98(4):603–620, April 2010.
Trust specification of functional components
TrustSpecification=< trustSpecID: String,
trustLevel: trustLevelType >
Effort required to create and carry out attacks to the element
Security requirement of communications
SecurityRequirement = < secRqmtID: String,
securityLevel: securityLevelType,
cLevelIndicator: EInt,
iLevelIndicator: Eint> where securityLevelType = { CONF,INTEGR, BOTH, NONE }
cLevelIndicator = { 128, ....}
iLevelIndicator = { 64, .... }
Quantitative indication of Confidentiality and Integrity of communications
Over 80 different embedded processors, interconnected with each other.
Key ECUs (Electronic Control Unit):
Engine Control Modul (ECM)
Electonic Brake Control Module (EBCM)
Transmission Control Module (TCM)
Vehicle Vision System (VVS)
Navigation Control Module (NCM)
…
Cinzia Bernardeschi1, Gabriele Del Vigna1, Marco Di Natale2, Gianluca Dini1, and Dario Varano1
1 Department of Information Engineering, University of Pisa, Largo L. Lazzarino 1, 56122 Pisa, Italy 2 Scuola Superiore Sant’Anna, Piazza Martiri della Libertà 33, 56127 Pisa, Italy